## Slide 1
ADSP Framework
  R-Car Gen3
2018/02/15
Automotive Solution Business Unit
Renesas Electronics Corporation

## Slide 2: INDEX
Current implementation of Linux ALSA & ADSP Framework Page 04 - Overview
Proposal for upgraded ALSA Page 10 - Architecture proposal / Split Cluster/Kernel/User Space - Linux & Android support capability - Target latency of audio subsystem - Timeline - Maintenance - Business model
Further discussion on Renault audio use cases Page 32 - Renault use cases - Renesas' feedback - Discussion

## Slide 3: Mantis Tickets
[1] Mantis #4411
Audio potential use cases overview and open points
[3] Mantis #4313
Capture path not working as stand alone
[4] Mantis #4967
Cannot Create Audio Card with Mix of sample audio Card and simple SCU card
[2] Mantis #4935
Cache latency data with external Memory
P.10, P.32
P.20
Closed
Patch provided

## Slide 4
Overview

## Slide 5: Overview of “ADSP Framework” EXISTING RENESAS’ IMPLEMENTATION
ARM
Application
ADSP
Cadence Partners’ Plugins
ADDA
ARM Core
Audio
HW-IPs
SSIU
(SSI)
ADSP Interface
ADSP Driver
ADSP Framework
ADSP Reference Plugins
  Renderer
  Capture
  Equalizer
Kernel Space
User Space
Renesas is preparing “ADSP Framework” as a package including source code, and consists of Interface, Driver, Framework, and Reference Plugins.
ADSP Framework was made from Cadence’s Framework for the following feature expansion.
- Interface between ARM side and ADSP side. - Interface and combination with Audio HW-IPs.
Reference Plugins are realizing direct Outputting /Inputting PCM data between ADSP and HW-IPs, SSI (Serial Sound Interface) and SCU (Sampling rate Converter Unit).
Renesas is ready to offer ADSP Framework for efficient ADSP software development.
Renesas continues ADSP solution development in collaboration with Audio expert partners.
R-Car Gen3
Audio
DMAC
SCU

## Slide 6: Specifications of audio modules (1)
Module |  | Function
ADSP (Tensilica-DSP) |  | The audio DSP (ADSP) consists of a DSP for audio processing, Xtensa® LX4 processor with HIFI2 Audio Engine from Tensilica®, and its control logics. HIFI2 is the major Audio DSP on PC.
SCU (Sampling rate Converter Unit) | SRC (Sampling Rate Converter) | Includes 10 SRC modules SRC0: 2ch,6ch,8ch/16bit,24bit/192kHz (max) SRC1,3,4: 2ch/16bit,24bit/192kHz (max) 6ch/16bit,24bit/128kHz (max) 8ch/16bit,24bit/96kHz (max) SRC2,9: 2ch/16bit,24bit/192kHz (max) SRC5,6,7,8: 2ch/16bit,24bit/192kHz (max)
 | CTU (Channel Transfer Unit) | Down-mixing and splitter functions
 | MIX (MIXer) | Mixing (adds) 2 to 4 sources into 1 output
 | DVC (Digital Volume Controller) | Volume control function including digital volume, volume ramp, and zero-crossing mute
Partners provide over 125 audio codecs for Tensilica’s ADSP.
Multi-channel and high-resolution audio codecs processing, by offloading ARM CPU load with ADSP
Several SCU modules can be used for multiple playbacks and capture paths
Different sound sources can be handled in case of front seat and rear seat entertainment.

## Slide 7: Specifications of audio modules (2)
module |  | Function
SSI (Serial Sound Interface) |  | Includes 10 SSI modules functioning as interfaces with external devices.
 |  | Supports TDM mode (As for a sampling frequency, 48 kHz is a maximum.)
 |  | Max. 16 independent monaural sound sources in TDM format.
ADMA | Audio Module to Audio Module | The Audio DMAC-Peripheral-Peripheral module controls data transfer between the audio modules connected to the audio local bus.
 | Memory to Audio Module | The Audio DMAC module controls data transfer between External Memory(DDR) and the audio modules connected to the audio local bus.
Several SSI modules for multiple playback and capture path
Audio DMAC (ADMA) loads-off the software load and audio data transfers

## Slide 8: Audio Data Routing Block Diagram
SCU
SCU integrates Sampling Rate Converter, Sound Mixer, and Digital Volume Controller with flexible audio path.
HW-IPs can be flexibly connected on Audio Local Bus dedicated to audio data transfer.
By exclusive audio bus with PP-DMAC or A-DMAC, making secure audio bandwidth and realizing multichannel audio transfer smooth.
Sound Mixer/Digital Volume
I²S
Audio local bus
I²S
I²S
I²S
I²S
I²S
I²S
I²S
I²S
I²S
SRC
SRC
SRC
SRC
SRC
SRC
SRC
SRC
SRC
SRC
MLBIF/
MLM
DTCP
A-DMAC
Audio local bus
ADSP HiFi2@530MHz
System Bus
PP-DMAC
CPU
Video
USB / Ether
DBSC
Sound Mixer/Digital Volume

## Slide 9: ADSP Framework Package
 | Software Product Name | Device | OS | License
[1] | ADSP Interface for Linux | ARM | Linux | Proprietary
[2] | ADSP Driver for Linux | ARM | Linux | GPLv2/MIT Dual
[3] | ADSP Framework | HiFi2 | XTOS | Proprietary
[4] | ADSP Reference Plugin | HiFi2 | XTOS | MIT
< ADSP Framework for Linux >
  [1] ADSP Interface for Linux Providing API for ADSP Framework control working in user space of Linux. Sample( OMX-like I/F Layer with proxy function, and “smoketest”)
  [2] ADSP Driver for Linux The program working in kernel space of Linux. Processing the download of ADSP firmware, Activating, Sending and receiving message. Now, with the today configuration, it consists of Proxy driver and ADSP loader.
  [3] ADSP Framework The control program working on ADSP of HiFi2 built by Xtensa Xplorer. Operating ADSP by controlling Plugins according to the message from upper layer.
  [4] ADSP Reference Plugin There are Capture/Renderer Plugin and Equalizer Plugin made by Renesas.

## Slide 10
Architecture proposal

## Slide 11: Status
[A] Renesas - Today
ALSA control - Non Support
[B] Renesas – Next step
Move ADSP to dynamic driver so that it can present itself as sound card.
[C] RNSL’s expectations
ASoC DPCM driver, as defined by ALSA
Driver created by Fiberdyne also draws data from ALSA Driver.
< ADSP - ALSA >
(1) All ADSP will be controlled by amixer? Amixer will control ADSP with parameters: Volume rate, sample rate converter, equalizer parameters.
Aplay will control ADSP with PCM parameters: PCM width, channel number, frequency, frame size. Because these parameters are related to transferring stream data.
(2) The audio Stream will be send to ADSP by native ALSA API (and not but userspace proxy with ADSP IPC)?
Yes, audio stream will be sent to ADSP from native ALSA API.
ALSA Driver get stream data from user and send to ADSP Driver, then to ADSP.
(3) The ADSP Firmware loading will be loaded by the ALSA driver?
No, ADSP Firmware loading will be loaded by ADSP Driver.
Currently, we implement an ALSA Driver in tentative version but there are 2 separated components: ADSP Driver and ALSA Driver.

## Slide 12: [A] ADSP Driver Block Diagram Today IMPLEMENTATION
Streaming Framework
Applications
PCM data
PCM parameters & extension parameters
Message data & Control
Creation and destruction command
Legend:
Sub-components
ALSA Driver
ALSA User Lib
User side
Kernel side
Hardware side
ALSA middle layer
PCM interface
Control interface
Kernel side
ALSA framework supported by Linux
ADSP Interface for Linux
SCU/
SSI
ADDA
ADSP Framework
ADSP Reference Plugin
ADSP HiFi
ak4613
ADSP Driver for Linux
PCM parameters
Proxy driver
ADSP loader
ADSP and ALSA operate separately. It is necessary to create an application to control via the ADSP I/F. The I/F controls the ADSP HW through the Proxy driver.

## Slide 13: [b] ALSA Block Diagram NEXT STEP IMPLEMENTATION
This figure shows the basic configuration of ADSP driver and the connection with the ALSA framework when performs playback and record to ADSP device.
Proxy driver | Add connect & communicate with ADSP base
ADSP loader | Add Register ALSA card step
ADSP base | New Add
ADSP ALSA driver | New Add
< ADSP Driver difference between [A] and [B] >
PCM data
PCM parameters & extension parameters
Message data & Control
Creation and destruction command
Legend:
Sub-components
Streaming Framework
Applications
ALSA Driver
ALSA User Lib
User side
Kernel side
Hardware side
ALSA middle layer
PCM interface
Control interface
Kernel side
SCU/
SSI
ADDA
ADSP Framework
ADSP Reference Plugin
ADSP HiFi
ak4613
ADSP Driver for Linux
PCM parameters
Proxy driver
ADSP loader
Extension interface
PCM callback
Control callback
ADSP ALSA driver
ADSP base
Reference Plugin component (Renderer/Capture/EQZ)
DDR
Shared memory
Extension parameters (volume, SRC)

## Slide 14: [C] ASoC Base Block Diagram
ASoC Layer
ASoC consists of the following block diagram. Through the ASoC layer, the ALSA driver is connected with three drivers. It consists of three drivers: Codec Driver, Machine Driver and Platform Driver. We think that Codec Driver and Machine Driver can be reused. For the Platform Driver, it is necessary to modify it for each hardware. Therefore, we need to prepare a suitable ADSP Driver for Linux on the Platform Driver.
Streaming Framework
Applications
ALSA Driver
ALSA User Lib
User side
Kernel side
Hardware side
ALSA middle layer
PCM interface
Control interface
Kernel side
SCU/
SSI
ADDA
ADSP Framework
ADSP Reference Plugin
ADSP HiFi
ak4613
PCM parameters
DDR
Shared memory
Extension parameters (volume, SRC)
Machine Driver
Codec Driver
Codec DAI
Platform Driver
CPU DAI
PCM data
PCM parameters & extension parameters
Message data & Control
Creation and destruction command
Legend:
Sub-components
If we do not customize this block, it will not connect to Gen3 ADSP.
ADSP Driver for Linux
Communication

## Slide 15: Comparison of renesas plan vs asoc
Item | [C] ASoC DPCM IMPLEMENTATION | [B] RENESAS NEXT STEP IMPLEMENTATION
Support connecting codec | ADSP driver is integrated into ASoC which supports transferring data to codec automatically. | In Fiberdyne, which is the basis of development, in the CES demonstration, Audio waiting time during direct output from HiFi 2 to codec is kept to a minimum. Renesas & Fiberdyne think that this implementation is fitting the automotive use cases.
Controlled by device tree | The sound card can be loaded automatically when booting board by setting configuring device tree. | Our ADSP ALSA sound card can’t be loaded automatically when booting board; it is loaded by software configuration.
DPCM | ADSP can work as a DPCM driver because in the machine driver simple-scu-audio-card already supports DPCM | Fiberdyne CES demo: ADSP has a DPCM-like solution, where the ALSA sound card exposes multiple playback PCM streams that can be dynamically routed inside the ADSP framework. Next step in RENESAS implementation is to leave this point open, depending on OEM audio implementation (ALSA configuration to be checked vs HW capabilities – or HiFi2 SW audio routing if needed)

## Slide 16
Linux & Android support capability

## Slide 17: RENESAS Audio SUB-SYSTEM (TODAY)
SCU/
SSI
ADDA
adsp-omx-launch (smoketest)
ALSA User Lib
ALSA Driver
ALSA Sink
xa-gst-omx
ADSP Equalizer Interface(OMX)
ADSP Renderer Interface(OMX)
ADSP Capture Interface(OMX)
ADSP Reference
Equalizer Plugin
ADSP Reference
Renderer Plugin
ADSP Reference
Capture Plugin
DDR
TCM
TCM
ADSP Interface for Linux
ADSP Driver for Linux
ADSP Framework
ADSP Reference Plugin
ADSP HiFi
File
ARM Codec
library
ARM Decoder
Streaming Framework(ex. GStreamer)
Sample
Test Program
Application / Media Player
User Application
GStreamer
gst-omx
OMX I/F
System integration part
Renesas
Sample
Customer
Reference
Control line
Audio Data Routing
ADSP
Decoded output example using ARM decoder
Example using ADSP (File->EQZ->Renderer->SSI)
SRC/DVC

## Slide 18: RENESAS Audio SUB-SYSTEM (NEXT STEP)
ALSA Driver
SCU/
SSI
ADDA
ALSA Sink
ADSP Reference
Equalizer Plugin
ADSP Reference
Renderer Plugin
ADSP Reference
Capture Plugin
DDR
TCM
TCM
ADSP Driver for Linux
ADSP Framework
ADSP Reference Plugin
ADSP HiFi
ARM Codec
library
ARM Decoder
Streaming Framework(ex. GStreamer)
Application / Media Player
User Application
GStreamer
gst-omx
OMX I/F
System integration part
Renesas
Sample
Customer
Reference
Control line
Audio Data Routing
ADSP
Decoded output example using ARM decoder
Example using ADSP (ALSA->EQZ->Renderer->SSI)
ALSA User Lib
ALSA->ADSP
Under development
SRC/DVC/CTU/MIX

## Slide 19: RENESAS Audio SUB-SYSTEM (ANDROID)
ALSA Driver
SCU/
SSI
ADDA
ADSP Reference
Equalizer Plugin
ADSP Reference
Renderer Plugin
ADSP Reference
Capture Plugin
DDR
TCM
TCM
ADSP Driver for Android
ADSP Framework
ADSP Reference Plugin
ADSP HiFi
Android Framework
Application / Media Player
User Application
Audio Finger
System integration part
Renesas
Sample
Customer
Reference
Control line
Audio Data Routing
ADSP
Decoded output example using ARM decoder
Example using ADSP (ALSA->EQZ->Renderer->SSI)
Tiny ALSA
SRC/DVC/CTU/MIX
Audio HAL
Android
Basic implementation planned (ADSP-FW control). Demo available (Fiberdyne)

## Slide 20
Target latency of audio subsystem

## Slide 21: Low Latency
ADSP
Audio Data Stream
ADSP
Reference
Plugin
D-TCM
A-DMAC
PP-DMAC
Output
FIFO
D-TCM
Input
FIFO
A-DMAC
PP-DMAC
DDR/
SCU/SSI
SCU/SSI
ADSP supports 2 types of DMAC transfer method, one is Audio-DMAC (A-DMAC) and the other is Audio-DMACpp (PP-DMAC : Peripheral to Peripheral). A-DMAC can transfer between System Bus and Audio Local Bus, so it is used to Data transfer between DDR and Audio HW-IPs. PP-DMAC is for connecting Audio HW-IPs on Audio Local Bus. For supporting multichannel audio processing, Audio routing is designed with low latency and selectable DMAC for efficient system design.
E.g. Renderer Processing
DDR/
SCU/SSI
SCU/SSI

## Slide 22: R-Car Audio IP latency - DDR
Audio data transfer latency for each Audio IPs as follows.
DDR
SRCin
_BUSIF
SRC5
SRCout
_BUSIF
Audio
DMAC
P.P.
SSI
125us * 2
20.8us * 4
8.2ms
Audio
DMAC
20.8us * 1
Audio Play-back
62.5us = 16kHz
125us = 8kHz
20.8us = 48kHz
Num of Buffers: *1 = One time,*2=Two times, *4=Four times
8kHz→48kHz
Stereo Data
DDR
SRCin
_BUSIF
SRC5
SRCout
_BUSIF
Audio
DMAC
P.P.
SSI
20.8us * 2
20.8us * 1
7.38ms
Audio
DMAC
125us * 1
Audio Recording
48kHz→8kHz
Stereo Data

## Slide 23: R-Car Audio IP latency - SRC
SRCin
_BUSIF
SRC5
SRCout
_BUSIF
Audio
DMAC
P.P.
ADSP
22.6us * 2
1.52ms
Audio
DMAC
P.P.
SSI
20.8us * 1
22.6us * 1
0.4us
20.8us * 1
SRCin
_BUSIF
SRC6
SRCout
_BUSIF
Audio
DMAC
P.P.
SSI
20.8us * 2
22.6us * 4
1.9ms
Audio
DMAC
P.P.
22.6us * 1
total = 1.609ms
total = 2.0754ms
(1)
Stereo data
Stereo data
44.1kHz -> 48kHz
48kHzHz -> 44.1kHz
SRCin
_BUSIF
SRC5
SRCout
_BUSIF
Audio
DMAC
P.P.
ADSP
20.8us * 2
1.9ms
Audio
DMAC
P.P.
SSI
22.6us * 1
20.8us * 1
0.4us
22.6us * 1
SRCin
_BUSIF
SRC6
SRCout
_BUSIF
Audio
DMAC
P.P.
SSI
22.6us * 2
20.8us * 4
1.52ms
Audio
DMAC
P.P.
20.8us * 1
total = 1.9854ms
total = 1.6918ms
Stereo data
Stereo data
48kHz -> 44.1kHz
44.1kHzHz -> 48kHz
(2)

## Slide 24: R-Car Audio IP latency - NO SRC
ADSP
Audio
DMAC
P.P.
SSI
22.6us * 1
0.4us
22.6us * 1
Audio
DMAC
P.P.
SSI
22.6us * 4
total = 0.023ms
total = 0.113ms
(3)
Stereo data
Stereo data
44.1kHz
44.1kHz
ADSP
Audio
DMAC
P.P.
SSI
20.8us * 1
0.4us
20.8us * 1
Audio
DMAC
P.P.
SSI
20.8us * 4
total = 0.0212ms
total = 0.104ms
(4)
Stereo data
Stereo data
48kHz
48kHz

## Slide 25
Timeline

## Slide 26: R-Car Gen3 Linux Release plan
Components | Device [Version] | Q1 / 2017 |  |  | Q2 / 2017 |  |  | Q3 / 2017 |  |  | Q4 / 2017 |  |  | Q1 / 2018 |  |  | Q2 / 2018 |  |  | Q3 / 2018 |  |  | Q4 / 2018 |  |  | Q1 / 2019 |  | 
 |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 3
Yocto
Kernel
Tool Chain
Wayland
Gstreamer
R-CAR H3
[Salvator X & XS]
[Starter Kit Premier]
R-CAR H3N
[Salvator XS]
R-CAR M3
[Salvator X & XS]
[Starter Kit Pro]
R-CAR M3N
[Salvator X & XS]
[Starter Kit Premier]
R-CAR E3
[TBC]
R-CAR D3
[Draak]
BSP
MM Package
(OGL3.1, MMP)
System
v2.17.0 (1)
v2.23.0(3)
v3.4.0 (4)
v3.6.0
v3.15.0
v2.23.1
β
F
β3
F
β
F
β3
FRC
F
α
β3
FRC
F
F
α
Yocto 2.1
LTSI 4.9
v2.19.0 (2)
β2
β2
Wayland 1.11.0
GST 1.6.3
Gcc linaro 5.2.1
β4
FRC
β5
v3.13.0 (6)
F-MR
F-MR
β4
F
α2
α
BSP, Gfx, IPL & QoS for reference & demo only
We will develop the new ADSP package
(refer to pages 13 and 18)
corresponding to ALSA for April END.
Target is Yv3.7.0 (May)
We are planning first release of the ADSP Alsa for Linux.
(see p.13 & 18)
Yocto 2.4
LTSI 2018
Followed by Y2.4
Followed by Y2.4
Gcc linaro 6.1 or later
v3.7.0 (5)

## Slide 27: R-Car Gen3 ANDROID Release plan for customers APPROVED BY GOOGLE
Android versions | Device versions | Q3 / 2017 |  | Q2 / 2017 |  |  | Q3 / 2017 |  |  | Q4 / 2017 |  |  | Q1 / 2018 |  |  | Q2 / 2018 |  |  | Q3 / 2018 |  |  | Q4 / 2018 |  |  | Q1 / 2019 |  |  | Q2 / 2019 |  | 
 |  | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 3 | 4 | 5 | 6
Pre-migration
BSP development
◆
Android O
Early Access
Quality test
◆
Android-O
AOSP
Oreo (8.0)
Linux Kernel 4.9
R-CAR H3
[Salv X & XS]
R-Car M3
[Salv X & XS]
R-Car H3
(SK Premium + KF)
R-CAR H3, M3
[Salv-X & XS]
R-Car H3
(SK Premium + KF)
R-Car H3, M3,
[Salvator-X & XS]
R-CarH3N
Salvator XS]
R-Car H3
(SK Premium + KF)
R-Car H3
[SK Premium + KF]
R-Car H3, H3N,M3, M3N
[Salv-XS]
R-Car H3
[SK Premium + KF]
R-Car E3 (TBC)
[Ebisu]
α
All Dates have dependencies, including Google deliverables, and are subject to change without notice.
Early release availability depends on Google authorization
Note: Early release milestone on Android P based on Oreo experience (+8 weeks from Google Drop)
◆
O-MR1 PDK
Early Access
◆
O-MR1
AOSP
α
eSep
α
Advanced
development
Oreo (8.1)
Linux Kernel 4.9
eJan
Android O
Early Access
O-MR1 PDK
Early Access
E
E
O-MR1 full source
Early Access
O-MR1 full source
Early Access
◆
β
eMar
Oreo (8.1)
Kernel update
Linux Kernel 4.14
Reference
Package (8.1)
1
◆
Android-P
Early Access
Pre-migration
BSP development
◆
Android-P
AOSP
eSep
eDec
Final
eJun
β
E
α
P full source
Early Access
P PDK
Early Access
P (9.0)
Linux Kernel 4.14
CTS & VTS Testing
α
α2
Final
CTS
CTS & VTS Testing
α
β
eJul
eFeb
eMay
mApr
CTS
mJun
eMar.
Linux Kernel 4.9
Linux Kernel 4.14
3
2
Linux Kernel 4.14
Under discussion
CTS&VTS Testing
SK & KF BSP released to AOSP site
99% CTS
89% VTS
We are planning first release of the ADSP for Android.
(Preliminary version)

## Slide 28
Business model

## Slide 29: ADSP Framework Package - ALSA
< ADSP Framework for Linux : ALSA >
  [1] ADSP Interface for Linux Since only the ALSA interface is needed, this package is not necessary any more.
  [2] ADSP Driver for Linux Include new submodules: ADSP ALSA driver and ADSP base. (Refer to p.13 & 18)
  [3] ADSP Framework [4] ADSP Reference Plugin Refer to p.9
 | Software Product Name | Device | OS | License
[1] | ADSP Interface for Linux | ARM | Linux | Proprietary
[2] | ADSP Driver for Linux | ARM | Linux | GPLv2/MIT Dual
[3] | ADSP Framework | HiFi2 | XTOS | Proprietary
[4] | ADSP Reference Plugin | HiFi2 | XTOS | MIT
We think that a patch file will be necessary for updating the Linux device tree.
We plan to include it in the ADSP Driver Linux package.

## Slide 30: ADSP Framework Package - Android
< ADSP Framework for Android >
  [1] ADSP Interface for Linux At this stage, there is no plan to provide the I/F sample yet.
  [2] ADSP Driver for Linux Basically the same as Linux ALSA version. (Refer to p.19)
  [3] ADSP Framework [4] ADSP Reference Plugin Refer to p.9
 | Software Product Name | Device | OS | License
[1] | ADSP Interface for Android | ARM | Android | Proprietary
[2] | ADSP Driver for Android | ARM | Android | GPLv2/MIT Dual
[3] | ADSP Framework | HiFi2 | XTOS | Proprietary
[4] | ADSP Reference Plugin | HiFi2 | XTOS | MIT
Android Framework which includes Audio HAL to connect it with ALSA will be provided in Android BSP as per Android milestones plan.

## Slide 31
Renault use cases

## Slide 32: HW MIXING poTENTIAL Use CASEs
SSI
SSI
SSI
MIX
CTU
SRC
SRC
SSI
ADAS
SRC
CTU
SRC
FM
DSP
MEDIA
NAV
CTU
SRC
NORMAL
VOICE
SSI
BT
CTU
SRC
SSI
SSI
DVC
ECHO
SRC
①
②
③
④
①② Can we have DMA configuration to do such path (using several instance)
③ Can ADAS path be safety?
④ Can we get Echo Reference from the output of the HW mixer?
・Currently, ADSP do not support CTU/MIX module.
CTU/MIX is currently being responded.

## Slide 33: sound source
SSI
SSI
SSI
MIX
CTU
SRC
SRC
SSI
ADAS
SRC
CTU
SRC
FM
DSP
MEDIA
NAV
CTU
SRC
NORMAL
VOICE
SSI
BT
CTU
SRC
SSI
SSI
DVC
ECHO
SRC
a
b
c
d
e
f
g
h
i
j
k
l
m
 | I/O | bit | ch | kHz | Data
a | O | 16 | 4 | 8/16/24 | for NR
b | O | 16 | 8 | 44.1 or 48 | for EC
c | I | 16 | 8 | 44.1 or 48 | Audio
d | I | 16 | 2 | 44.1 or 48 | Radio
e | I | 16 | 1 | 24 | Audio guidance
f | O | 16 | 2 | 8/16/24 or 48 | Regular capture
g | I | 16 | 2 | 16/24 | Speech recognition microphone
h | I | 16 | 2 | 16/24 | Speech recognition microphone
i | I | 16 | 1 | 8/16/24/44.1/48 | Optional: Park Assist sound from ADAS
j | O | 16/24 | 8 | 44.1 or 48 | Car speakers
k | I | 16 | 1 | 8/16 | BT IN
l | O | 16 | 1 | 8/16 | BT OUT
m | I | 16 | 2 | 8/16/24/44.1/48 | Additional Mic
What kind of sound source input / output data?
4 channels flow synchronize between the 2 SSI
Possibly Simultaneous.
TDM 2ch*4=8ch

## Slide 34: Rate Conversion
SSI
SSI
SSI
MIX
CTU
SRC
SRC
SSI
ADAS
SRC
CTU
SRC
FM
DSP
MEDIA
NAV
CTU
SRC
NORMAL
VOICE
SSI
BT
CTU
SRC
SSI
SSI
DVC
ECHO
SRC
a
b
c
d
e
f
g
 | input kHz | ch | output kHz | Quality
a | 16/24/48 | 2 | 8/16/24 | Voice =General
b | 16/24/48 | 2 | 8/16/24 | Voice =General
c | 8/16/24/44.1/48 | 1 | 44.1 or 48 | ?
d | 44.1 or 48 | 8 | 44.1 or 48 | Audio =Hight
e | 16/24 | 1 | 44.1 or 48 | ?
f | 8/16 | 1 | 44.1 or 48 | ?
g | 8/16/24/44.1/48 | 1 | 8/16 | ?
I / O frequency
Information on the rate converter was filled with reference to the previous page.

## Slide 35
Renesas' feedback

## Slide 36: ① Voice Path
SSI
SSI
SRC
SRC
DSP
VOICE
SSI
SSI
SRC7
SRC８
DSP
VOICE
SSI
SSI
SRC
SRC
CTU1
MIX
DSP
VOICE
or
x: What does this connection mean?
・Two inputs to ADSP are OK!
・SRC uses SRC7 or SRC8 general sound quality, the reason is for speech recognition.
・In advance, after MIX it is also OK for DVC->DSP
→HW : It makes a possibility that resources may become insufficient when thinking overall.
x
DVC

## Slide 37: ① Voice Path - Data Flow
SRC3
DVC0
SSI0
SCU
Memory
CTU0
DVC1
ADSP
SRC6
SRC4
SRC9
SRC0
SRC1
SRC2
SRC5
SRC7
SRC8
SSI1
SSI2
SSI9
SSI3
SSI4
SSI5
SSI6
SSI7
SSI8
Audio Local Bus / Audio DMA Bus
Audio-DMAC
(32ch)
SRC3/6
SRC4/9
SRC0/1
SRC2/5
0
1
2
3
MIX0
CTU1
MIX1
0
1
2
3
Audio-DMAC-pp
Route path.
SSI7->SRC7->ADSP->Memory SSI8->SRC8->ADSP->Memory

## Slide 38: ② Bluetooth Path
・If exclusive control, “SSI->SRC->SSI->BT” is OK, and “SSI->DVC->NORMAL” has some HW restrictions.(HW restriction : When SSI -> SRC -> CMD -> memory, SRC synchronization mode can not be used, asynchronous mode only)
★It is necessary for the player to implement DVC.
・Or you can set it to cancel by input and output.
However, pay attention to the number of HW resources.
NORMAL
BT
SSI
SSI
DVC
SRC
x
x: Simultaneous transfer is not possible.
NORMAL
BT
SSI
SSI
SRC
What do you mean? “NORMAL”

## Slide 39: ② Bluetooth Path - Data Flow
SRC3
DVC0
SSI0
SCU
Memory
CTU0
DVC1
ADSP
SRC6
SRC4
SRC9
SRC0
SRC1
SRC2
SRC5
SRC7
SRC8
SSI1
SSI2
SSI9
SSI3
SSI4
SSI5
SSI6
SSI7
SSI8
Audio Local Bus / Audio DMA Bus
Audio-DMAC
(32ch)
SRC3/6
SRC4/9
SRC0/1
SRC2/5
0
1
2
3
MIX0
CTU1
MIX1
0
1
2
3
Audio-DMAC-pp
Route path.
SSI6->Memory Memory->SRC5->SSI5

## Slide 40: ③ ADAS Path
・ DVC is not described in the path (P.33)
< Functional safety requirement >
DDR->Audio DMAC->SSI3 → SSI4->Audio DMAC->DDR
The CPU compares the DDRs with each other by SW and confirms the agreement.
★There is SRC/CMD, because data is being processed, direct comparison can not be done.
SSI
MIX
SSI
ADAS
CTU
SRC
DVC

## Slide 41: ③ ADAS Path - Data Flow
SRC3
DVC0
SSI0
SCU
Memory
CTU0
DVC1
ADSP
SRC6
SRC4
SRC9
SRC0
SRC1
SRC2
SRC5
SRC7
SRC8
SSI1
SSI2
SSI9
SSI3
SSI4
SSI5
SSI6
SSI7
SSI8
Audio Local Bus / Audio DMA Bus
Audio-DMAC
(32ch)
SRC3/6
SRC4/9
SRC0/1
SRC2/5
0
1
2
3
MIX0
CTU1
MIX1
0
1
2
3
Audio-DMAC-pp
Route path.
SSI4->SRC3->CTU00->MIX0->DVC0->SSI0

## Slide 42: ④ MIXING
・HW : Can not transfer to SSI and ADSP at the same time.
・It is possible to input 4 data to the CTU and mix it.
However, DVC is required.
SSI
MIX
CTU
SRC
CTU
DSP
CTU
SRC
CTU
ECHO
Audio/Radio
x
y
Guidance
Headset
？
x: Simultaneous transfer is not possible.
y: What does this connection mean?
SSI
MIX
CTU0
SRC
CTU0
DSP
CTU0
SRC
CTU0
ECHO
Audio/Radio
Guidance
？
DVC
SSI

## Slide 43: ④ MIXING - Data Flow
SRC3
DVC0
SSI0
SCU
Memory
CTU0
DVC1
ADSP
SRC6
SRC4
SRC9
SRC0
SRC1
SRC2
SRC5
SRC7
SRC8
SSI1
SSI2
SSI9
SSI3
SSI4
SSI5
SSI6
SSI7
SSI8
Audio Local Bus / Audio DMA Bus
Audio-DMAC
(32ch)
SRC3/6
SRC4/9
SRC0/1
SRC2/5
0
1
2
3
MIX0
CTU1
MIX1
0
1
2
3
Audio-DMAC-pp
Route path.
SSI4->SRC3 ->CTU00->MIX0->DVC0->SSI0
Memory->SRC4 ->CTU01
ADSP->SRC0- >CTU02
SSI3->SRC2 ->CTU03
SSI1->ADSP->Memory

## Slide 44: Implementation prediction case
SSI7
SSI8
SSI0
MIX0
CTU0
SRC0
SRC7
SSI4
ADAS
SRC8
CTU0
SRC3
FM
DSP
MEDIA
NAV
CTU0
SRC4
NORMAL
VOICE
SSI3
BT
CTU0
SRC2
SSI5
SSI6
ECHO
SRC5
SSI1
SSI7->SRC7->ADSP->Memory SSI8->SRC8->ADSP->Memory
SSI6->Memory Memory->SRC5->SSI5
SSI4->SRC3 ->CTU00->MIX0->DVC0->SSI0
Memory->SRC4 ->CTU01
ADSP->SRC0- >CTU02
SSI3->SRC2 ->CTU03
SSI1->ADSP->Memory

## Slide 45: Implementation prediction case - Data Flow
SRC3
DVC0
SSI0
SCU
Memory
CTU0
DVC1
ADSP
SRC6
SRC4
SRC9
SRC0
SRC1
SRC2
SRC5
SRC7
SRC8
SSI1
SSI2
SSI9
SSI3
SSI4
SSI5
SSI6
SSI7
SSI8
Audio Local Bus / Audio DMA Bus
Audio-DMAC
(32ch)
SRC3/6
SRC4/9
SRC0/1
SRC2/5
0
1
2
3
MIX0
CTU1
MIX1
0
1
2
3
Audio-DMAC-pp
Route path.

## Slide 46
Discussion

## Slide 47
Renesas.com