## Slide 1
ADSP ALSA DRIVER DETAIL
NOVEMBER 2017

## Slide 2
REVISION HISTORY
Rev. | Date | Description |  | Approved by | Created by
 |  | Page | Summary |  | 
1.00 | 29/11/2017 | - | First Edition issued. | Nguyen Nguyen | Vu Phan
2.00 | 21/06/2018 | 22 to 58 | Support ASoC | Vu Phan | Nguyen Dang
3.00 | 13/08/2018 | - | Add TDM/CTU/MIX feature | Vu Phan | Nguyen Dang
4.00 | 27/08/2018 | - | Add CTU/MIX feature | Vu Phan | Nguyen Dang

## Slide 3: Agenda
Oveview 3
Terminologies 4
Macros 6
External functions 9
Callbacks 17
Platform Interface 20
Platform Driver 23
Internal functions 27
PCM Interface 58

## Slide 4: Agenda
Control Interface 84
Error code 109

## Slide 5: OVERVIEW
ADSP
ADSP ALSA Driver
Control Callback
Playback/Capture Equalizer
Playback/Capture/TDM Playback/TDM Capture Sample Rate
Playback/Capture/TDM Renderer/TDM Capture Volume
Register/Unregister plugin, set HW parameters in initialization phase
Renderer control
Capture control
Equalizer control
PCM Callback
Renderer plugin
Capture plugin
Equalizer plugin
Set/Get HW parameters for volume, sample rate, equalizer setting/getting
Control plugin: Register/Unregister, send/receive command…
Subtracted object. It contains commands related to setting/getting params, register/unregister plugin
Callbacks are defined for PCM Interface, Control Interface
Renderer/Capture/Equalizer/TDM Renderer/TDM Capture Plugin in ADSP side
TDM Renderer control
TDM Capture control
TDM Renderer plugin
TDM Capture plugin
Renderer control
Renderer control
Renderer control
Capture control
Capture control
Capture control
Equalizer control
Equalizer control
Equalizer control
Renderer plugin
Renderer plugin
Renderer plugin
Capture plugin
Capture plugin
Capture plugin
Equalizer plugin
Equalizer plugin
Equalizer plugin

## Slide 6: TERMINOLOGY
Terms | Explanation
ALSA | Advanced Linux Sound Architecture (ALSA) is a software framework and part of the Linux kernel that provides an application programming interface (API) for sound card device drivers.
Stream | A PCM interface consists of PCM playback, capture, TDM playback and TDM capture streams and each PCM stream consists of one or more PCM substreams.
Substream | A substream correspond to a PCM file opened or recorded.
Internal functions | Functions are defined in target document
External functions | Functions are called in target document but defined in another location
PCM Interface | Control PCM operation
Control Interface | Control Parameter setting
Renderer | A plugin of ADSP is used to playback data
Capture | A plugin of ADSP is used to record data
Equalizer | A plugin of ADSP is used to process sound
TDM Renderer | A plugin of ADSP is used to playback and merge data
TDM Capture | A plugin of ADSP is used to record and split data
Period | A term that corresponds to a fragment in the ALSA
Period size | The size at which a PCM interrupt is generated

## Slide 7: Macros
Below are macros defined for ADSP ALSA Driver
Macros | Values | Description
RDR_DAI_IDX0 | 0 | DAI index 0 for playback/record functions of mono/stereo format
RDR_DAI_IDX1 | 1 | DAI index 1 for playback/record functions of mono/stereo format
RDR_DAI_IDX2 | 2 | DAI index 2 for playback/record functions of mono/stereo format
RDR_DAI_IDX3 | 3 | DAI index 3 for playback/record functions of mono/stereo format
TDM_DAI_IDX | 4 | DAI index for playback/record functions of TDM format
MAX_DAI_IDX | 5 | Maximum number of DAI supported
RDR_CONTROL_NUM | 9 | Total number of control interfaces for record and playback. For further information of the control interfaces, refer to the snd_adsp_pcm_new’s slide
TDM_CONTROL_NUM | 4 | Total number of control interfaces for TDM record and TDM playback. For further information of the control interfaces, refer to the snd_adsp_pcm_new’s slide

## Slide 8: Macros
Below are macros defined for ADSP ALSA Driver
Macros | Values | Description
FRAME_SIZE | 1024 | Supported frame-size
MIN_CHANNEL | 1 | Minimum number of channels supported in Renderer/Capture case
MAX_CHANNEL | 2 | Maximum number of channels supported in Renderer/Capture case
MIN_BUF_SIZE | FRAME_SIZE x MIN_CHANNEL x 2 | Minimum buffer size in byte unit in Renderer/Capture case. ‘2’ is the size of 16-bit stream in byte unit.
MAX_BUF_SIZE | FRAME_SIZE x MAX_CHNNEL x 4 | Maximum buffer size in byte unit in Renderer/Capture case. ‘4’ is the size in byte unit to store 24-bit stream.
MIN_PERIOD | 1 | Minimum number of periods in a buffer in Renderer/Capture case
MAX_PERIOD | 4 | Maximum number of periods in a buffer in Renderer/Capture case

## Slide 9: Macros
Below are macros defined for ADSP ALSA Driver
Macros | Values | Description
TDM_MIN_CHANNEL | 6 | Minimum number of channels supported in TDMRenderer/TDM Capture case
TDM_MAX_CHANNEL | 8 | Maximum number of channels supported in TDMRenderer/TDM Capture case
TDM_MIN_BUF_SIZE | FRAME_SIZE x TDM_MIN_CHANNEL x 2 | Minimum buffer size in byte unit in TDM Renderer/TDM Capture case. ‘2’ is the size of 16-bit stream in byte unit.
TDM_MAX_BUF_SIZE | FRAME_SIZE x TDM_MAX_CHANNEL x 4 | Maximum buffer size in byte unit in TDM Renderer/TDM Capture case. ‘4’ is the size in byte unit to store 24-bit stream.
TDM_MIN_PERIOD | 1 | Minimum number of periods in a buffer in TDM Renderer/TDM Capture case
TDM_MAX_PERIOD | 4 | Maximum number of periods in a buffer in TDM Renderer/TDM Capture case

## Slide 10: Macros
Below are macros defined for ADSP ALSA Driver
Macros | Values | Description
DIRECT_PLAYBACK | 0 | This macro indicates that playback stream is used
DIRECT_RECORD | 1 | This macro indicates that capture stream is used
DIRECT_NUM | 2 | Total number of stream direction

## Slide 11: EXTERNAL FUNCTIONS
    xf_adsp_renderer_create
    xf_adsp_renderer_set_params
    xf_adsp_renderer_get_params
    xf_adsp_renderer_destroy
    xf_adsp_capture_create
    xf_adsp_capture_set_params
    xf_adsp_capture_get_params
    xf_adsp_capture_destroy
External functions: below functions are used in PCM/Control interface which are defined in xf-adsp-base.c.
    xf_adsp_equalizer_create
    xf_adsp_equalizer_set_params
    xf_adsp_equalizer_get_params
    xf_adsp_equalizer_destroy
    xf_adsp_tdm_capture_create
    xf_adsp_tdm_capture_set_params
    xf_adsp_tdm_capture_get_params
    xf_adsp_tdm_capture_destroy

## Slide 12: EXTERNAL FUNCTIONS
    xf_adsp_tdm_renderer_create
    xf_adsp_tdm_renderer_set_params
    xf_adsp_tdm_renderer_get_params
    xf_adsp_tdm_renderer_destroy
    xf_adsp_allocate_mem_pool
    xf_adsp_get_data_from_pool
    xf_adsp_free_mem_pool
    xf_adsp_fill_this_buffer
    xf_adsp_empty_this_buffer
    xf_adsp_get_param
    xf_adsp_set_param
External functions: below functions are used in PCM/Control interface which are defined in xf-adsp-base.c.

## Slide 13: EXTERNAL FUNCTIONS
External functions: Below functions are defined in xf-adsp-base.c.
Please refer ADSP_Driver_Extension material to get detail information.
Function name | Description
xf_adsp_renderer_create | Initializes a Renderer instance, registers ADSP Renderer plugin and initializes parameters with default values of ADSP Renderer plugin.
xf_adsp_renderer_destroy | Unregisters ADSP Renderer plugin, frees registered handler and instance.
xf_adsp_renderer_set_params | Set all parameters for ADSP Renderer plugin based on the values in params structure of Renderer instance.
xf_adsp_renderer_get_params | Get ADSP Renderer parameters and stores the returned values in params structure of Renderer instance.

## Slide 14: EXTERNAL FUNCTIONS
External functions: Below functions are defined in xf-adsp-base.c.
Please refer ADSP_Driver_Extension material to get detail information.
Function name | Description
xf_adsp_capture_create | Initializes a Capture instance, registers ADSP Capture plugin and initializes parameters with default values of ADSP Capture plugin.
xf_adsp_capture_destroy | Unregisters ADSP Capture plugin, frees registered handler and instance.
xf_adsp_capture_set_params | Set all parameters for ADSP Capture plugin based on the values in params structure of Capture instance.
xf_adsp_capture_get_params | Get ADSP Capture parameters and stores the returned values in params structure of Capture instance.

## Slide 15: EXTERNAL FUNCTIONS
External functions: Below functions are defined in xf-adsp-base.c.
Please refer ADSP_Driver_Extension material to get detail information.
Function name | Description
xf_adsp_equalizer_create | Initializes a Equalizer instance, registers ADSP Equalizer plugin and initializes parameters with default values of ADSP Equalizer plugin.
xf_adsp_equalizer_destroy | Unregisters ADSP Equalizer plugin, frees registered handler and instance.
xf_adsp_equalizer_set_params | Set all parameters for ADSP Equalizer plugin based on the values in params structure of Equalizer instance.
xf_adsp_equalizer_get_params | Get ADSP Equalizer parameters and stores the returned values in params structure of Equalizer instance.

## Slide 16: EXTERNAL FUNCTIONS
External functions: Below functions are defined in xf-adsp-base.c.
Please refer ADSP_Driver_Extension material to get detail information.
Function name | Description
xf_adsp_tdm_renderer_create | Initializes a TDM Renderer instance, registers ADSP TDM Renderer plugin and initializes parameters with default values of ADSP TDM Renderer plugin.
xf_adsp_tdm_renderer_destroy | Unregisters ADSP TDM Renderer plugin, frees registered handler and instance.
xf_adsp_tdm_renderer_set_params | Set all parameters for ADSP TDM Renderer plugin based on the values in params structure of TDM Renderer instance.
xf_adsp_tdm_renderer_get_params | Get ADSP TDM Renderer parameters and stores the returned values in params structure of TDM Renderer instance.

## Slide 17: EXTERNAL FUNCTIONS
External functions: Below functions are defined in xf-adsp-base.c.
Please refer ADSP_Driver_Extension material to get detail information.
Function name | Description
xf_adsp_tdm_capture_create | Initializes a TDM Capture instance, registers ADSP TDM Capture plugin and initializes parameters with default values of ADSP TDM Capture plugin.
xf_adsp_tdm_capture_destroy | Unregisters ADSP TDM Capture plugin, frees registered handler and instance.
xf_adsp_tdm_capture_set_params | Set all parameters for ADSP TDM Capture plugin based on the values in params structure of TDM Capture instance.
xf_adsp_tdm_capture_get_params | Get ADSP TDM Capture parameters and stores the returned values in params structure of TDM Capture instance.

## Slide 18: EXTERNAL FUNCTIONS
External functions: Below functions are defined in xf-adsp-base.c.
Please refer ADSP_Driver_Extension material to get detail information.
Function name | Description
xf_adsp_allocate_mem_pool | Send a XF_ALLOC to ADSP to request a memory pool with desired pool size and buffer length.
xf_adsp_get_data_from_pool | Get a data buffer from pool, which registered before.
xf_adsp_fill_this_buffer | Send a XF_FILL_THIS_BUFFER command to ADSP framework.
xf_adsp_empty_this_buffer | Send a XF_EMPTY_THIS_BUFFER command to ADSP framework.
xf_adsp_set_param | Set a single parameter to a registered plugin.
xf_adsp_get_param | Get a data buffer from pool, which registered before.

## Slide 19: CALLBACKs
    snd_adsp_rdr_empty_buf_done
    snd_adsp_rdr_fill_buf_done
    snd_adsp_cap_empty_buf_done
    snd_adsp_cap_fill_buf_done
Callbacks: below callback are defined in ADSP ALSA Driver

## Slide 20: CALLBACKs
Callbacks:
    snd_adsp_rdr_empty_buf_done
snd_adsp_rdr_empty_buf_done |  | 
Synopsis | In playback/TDM playback case, update hardware position. The callback is called when ADSP ALSA driver get response message from ADSP. | 
Syntax | static int snd_adsp_rdr_empty_buf_done(void *data, int opcode, int length, char *buffer) | 
Parameter | void *data | Pointer to base data
 | int opcode | Command code
 | int length | Length of buffer
 | char *buffer | Pointer to data buffer
Return value | 0 | Always returns 0
    snd_adsp_rdr_fill_buf_done
snd_adsp_rdr_fill_buf_done |  | 
Synopsis | In playback/TDM playback case, it is dummy function. | 
Syntax | static int snd_adsp_rdr_fill_buf_done(void *data, int opcode, int length, char *buffer) | 
Parameter | void *data | Pointer to base data
 | int opcode | Command code
 | int length | Length of buffer
 | char *buffer | Pointer to data buffer
Return value | 0 | Always returns 0

## Slide 21: CALLBACKs
Callbacks:
    snd_adsp_cap_empty_buf_done
snd_adsp_cap_empty_buf_done |  | 
Synopsis | In capture/TDM capture, it is dummy function. | 
Syntax | static int snd_adsp_cap_empty_buf_done(void *data, int opcode, int length, char *buffer) | 
Parameter | void *data | Pointer to base data
 | int opcode | Command code
 | int length | Length of buffer
 | char *buffer | Pointer to data buffer
Return value | 0 | Always returns 0
    snd_adsp_cap_fill_buf_done
snd_adsp_cap_fill_buf_done |  | 
Synopsis | In capture/TDM capture, update hardware position. The callback is called when ADSP ALSA driver get response message from ADSP. | 
Syntax | static int snd_adsp_cap_fill_buf_done(void *data, int opcode, int length, char *buffer) | 
Parameter | void *data | Pointer to base data
 | int opcode | Command code
 | int length | Length of buffer
 | char *buffer | Pointer to data buffer
Return value | 0 | Always returns 0

## Slide 22: CALLBACKs
Callbacks:
    snd_adsp_event_handler
snd_adsp_event_handler |  | 
Synopsis | Event handler callback to notify error from ADSP | 
Syntax | static int snd_adsp_event_handler(void *data) | 
Parameter | void *data | Pointer to base data
Return value | 0 | Always returns 0

## Slide 23: platform interface
Create new PCM: snd_adsp_pcm_new

## Slide 24: platform interface
snd_adsp_pcm_new()
snd_adsp_pcm_new |  | 
Synopsis | This API registers necessary control interfaces for ADSP soundcard based on CPU DAI type (playback/capture type or TDM playback/TDM capture type). In playback/capture case, when registering control interfaces for the second/third/fourth playback/capture, MIX usage flag is raised to 1 for that stream to be played mixed with the first one. It also pre-allocates a memory region for ALSA buffer for transferring data. | 
Syntax | static int snd_adsp_pcm_new(struct snd_pcm_runtime *runtime) | 
Parameter | struct snd_pcm_runtime *runtime | Pointer to runtime data
Return value | 0 | Success
 | -EINVAL | Cannot register a control into ALSA framework
Begin job
runtime->cpu_dai->id == RDR_DAI_IDX 0 or 1 or 2 or 3
Get sound card data:
card = runtime->card->snd_card
Get driver data of ADSP sound card:
adsp_card = snd_soc_dai_get_drvdata(runtime->cpu_dai)
T
Preallocate ALSA buffer by calling snd_pcm_lib_preallocate_pages_for_all with alsa_buf_sz size
End job
A
F
B

## Slide 25: platform interface
snd_adsp_pcm_new()
A
index < RDR_CONTROL_NUM
Assign control interfaces to rdr_ctr[CONTROL_NUM] for the current capture/playback stream
err < 0
T
F
T
index++ to process adding next control
F
Assign ALSA buffer
alsa_buf_sz = MAX_BUFFER_BYTES
Add card control:
kctl[index] = snd_ctl_new1(rdr_ctr[index], adsp_card)
err = snd_ctl_add(card, kctl[index])
End job
Return -EINVAL
index = 0
Not the 1st capture/playback stream
Raise MIX control
T
F
[NOTE]:
RDR_CONTROL_NUM as we have 9 structures of Control APIs:
snd_adsp_playback_volume_control
snd_adsp_playback_sample_rate_out_control
snd_adsp_playback_out_channel_control
snd_adsp_playback_equalizer_control
snd_adsp_playback_equalizer_switch_control
snd_adsp_capture_volume_control
snd_adsp_capture_sample_rate_in_control
snd_adsp_capture_equalizer_control
snd_adsp_capture_equalizer_switch_control

## Slide 26: platform interface
snd_adsp_pcm_new()
B
index < TDM_CONTROL_NUM
Assign control interfaces to tdm_ctr[TDM_CONTROL_NUM]
err < 0
T
F
T
index++ to process adding next control
F
Assign ALSA buffer
alsa_buf_sz = TDM_MAX_BUFFER_BYTES
Add card control:
kctl[index] = snd_ctl_new1(tdm_ctr[index], adsp_card)
err = snd_ctl_add(card, kctl[index])
End job
Return -EINVAL
index = 0
[NOTE]:
TDM_CONTROL_NUM as we have 4 structures of Control APIs:
snd_adsp_tdm_playback_volume_control
snd_adsp_tdm_playback_sample_rate_out_control
snd_adsp_tdm_capture_volume_control
snd_adsp_tdm_capture_sample_rate_in_control

## Slide 27: platform driver
Register platform device: snd_adsp_probe

## Slide 28: platform DRIVER
snd_adsp_probe()
snd_adsp_probe |  | 
Synopsis | This callback is called to register platform driver with 5 CPU DAIs (4 DAIs for playback/record and 1 DAI for TDM playback/TDM record) and add ADSP sound card component to ASoC framework. | 
Syntax | static int snd_adsp_probe(struct platform_device *pdev) | 
Parameter | struct platform_device *pdev | Pointer to platform device structure
Return value | 0 | Success
 | -ENOMEM | Cannot allocate ADSP sound card data structure
 | -EINVAL | Cannot to register platform device Cannot add ADSP sound card component to ASoC framework
Begin job
Allocate ADSP sound card data structure in kernel
Init parameters: ADSP sound card data structure with values of 0, struct of control interface with values of -1
error returned?
T
F
F
T
Error returned?
Register platform device by calling snd_soc_register_platform
T
F
Unregister platform device by calling snd_soc_unregister_platform
Save driver data:
dev_set_drvdata(pdev->dev, allocated ADSP sound card)
End job
Return -EINVAL
Mark Equalizer switch = 0 in all records and playbacks
Mark MIX is unused
Fill convention of values for PCM width, min channel, max channel, sampling rate for Renderer, Capture, TDM Renderer, TDM Capture
error returned
Return -ENOMEM
Add ADSP sound card component to ASoC framework by calling snd_soc_register_component

## Slide 29: platform driver
Remove platform device: snd_adsp_remove

## Slide 30: platform DRIVER
snd_adsp_remove()
snd_adsp_remove |  | 
Synopsis | This callback is used to unregister platform driver and remove ADSP sound card component from ASoC framework. | 
Syntax | static int snd_adsp_remove(struct platform_device *pdev) | 
Parameter | struct platform_device *pdev | Pointer to platform device structure
Return value | 0 | Success
 | -ENODEV | ADSP sound card data is invalid
Begin job
Get ADSP sound card data by calling dev_get_drvdata
Free ADSP sound card
F
ADSP sound card data is invalid
T
End job
Return -ENODEV
Unregister platform driver by calling snd_soc_unregister_component and snd_soc_unregister_platform

## Slide 31: INTERNAL FUNCTIONS
    snd_adsp_get_drvdata_from_substream
    snd_adsp_get_base_from_substream
    snd_adsp_get_base_from_hrt
    snd_adsp_get_dai_id_from_substream
    snd_adsp_hrtimer_func
    snd_adsp_playback_init
    snd_adsp_record_init
    snd_adsp_playback_prepare
    snd_adsp_record_prepare
    snd_adsp_tdm_playback_init
    snd_adsp_tdm_record_init
Internal functions: below functions are defined in ADSP ALSA Driver
    snd_adsp_tdm_playback_prepare
    snd_adsp_tdm_record_prepare
    snd_adsp_get_eqz_params_from_control
    snd_adsp_playback_deinit
    snd_adsp_record_deinit
    snd_adsp_tdm_playback_deinit
    snd_adsp_tdm_record_deinit
    snd_adsp_copy_data
    snd_adsp_pcm_transfer

## Slide 32: INTERNAL FUNCTIONS
snd_adsp_get_drvdata_from_substream()
Begin job
Return
pointer to driver data
Get the ADSP sound card’s data by calling snd_soc_dai_get_drvdata(substream->private_data->cpu_dai)
snd_adsp_get_drvdata_from_substream |  | 
Synopsis | This functions is used to get the ADSP sound card’s data | 
Syntax | static void *snd_adsp_get_drvdata_from_substream(struct snd_pcm_substream *substream) | 
Parameter | struct snd_pcm_substream *substream | Pointer to PCM substream
Return value | Pointer | Pointer to driver data of the substream
[Note] For further information about snd_soc_soc_dai_get_drvdata, refer to https://elixir.bootlin.com/linux/latest/source/include/sound/soc-dai.h#L356

## Slide 33: INTERNAL FUNCTIONS
snd_adsp_get_base_from_hrt()
snd_adsp_get_base_from_hrt |  | 
Synopsis | This function is used to get base data of high-resolution timer | 
Syntax | static struct snd_adsp_base_info *snd_adsp_get_base_from_hrt(struct hrtimer *hrt) | 
Parameter | struct hrtimer *hrt | Pointer to base data of high-resolution timer
Return value | hrt | Pointer to base data of high-resolution timer
Return hrt
Begin job

## Slide 34: INTERNAL FUNCTIONS
snd_adsp_get_base_from_substream()
snd_adsp_get_base_from_substream |  | 
Synopsis | This function is used to get base data of playback/capture/TDM playback/TDM capture | 
Syntax | static struct snd_adsp_base_info *snd_adsp_get_base_from_substream(struct snd_pcm_substream *substream) | 
Parameter | struct snd_pcm_substream *substream | Pointer to PCM substream
Return value | base | Base data of the playback/capture/TDM playback/TDM capture
 | NULL | Capture/Renderer/TDM Capture/TDM Renderer has not been created
F
Return base
DAI index is RDR_DAI_IDX 0 or 1 or 2 or 3
T
Begin job
Get ADSP sound card data:
adsp_card = snd_adsp_get_drvdata_from_substream
A
B
Get DAI index by snd_adsp_get_dai_id_from_substream

## Slide 35: INTERNAL FUNCTIONS
snd_adsp_get_base_from_substream()
base = adsp_card->playback[DAI index]->base
F
T
F
F
End
Is the substream playback?
T
adsp_card->playback[DAI index] valid?
A
T
adsp_card->record[DAI index] valid?
base = adsp_card->record[DAI index]->base
base = NULL

## Slide 36: INTERNAL FUNCTIONS
snd_adsp_get_base_from_substream()
base = adsp_card->tdm_playback->base
F
T
F
F
End
Is the substream playback?
T
adsp_card->tdm_playback valid?
B
T
adsp_card->tdm_record valid?
base = adsp_card->tdm_record->base
base = NULL

## Slide 37: INTERNAL FUNCTIONS
snd_adsp_get_dai_id_from_substream()
snd_adsp_get_dai_id_from_substream |  | 
Synopsis | This function is used to get CPU DAI index | 
Syntax | static int *snd_adsp_get_dai_id_from_substream(struct snd_pcm_substream *substream) | 
Parameter | struct snd_pcm_substream *substream | Pointer to PCM substream
Return value | CPU DAI index | 
Return rtd->cpu_dai->id
Begin job
rtd = substream->private_data

## Slide 38: INTERNAL FUNCTIONS
snd_adsp_hrtimer_func()
snd_adsp_hrtimer_func |  | 
Synopsis | This callback is called to reset the high-resolution timer after it expires. It also update HW pointer for the next period to transfer. | 
Syntax | static enum hrtimer_restart snd_adsp_hrtimer_func(struct hrtimer *hrt) | 
Parameter | struct hrtimer *hrt | High-resolution timer data
Return value | HRTIMER_RESTART | The timer will start after it expires
Forward hrtimer by calling hrtime_forward_now
F
Return HRTIMER_RESTART
base->hw_idx != 0
T
Begin job
snd_pcm_period_elapsed to update the PCM status for the next period
base = snd_adsp_get_base_from_hrt
[Note] HRTIMER_RESTART is the macro defined in https://elixir.bootlin.com/linux/v4.17.1/source/include/linux/hrtimer.h#L61

## Slide 39: INTERNAL FUNCTIONS
snd_adsp_playback_init()
snd_adsp_playback_init |  | 
Synopsis | This function is used to create and initialize playback. If Equalizer is used, Equalizer will be created. It also initializes high-resolution timer for updating status. | 
Syntax | static int snd_adsp_playback_init(struct snd_adsp_playback **playback_data, int eqz_flag, struct snd_pcm_substream *substream) | 
Parameter | struct snd_adsp_playback **playback_data | Address of pointer to playback data
 | int eqz_flag | Equalizer flag indicating that equalizer is used or not
 | struct snd_pcm_substream *substream | Pointer to PCM substream
Return value | 0 | Success
 | -EINVAL | Cannot allocate memory for playback data Cannot create Renderer/Equalizer component
Begin job
Return
-EINVAL
Allocate memory for playback data in kernel side using kmalloc
Save playback data to adsp_card’s playback
Mark Renderer, Equalizer, playback’s high-resolution timer not created
Create and register Renderer by calling xf_adsp_renderer_create()
No error?
No error?
T
F
T
Init high-resolution timer for updating HW status
Mark playback’s high-resolution timer created
F
Return
-EINVAL
F
Mark that Renderer is created and set target handle ID as Renderer ID
Save substream data for Renderer
Equalizer is used?
T
Create and register Equalizer by calling xf_adsp_equalizer_create()
Mark that Equalizer is created and set target handle ID as Equalizer ID
No error?
T
Return
-EINVAL
F
End job
Init lock by spin_lock_init call

## Slide 40: INTERNAL FUNCTIONS
snd_adsp_record_init()
snd_adsp_record_init |  | 
Synopsis | This function is used to create and initialize capture. If Equalizer is used, Equalizer will be created. It also initializes high-resolution timer for updating status. | 
Syntax | static int snd_adsp_record_init(struct snd_adsp_record **record_data, int eqz_flag, struct snd_pcm_substream *substream) | 
Parameter | struct snd_adsp_record **record_data | Address of pointer to capture data
 | int eqz_flag | Equalizer flag indicating that equalizer is used or not
 | struct snd_pcm_substream *substream | Pointer to PCM substream
Return value | 0 | Success
 | -EINVAL | Cannot allocate memory for capture data Cannot create Capture/Equalizer component
Begin job
Return
-EINVAL
Allocate memory for capture data
Save capture data to adsp_card’s capture
Mark Capture, Equalizer, record’s high resolution timer not created
Create and register Capture by calling xf_adsp_capture_create()
No error?
No error?
T
F
T
Init high-resolution timer for updating HW status
Mark record’s high resolution timer created
F
Return
-EINVAL
F
Mark that Capture is created and set target handle ID as Capture ID
Save substream data for Capture
Equalizer is used?
T
Create and register Equalizer by calling xf_adsp_equalizer_create()
Mark that Equalizer is created and set target handle ID as Equalizer ID
No error?
T
Return
-EINVAL
F
End job
Init lock by spin_lock_init call

## Slide 41: INTERNAL FUNCTIONS
snd_adsp_tdm_playback_init()
snd_adsp_tdm_playback_init |  | 
Synopsis | This function is used to create and initialize TDM playback. It also initializes high-resolution timer for updating status. | 
Syntax | static int snd_adsp_tdm_playback_init(struct snd_adsp_tdm_playback **tdm_playback_data, struct snd_pcm_substream *substream) | 
Parameter | struct snd_adsp_tdm_playback **tdm_playback_data | Address of pointer to TDM playback data
 | struct snd_pcm_substream *substream | Pointer to PCM substream
Return value | 0 | Success
 | -EINVAL | Cannot allocate memory for TDM playback data Cannot create TDM Renderer component
Begin job
Return
-EINVAL
Allocate memory for TDM playback data in kernel side using kmalloc
Save TDM playback data to adsp_card’s TDM playback data
Mark TDM Renderer and its high-resolution timer not created
Create and register TDM Renderer by calling xf_adsp_tdm_renderer_create()
No error?
No error?
F
T
Init high-resolution timer for updating HW status
Mark TDM playback’s high-resolution timer created
Return
-EINVAL
F
Save substream data for TDM Renderer
T
End job
Init lock by spin_lock_init call
Mark TDM Renderer is created

## Slide 42: INTERNAL FUNCTIONS
snd_adsp_tdm_record_init()
snd_adsp_tdm_record_init |  | 
Synopsis | This function is used to create and initialize TDM record. It also initializes high-resolution timer for updating status. | 
Syntax | static int snd_adsp_tdm_record_init(struct snd_adsp_tdm_record **tdm_record_data, struct snd_pcm_substream *substream) | 
Parameter | struct snd_adsp_tdm_record **tdm_record_data | Address of pointer to TDM record data
 | struct snd_pcm_substream *substream | Pointer to PCM substream
Return value | 0 | Success
 | -EINVAL | Cannot allocate memory for TDM record data Cannot create TDM Capture component
Begin job
Return
-EINVAL
Allocate memory for TDM record data in kernel side using kmalloc
Save TDM record data to adsp_card’s TDM record data
Mark TDM Capture and its high-resolution timer not created
Create and register TDM Capture by calling xf_adsp_tdm_capture_create()
No error?
No error?
F
T
Init high-resolution timer for updating HW status
Mark TDM record’s high resolution timer created
Return
-EINVAL
F
Save substream data for TDM Capture
T
End job
Init lock by spin_lock_init call
Mark TDM Capture is created

## Slide 43: INTERNAL FUNCTIONS
snd_adsp_playback_prepare()
Begin job
Return
-EINVAL
Get runtime’s parameters: frequency sampling, channel, PCM width, frame size
Error returned?
T
Get number of bytes in a period:
base->period_bytes = snd_pcm_lib_period_bytes(substream)
Save indirect PCM information: HW buffer size, SW buffer size, HW queue size to base data of substream
Renderer is not ready
Prepare parameters: input frequency sampling, channel, PCM width, frame size, mix control flag
Get volume rate, output sampling rate, output channel from corresponding playback’s control interfaces
Set parameters to Renderer by calling xf_adsp_renderer_set_params()
T
F
F
B
snd_adsp_playback_prepare |  | 
Synopsis | This function is used to set paramters to Renderer component. It is also used to set parameters for Equalizer if Equalizer is used. | 
Syntax | static int snd_adsp_playback_prepare(struct snd_adsp_playback *playback, struct snd_pcm_substream *substream) | 
Parameter | struct snd_adsp_playback *playback | Pointer to playback data
 | struct snd_pcm_substream *substream | Pointer to PCM substream
Return value | 0 | Success
 | -EINVAL | Cannot set parameters to Renderer/Equalizer Cannot allocate ADSP buffer pool Cannot route Equalizer and Renderer. In case of Equalizer used, cannot send message with opcode XF_EMPTY_THIS_BUFFER to Renderer plugin, Cannot kick init-processing for ADSP plugins.
Get base data: base = &playback->base and get DAI index
Calculate data buffer size:
16-bit data: base->buf_bytes = to base->period_bytes
24-bit data (S24_3LE only): base->buf_bytes = (base->period_bytes * 3 (bytes) / 4 (bytes))
[Notes]
XF_BUF_POOL_SIZE is defined in ADSP Driver Extension Detail Design
MIX is enabled?
Change to use DMAC transfer type DMA1 = ADMAC_CH01
T
F
A
These settings make ADSP use SRC and FIFO to transfer data to SSI0
Prepare parameters: device1 = SRC0, device 2 = SSI0, DMA1 = PDMA0, DMA2 = PDMA1

## Slide 44: INTERNAL FUNCTIONS
snd_adsp_playback_prepare()
End job
Return
-EINVAL
Get buffers from playback->renderer->buf_pool: base->buffer[i] = xf_adsp_get_data_from_pool()
Mark Renderer is ready
Error returned?
T
Equalizer is used
Prepare parameters: frequency sampling, channel, PCM width, Equalizer’s characteristics
Set parameters to Equalizer by calling xf_adsp_equalizer_set_params()
Route Equalizer to Renderer by calling xf_adsp_route()
T
F
A
Mark Equalizer is ready
F
B
Return
-EINVAL
Error returned?
T
F
Allocate ADSP buffer pool for execution:
playback->renderer->buf_pool = xf_adsp_allocate_mem_pool(XF_BUF_POOL_SIZE, base->buf_bytes)
Return
-EINVAL
Cannot allocate
T
F
C
Send zero buffer to plugin to kick Renderer init-processing
T
Error returned
F
Return
-EINVAL

## Slide 45: INTERNAL FUNCTIONS
snd_adsp_playback_prepare()
End job
Send 4 buffers with data = 0 by calling xf_adsp_empty_this_buffer()
T
Wait until all buffers are returned, or
runtime_err flag is enabled
Error returned
Decrease number buffer in the queue
i = i + 1
C
F
Return
-EINVAL
Reset HW data position:
base->hw_idx = 0
i = 0
i < XF_BUF_POOL_SIZE
T
F
T
Error returned
F
Return
-EINVAL

## Slide 46: INTERNAL FUNCTIONS
snd_adsp_record_prepare()
Begin job
Return
-EINVAL
Get base data: base = &record->base and get DAI index
Get runtime’s parameters: frequency sampling, channel, PCM width, frame size
Error returned?
T
Get number of bytes in a period:
base->period_bytes = snd_pcm_lib_period_bytes(substream)
Save indirect PCM information: HW buffer size, SW buffer size, HW queue size to base data of substream
Capture is not ready
Prepare parameters: channel, PCM width, frame size, output sampling rate
Get input frequency sampling, volume rate from corresponding capture’s control interface,
Use FIFO to transfer data
Set parameters to Capture by calling xf_adsp_capture_set_params()
Allocate ADSP buffer pool for execution:
record->capture->buf_pool = xf_adsp_allocate_mem_pool(XF_BUF_POOL_SIZE, base->buf_bytes)
T
F
Return
-EINVAL
Cannot allocate
T
F
A
F
B
snd_adsp_record_prepare |  | 
Synopsis | This function is used to set paramters to Capture component. It is also used to set parameters for Equalizer if Equalizer is used. It also sends a zero-length buffer to kick off init process. Then it sends buffers down to Capture plugin to execute. | 
Syntax | static int snd_adsp_record_prepare(struct snd_adsp_record *record, struct snd_pcm_substream *substream) | 
Parameter | struct snd_adsp_record *record | Pointer to capture data
 | struct snd_pcm_substream *substream | Pointer to PCM substream
Return value | 0 | Success
 | -EINVAL | Cannot set parameters to Capture/Equalizer Cannot allocate ADSP buffer pool Cannot route Equalizer and Capture Cannot send message with opcode XF_FILL_THIS_BUFFER to Capture plugin, Cannot kick init-processing for ADSP plugins.
Calculate data buffer size:
16-bit data: base->buf_bytes = to base->period_bytes
24-bit data (S24_3LE only): base->buf_bytes = (base->period_bytes * 3 (bytes) / 4 (bytes))
[Notes]
XF_BUF_POOL_SIZE is defined in ADSP Driver Extension Detail Design

## Slide 47: INTERNAL FUNCTIONS
snd_adsp_record_prepare()
Return
-EINVAL
Get buffers from record->capture->buf_pool: base->buffer[i] = xf_adsp_get_data_from_pool()
Mark Capture is ready
Error returned?
T
Equalizer is used
Prepare parameters: frequency sampling, channel, PCM width, Equalizer’s characteristics
Set parameters to Equalizer by calling xf_adsp_equalizer_set_params()
Route Equalizer to Capture by calling xf_adsp_route()
T
F
A
Mark Equalizer is ready
F
C
Return
-EINVAL
Error returned?
T
F

## Slide 48: INTERNAL FUNCTIONS
snd_adsp_record_prepare()
End job
Send a buffer with length = 0 to kick init process by calling xf_adsp_fill_this_buffer()
F
Reset HW data position:
base->hw_idx = 0
Equalizer is used
Decrease number buffer in the queue
Wait until initialization is finished
C
T
B
Send 4 buffers down to Capture plugin calling xf_adsp_fill_this_buffer().
Decrease number of buffers in the queue after sending each.
Wait until all buffers are returned, or
runtime_err flag is enabled
Error returned
Return
-EINVAL
T
F

## Slide 49: INTERNAL FUNCTIONS
snd_adsp_tdm_playback_prepare()
Begin job
Return
-EINVAL
Get runtime’s parameters: frequency sampling, channel mode, PCM width, frame size
Error returned?
T
Get number of bytes in a period:
base->period_bytes = snd_pcm_lib_period_bytes(substream)
Save indirect PCM information: HW buffer size, SW buffer size, HW queue size to base data of substream
TDM Renderer is not ready
Prepare parameters: channel mode, input frequency sampling, PCM width, frame size, volume rate, output sampling rate, first device
Use DMAC transfer type to transfer data
Set parameters to TDM Renderer by calling xf_adsp_tdm_renderer_set_params()
T
F
A
F
B
snd_adsp_tdm_playback_prepare |  | 
Synopsis | This function is used to set paramters to TDM Renderer component. | 
Syntax | static int snd_adsp_tdm_playback_prepare(struct snd_adsp_tdm_playback *tdm_playback, struct snd_pcm_substream *substream) | 
Parameter | struct snd_adsp_tdm_playback *tdm_playback | Pointer to TDM playback data
 | struct snd_pcm_substream *substream | Pointer to PCM substream
Return value | 0 | Success
 | -EINVAL | Cannot set parameters to TDM Renderer Cannot allocate ADSP buffer pool, Cannot kick init-processing for ADSP plugins.
Get base data: base = &tdm_playback->base
Calculate data buffer size:
16-bit data: base->buf_bytes = to base->period_bytes
24-bit data (S24_3LE only): base->buf_bytes = (base->period_bytes * 3 (bytes) / 4 (bytes))

## Slide 50: INTERNAL FUNCTIONS
snd_adsp_tdm_playback_prepare()
End job
Get buffers from tdm_playback->tdm_renderer->buf_pool:
base->buffer[i] = xf_adsp_get_data_from_pool()
Mark TDM Renderer is ready
A
B
Allocate ADSP buffer pool for execution:
tdm_playback->tdm_renderer->buf_pool = xf_adsp_allocate_mem_pool(XF_BUF_POOL_SIZE, base->buf_bytes)
Return
-EINVAL
Cannot allocate
T
F
[Notes]
XF_BUF_POOL_SIZE is defined in ADSP Driver Extension Detail Design
T
F
Send zero buffer to plugin to kick Renderer init-processing, and wait for the response successful message or runtime_err flag
Error returned

## Slide 51: INTERNAL FUNCTIONS
snd_adsp_tdm_record_prepare()
Begin job
Return
-EINVAL
Get runtime’s parameters: frequency sampling, channel mode, PCM width, frame size
Error returned?
T
Get number of bytes in a period:
base->period_bytes = snd_pcm_lib_period_bytes(substream)
Save indirect PCM information: HW buffer size, SW buffer size, HW queue size to base data of substream
TDM Capture is not ready
Prepare parameters: channel mode, input frequency sampling, PCM width, frame size, volume rate, output sampling rate, first device
Use FIFO to transfer data
Set parameters to TDM Capture by calling xf_adsp_tdm_capture_set_params()
T
F
A
F
B
snd_adsp_tdm_record_prepare |  | 
Synopsis | This function is used to set paramters to TDM Capture component. . It also sends a zero-length buffer to kick off init process. Then it sends buffers down to TDM Capture plugin to execute. | 
Syntax | static int snd_adsp_tdm_record_prepare(struct snd_adsp_tdm_record *tdm_record, struct snd_pcm_substream *substream) | 
Parameter | struct snd_adsp_tdm_record *tdm_record | Pointer to TDM record data
 | struct snd_pcm_substream *substream | Pointer to PCM substream
Return value | 0 | Success
 | -EINVAL | Cannot set parameters to TDM Capture Cannot allocate ADSP buffer pool Cannot send message with opcode XF_FILL_THIS_BUFFER to TDM Capture plugin, Cannot kick init-processing for ADSP plugins.
Get base data: base = &tdm_record->base
Calculate data buffer size:
16-bit data: base->buf_bytes = to base->period_bytes
24-bit data (S24_3LE only): base->buf_bytes = (base->period_bytes * 3 (bytes) / 4 (bytes))

## Slide 52: INTERNAL FUNCTIONS
snd_adsp_tdm_record_prepare()
Get buffers from tdm_record->tdm_capture->buf_pool:
base->buffer[i] = xf_adsp_get_data_from_pool()
Mark TDM Capture is ready
A
Allocate ADSP buffer pool for execution:
tdm_record->tdm_capture->buf_pool = xf_adsp_allocate_mem_pool(XF_BUF_POOL_SIZE, base->buf_bytes)
Return
-EINVAL
Cannot allocate
T
F
[Notes]
XF_BUF_POOL_SIZE is defined in ADSP Driver Extension Detail Design
Send a buffer with length = 0 to kick init process by calling xf_adsp_fill_this_buffer(),
and wait for the response successful message or runtime_err flag
End job
B
T
F
Error returned

## Slide 53: INTERNAL FUNCTIONS
snd_adsp_playback_deinit()
snd_adsp_playback_deinit |  | 
Synopsis | This function is used to de-initialize Renderer and release its buffer pool. It is also used to de-initialize Equalizer if Equalizer is used. | 
Syntax | static int snd_adsp_playback_deinit(struct snd_adsp_playback *playback) | 
Parameter | struct snd_adsp_playback *playback | Pointer to playback data
Return value | 0 | Success
 | -EINVAL | Cannot de-initialize Renderer/Equalizer
Begin job
Return
-EINVAL
Error returned?
T
Destroy Renderer component
Renderer is created
Send EMPTY_THIS_BUFFER with buffer length = 0 down to Renderer plugin to terminate the process
Release buffer pool by calling xf_adsp_free_mem_pool
T
F
Equalizer is created
T
F
B
F
A
Playback data allocated
T
Return
-EINVAL
Error returned?
Destroy Equalizer component
T
F
F
A
Cancel high-resolution timer interrupt if high-resolution timer has been created and free playback data
B
End job

## Slide 54: INTERNAL FUNCTIONS
snd_adsp_record_deinit()
snd_adsp_record_deinit |  | 
Synopsis | This function is used to de-initialize Capture and release its buffer pool. It is also used to de-initialize Equalizer if Equalizer is used. | 
Syntax | static int snd_adsp_record_deinit(struct snd_adsp_record *record) | 
Parameter | struct snd_adsp_record *record | Pointer to capture data
Return value | 0 | Success
 | -EINVAL | Cannot de-initialize Capture/Equalizer
Begin job
Return
-EINVAL
Error returned?
T
Destroy Capture component
Capture is created
Send EMPTY_THIS_BUFFER with buffer length = 0 down to Capture plugin to terminate the process
Release buffer pool by calling xf_adsp_free_mem_pool
T
F
Equalizer is created
T
F
B
F
A
Capture data allocated
T
Return
-EINVAL
Error returned?
Destroy Equalizer component
T
F
F
A
Cancel high-resolution timer interrupt if high-resolution timer has been created and free capture data
B
End job

## Slide 55: INTERNAL FUNCTIONS
snd_adsp_tdm_playback_deinit()
snd_adsp_tdm_playback_deinit |  | 
Synopsis | This function is used to de-initialize TDM Renderer and release its buffer pool. | 
Syntax | static int snd_adsp_tdm_playback_deinit(struct snd_adsp_tdm_playback *tdm_playback) | 
Parameter | struct snd_adsp_tdm_playback *tdm_playback | Pointer to TDM playback data
Return value | 0 | Success
 | -EINVAL | Cannot de-initialize TDM Renderer
Begin job
Return
-EINVAL
Error returned?
T
Destroy TDM Renderer component:
xf_adsp_tdm_renderer_destroy()
TDM Renderer is created
Send EMPTY_THIS_BUFFER with buffer length = 0 to TDM Renderer plugin to terminate the process
Release buffer pool by calling xf_adsp_free_mem_pool
T
F
F
TDM playback data allocated
T
F
Cancel high-resolution timer interrupt if high-resolution timer has been created and free TDM playback data
End job

## Slide 56: INTERNAL FUNCTIONS
snd_adsp_tdm_record_deinit()
snd_adsp_tdm_record_deinit |  | 
Synopsis | This function is used to de-initialize TDM Capture and release its buffer pool. | 
Syntax | static int snd_adsp_tdm_record_deinit(struct snd_adsp_tdm_record *tdm_record) | 
Parameter | struct snd_adsp_tdm_record *tdm_record | Pointer to TDM record data
Return value | 0 | Success
 | -EINVAL | Cannot de-initialize TDM Capture
Begin job
Return
-EINVAL
Error returned?
T
Destroy TDM Capture component:
xf_adsp_tdm_capture_destroy()
TDM Capture is created
Send EMPTY_THIS_BUFFER with buffer length = 0 to TDM Capture plugin to terminate the process
Release buffer pool by calling xf_adsp_free_mem_pool
T
F
F
TDM record data allocated
T
F
Cancel high-resolution timer interrupt if high-resolution timer has been created and free TDM record data
End job

## Slide 57: INTERNAL FUNCTIONS
snd_adsp_copy_data()
snd_adsp_copy_data |  | 
Synopsis | This function is used to copy from source to destination. It also converts data formats if data formats of ALSA buffer and ADSP buffer are mismatched. | 
Syntax | static inline void snd_adsp_copy_data(void *dst, void *src, int dst_size, int src_size) | 
Parameter | void *dst | Pointer to destination to which data are copied
 | void *src | Pointer to source place from which data are copied
 | int dst_size | Size of destination
 | int src_size | Size of source place
Return value | None | 
Begin job
memcpy(dst, src, dst_size)
Convert src from S24_LE to S24_3LE and copy data from src to dst
End job
dst_size < src_size
F
T
dst_size == src_size
T
F
Adjust destination and source position for the next copy according to each’s data format
still got data
Convert src from S24_3LE to S24_LE and copy data from src to dst
F
Adjust destination and source position for the next copy according to each’s data format
still got data
T
F
T
Conversion of data format between S24_3LE and S24_LE:
S24_LE to S24_3LE: S24_3LE to S24_LE:
s24_3le[0] = s24_le[0] s24_le[0] = s24_3le[0]
s24_3le[1] = s24_le[1] s24_le[1] = s24_3le[1]
s24_3le[2] = s24_le[2] s24_le[2] = s24_3le[2]
s24_le[3] = 0
s24_le:
1 byte
1 sample
1 sample
s24_3le:
1 sample
1 byte
1 sample

## Slide 58: INTERNAL FUNCTIONS
snd_adsp_pcm_transfer()
snd_adsp_pcm_transfer |  | 
Synopsis | This function is used to transfer data between ALSA and ADSP. | 
Syntax | static void snd_adsp_pcm_transfer(struct snd_pcm_substream *substream, struct snd_pcm_indirect *rec, size_t bytes) | 
Parameter | struct snd_pcm_substream *substream | Pointer to PCM substream
 | struct snd_pcm_indirect *rec | Pointer to indirect PCM
 | size_t bytes | Bytes to be transfered
Return value | None | 
Begin job
trans_byte > 0
trans_bytes = bytes
buf_bytes = base->buf_bytes
period_bytes = base->period_bytes
Get base data of playback/capture/TDM playback/TDM capture:
base = snd_adsp_get_base_from_substream
Get direction = substream->stream
Get ALSA buffer = substream->runtime->dma_area + rec->sw_data
base->buf_queue > 0 && trans_bytes >= period_bytes
T
F
B
F
A
T
direction is playback?
Decrement number of buffer in the queue and unlock resource
T
F
C
Get data buffer pointer from the stream:
data_buff = base->buffer[base->buf_idx]
D
Lock resource to process data
Unlock resource
End job
D

## Slide 59: INTERNAL FUNCTIONS
snd_adsp_pcm_transfer()
Copy data from user by calling snd_adsp_copy_data(data_buff, ALSA buf, buf_bytes, period_bytes)
idx exceed number of buffer
T
Send data_buff down with buf_bytes length down to Renderer/Equalizer/TDM Renderer plugin to empty_this_buffer
Advance to the next buffer:
base->buf_idx++;
Update trans_bytes = trans_bytes – period_bytes
A
Reset idx to 0
C
Copy data to user by calling snd_adsp_copy_data(ALSA_buf, data_buff, period_bytes, buf_bytes)
Send data_buff down with buf_bytes length down to Capture/Equalizer/TDM Capture plugin to fill_this_buffer
B
F
EmptyThisBuffer fail?
base->runtime_err = TRUE
base->runtime_err = TRUE
T
F
FillThisBuffer fail?
T
F

## Slide 60: INTERNAL FUNCTIONS
snd_adsp_get_eqz_params_from_control()
snd_adsp_get_eqz_params_from_control |  | 
Synopsis | In playback stream case, this function will copy equalizer param from control object to eqz params structure of equalizer plugin to set parameters for the plugin in next step | 
Syntax | static void snd_adsp_get_eqz_params_from_control(struct xf_adsp_equalizer_params *eqz_params, struct xf_adsp_equalizer_params *eqz_ctr_params, bool flag) | 
Parameter | struct xf_adsp_equalizer_params *eqz_params | Pointer to Equalizer parameters structure
 | struct xf_adsp_equalizer_params *eqz_params | Pointer to Equalizer param is stored in control object
 | bool flag | Flag indicating this function is used for setting or getting Equalizer parameters’ values. ‘True’ for setting and ‘false’ for getting
Return value | None | 

## Slide 61
Start
flag == true
In Parametric equalizer, get 9 filters parameters’ (filter type, bandwidth, gain, gainbase, frequency centre) value in eqz_ctr_params to eqz_params if those values are in eqz_ctr_params are valid.
End
yes
In Parametric equalizer, get 9 filters parameters’ (filter type, bandwidth, gain, gainbase, frequency centre) value in eqz_params to eqz_ctr_params.
no
eqz_ctr_params->eqz_type >= 0
eqz_params->eqz_type = eqz_ctr_params->eqz_type
no
In Graphic equalizer, get 5 graphic gains’ value in eqz_ctr_params to eqz_params if those values in eqz_ctr_params are valid
eqz_ctr_params->eqz_type = eqz_params->eqz_type
In Graphic equalizer, get 5 graphic gains’ value in eqz_params to eqz_ctr_params
snd_adsp_get_eqz_params_from_control()

## Slide 62: PCM INTERFACE
    snd_adsp_pcm_open
    snd_adsp_pcm_close
    snd_adsp_pcm_hw_params
    snd_adsp_pcm_hw_free
    snd_adsp_pcm_prepare
    snd_adsp_pcm_trigger
    snd_adsp_pcm_ack
PCM Interface functions: below functions are defined for PCM Interface

## Slide 63: PCM INTERFACE
Open callback: snd_adsp_pcm_open

## Slide 64: PCM INTERFACE
Open callback: snd_adsp_pcm_open
snd_adsp_pcm_open |  | 
Synopsis | This callback is used for record/playback streams and TDM streams. In Capture/Renderer case, it registers a Capture/Renderer plugin. It also registers Equalizer plugin if Equalizer switch is set to 1. Get range of hardware parameter into substream. In TDM Capture/Renderer case, it registers a TDM Capture/Renderer plugin. It also gets range of hardware parameter into substream. | 
Syntax | static int snd_adsp_pcm_open(struct snd_pcm_substream *substream) | 
Parameter | struct snd_pcm_substream *substream | Pointer to a pcm substream
Return value | 0 | Success
 | -EINVAL | The registering of Capture/Renderer or Equalizer plugin, or a TDM Capture/Renderer plugin fails.
Start
Get ADSP soundcard driver data
DAI index is RDR_DAI_IDXn
(n = 0,1,2,3)
End
No
Yes
Get DAI index
A
B
snd_pcm_hw_constraint_integer() to apply integer constraint to a period
snd_soc_set_runtime_hwparams(substream, hw param struct) to set runtime HW parameter
snd_pcm_hw_constraint_single() to make each period 1024 frames

## Slide 65: PCM INTERFACE
Open callback: snd_adsp_pcm_open
A
Substream is playback
End
No
No
snd_adsp_playback_init() to initialize Renderer
Error returned?
No
Yes
Yes
snd_adsp_playback_deinit()
snd_adsp_record_init() to initialize Capture
Error returned?
Yes
snd_adsp_record_deinit()
Return -EINVAL

## Slide 66: PCM INTERFACE
Open callback: snd_adsp_pcm_open
B
Substream is playback
End
No
No
snd_adsp_tdm_playback_init() to initialize TDM Renderer
Error returned?
No
Yes
Yes
snd_adsp_tdm_playback_deinit()
snd_adsp_tdm_record_init() to initialize TDM Capture
Error returned?
Yes
snd_adsp_tdm_record_deinit()
Return -EINVAL

## Slide 67: PCM INTERFACE
Close callback: snd_adsp_pcm_close

## Slide 68: PCM INTERFACE
Close callback: snd_adsp_pcm_close
Start
Get ADSP soundcard driver data
Get DAI index
DAI index is RDR_DAI_IDXn (n = 0,1,2,3)
A
No
Yes
err = 0
B
End
snd_adsp_pcm_close |  | 
Synopsis | This callback is used for record/playback streams and TDM streams. In Capture/Renderer case, it unregisters the Capture/Renderer plugin. It also unregisters Equalizer plugin if Equalizer switch is set to 1. In TDM Capture/Renderer case, it unregisters the TDM Capture/Renderer plugin. | 
Syntax | static int snd_adsp_pcm_close(struct snd_pcm_substream *substream) | 
Parameter | struct snd_pcm_substream *substream | Pointer to a pcm substream
Return value | 0 | Success
 | -EINVAL | The unregistering of the Capture/Renderer or Equalizer plugin, or TDM Capture/Renderer plugin fails.

## Slide 69: PCM INTERFACE
Close callback: snd_adsp_pcm_close
A
Substream is playback
End
No
No
Reset Renderer pointer to NULL
err = snd_adsp_playback_deinit() to de-initialize Renderer
Error returned?
No
Yes
Yes
err = snd_adsp_record_deinit() to de-initialize Capture
Error returned?
Yes
Reset Capture pointer to NULL
err = -EINVAL
err = -EINVAL

## Slide 70: PCM INTERFACE
Close callback: snd_adsp_pcm_close
B
Substream is playback
End
No
No
Reset TDM Renderer pointer to NULL
err = snd_adsp_tdm_playback_deinit() to de-initialize TDM Renderer
Error returned?
No
Yes
Yes
err = snd_adsp_tdm_record_deinit() to de-initialize TDM Capture
Error returned?
Yes
Reset TDM Capture pointer to NULL
err = -EINVAL
err = -EINVAL

## Slide 71: PCM INTERFACE
Prepare callback: snd_adsp_pcm_prepare

## Slide 72: PCM INTERFACE
Prepare callback: snd_adsp_pcm_prepare
snd_adsp_pcm_prepare |  | 
Synopsis | Initialize hardware data position with value 0 then set default volume value is 100% unless user set volume before. In this function, Capture/Renderer plugin or TDM Capture/Renderer is set up to go to running state. In Capture/Renderer case, if Equalizer switch is enabled, it is also set up, then set route Capture/Renderer with Equalizer. This callback is also called when data overrun or underrun error occurs. | 
Syntax | static int snd_adsp_pcm_prepare(struct snd_pcm_substream *substream) | 
Parameter | struct snd_pcm_substream *substream | Pointer to a pcm substream
Return value | 0 | Success
 | -EINVAL | Cannot set parameters to Capture/Renderer/Equalizer/TDM Capture/TDM Renderer plugin. Cannot allocate ADSP buffer pool. Cannot route Equalizer and Capture/Renderer, ADSP plugin initialization fails.
Start
Get ADSP soundcard driver data
Get DAI index
DAI index is RDR_DAI_IDXn
(n=0,1,2,3)
A
No
Yes
B
End

## Slide 73: PCM INTERFACE
A
Substream is playback
End
No
No
snd_adsp_playback_prepare() to set parameters and allocate necessary memory regions for Renderer
Error returned?
No
Yes
Yes
snd_adsp_record_prepare() to set paramters and allocate necessary memory regions for Capture
Error returned?
Yes
No
Return -EINVAL
Prepare callback: snd_adsp_pcm_prepare

## Slide 74: PCM INTERFACE
B
Substream is playback
End
No
No
snd_adsp_tdm_playback_prepare() to set parameters and allocate necessary memory regions for TDM Renderer
Error returned?
No
Yes
Yes
snd_adsp_tdm_record_prepare() to set paramters and allocate necessary memory regions for TDM Capture
Error returned?
Yes
No
Return -EINVAL
Prepare callback: snd_adsp_pcm_prepare

## Slide 75: PCM INTERFACE
HW parameter callback: snd_adsp_pcm_hw_params

## Slide 76: PCM INTERFACE
HW parameter callback: snd_adsp_pcm_hw_params
snd_adsp_pcm_hw_params |  | 
Synopsis | This callback is used to allocate ALSA buffer to transfer data. It also sets expiration time for high-resolution timer. | 
Syntax | static int snd_adsp_pcm_hw_params(struct snd_pcm_substream *substream, struct snd_pcm_hw_params *hw_params) | 
Parameter | struct snd_pcm_substream *substream | Pointer to a pcm substream.
 | struct snd_pcm_hw_params hw_params | Hardware parameter is set up by the application
Return value | 0 | Success
 | -ENOMEM | Cannot allocate ALSA buffer
Start
End
Get base data of playback/capture/TDM playback/TDM capture
base = snd_adsp_get_base_from_substream
Error returned
snd_pcm_lib_malloc_pages() for allocating ALSA buffer to transfer data
No
Yes
Set expiration time for high-resolution timer. This value is equal to duration of a frame transfer
Return -ENOMEM
Reset ALSA buffer
(substream->runtime->dma_are)

## Slide 77: PCM INTERFACE
HW free callback: snd_adsp_pcm_hw_free

## Slide 78: PCM INTERFACE
HW free callback: snd_adsp_pcm_hw_free
snd_adsp_pcm_hw_free |  | 
Synopsis | This callback is used to deallocate ALSA buffer. | 
Syntax | static int snd_adsp_pcm_hw_free(struct snd_pcm_substream *substream) | 
Parameter | struct snd_pcm_substream *substream | Pointer to a pcm substream.
Return value | 0 | Success
 | -EINVAL | Cannot deallocate ALSA buffer
Start
End
Error returned
snd_pcm_lib_free_pages() for deallocating ALSA buffer
No
Yes
Return -EINVAL

## Slide 79: PCM INTERFACE
Trigger callback: snd_adsp_pcm_trigger

## Slide 80: PCM INTERFACE
Trigger callback: snd_adsp_pcm_trigger
snd_adsp_pcm_trigger |  | 
Synopsis | Start, stop, resume, suspend PCM substream | 
Syntax | static int snd_adsp_pcm_trigger(struct snd_pcm_substream *substream, int idx) | 
Parameter | struct snd_pcm_substream *substream | Pointer to a pcm substream
 | int idx | Start, stop, resume, suspend command
Return value | 0 | Success
 | -EINVAL | Invalid command, cannot send fill buffer command to ADSP when performing capture, TDM capture functions
Start
Get ADSP soundcard driver data
idx is start or resume
End
No
Start high-resolution timer
Yes
Yes
No
idx is stop or suspend
Return -EINVAL
Send available buffer to ADSP in case of capture and TDM capture function
Error returned
Return -EINVAL

## Slide 81: PCM INTERFACE
Pointer callback: snd_adsp_pcm_pointer

## Slide 82: PCM INTERFACE
Pointer callback: snd_adsp_pcm_pointer
snd_adsp_pcm_pointer |  | 
Synopsis | Return data position on the buffer in frames. | 
Syntax | static snd_pcm_uframes_t snd_adsp_pcm_pointer(struct snd_pcm_substream *substream) | 
Parameter | struct snd_pcm_substream *substream | Pointer to a pcm substream
Return value | pointer | Position offset in frames on hardware buffer.
Start
A
Lock the resource base->lock
hw_idx >= hw_buffer_size
Lock resource base->lock
hw_idx -= (hw_buffer_size / period_bytes) * buf_bytes
Unlock resource base->lock
No
Yes
hw_idx = (base->hw_idx / base->buf_bytes) * base->period_bytes
Get base data of playback/capture/TDM playback/TDM capture
base = snd_adsp_get_base_from_substream()
Unlock the resource base->lock
hw_buffer_size = base->pcm_indirect.hw_buffer_size
Return pointer

## Slide 83: PCM INTERFACE
Pointer callback: snd_adsp_pcm_pointer
A
End
Stream is playback
pointer = snd_pcm_indirect_playback_pointer() to get the data position
No
Yes
pointer = snd_pcm_indirect_capture_pointer() to get the data position

## Slide 84: PCM INTERFACE
Ack callback: snd_adsp_pcm_ack

## Slide 85: PCM INTERFACE
Ack callback: snd_adsp_pcm_ack
snd_adsp_pcm_ack |  | 
Synopsis | This callback is called in read/write operation. It calls transfer function to transfer data from ALSA buffer to ADSP buffer and vice versa. | 
Syntax | static int snd_adsp_pcm_ack(struct snd_pcm_substream *substream) | 
Parameter | struct snd_pcm_substream *substream | Pointer to a pcm substream
Return value | 0 | Success
 | -EINVAL | Cannot transfer data from ALSA buffer to ADSP buffer, or runtime error has been trigger.
Start
End
Get base data of playback/capture/TDM playback/TDM capture:
base = snd_adsp_get_base_from_substream
Stream is playback
snd_pcm_indirect_playback_transfer() to transfer data
No
Yes
snd_pcm_indirect_capture_transfer() to transfer data
base->runtime_err == TRUE
No
Return -EINVAL
Yes

## Slide 86: PCM INTERFACE
snd_adsp_pcm_ack
{ …
xf_adsp_empty_this_buffer
…}
    Scheme of hw position update:
        For playback/TDM playback stream:
        base->hw_idx is position of hardware buffer
snd_adsp_pcm_open
hw_idx = 0
snd_adsp_pcm_prepare
hw_idx = 0
snd_adsp_pcm_pointer
snd_adsp_rdr_empty_buf_done
hw_idx += length
Main thread
Response thread
Note:
Value length is get from response message structure info.
Next | ID | opcode | length | address
Structure of messge buffer |  |  |  | 
Wait respone message

## Slide 87: PCM INTERFACE
snd_adsp_pcm_ack
{ …
xf_adsp_fill_this_buffer
… }
    Scheme of hw position update:
        For capture/TDM capture stream:
        base->hw_idx is position of hardware buffer
snd_adsp_capture_pcm_open
hw_idx = 0
snd_adsp_pcm_prepare
hw_idx = 0
snd_adsp_pcm_pointer
snd_adsp_cap_fill_buf_done
hw_idx += length
Wait response message
Main thread
Response thread
Note:
Value length is get from response message structure info.
Next | ID | opcode | length | address
Structure of messge buffer |  |  |  | 

## Slide 88: CONTROL INTERFACE
Volume Control
Sample Rate Converter Control
Equalizer Control
Renderer Output Channel Control

## Slide 89: CONTROL INTERFACE
Volume Control:
struct snd_kcontrol_new snd_adsp_playback_volume_control[MAX_DAI_IDX – 1]. n-th element is assigned as below (n = 0, 1, 2, 3):
snd_adsp_playback_volume_control[n] =
{
.iface = SNDRV_CTL_ELEM_IFACE_MIXER,
.index = RDR_DAI_IDXn,
.name = “PlaybackVolume”,
.info = &snd_adsp_control_volume_info,
.get = &snd_adsp_control_volume_get,
.put = &snd_adsp_control_volume_put
}
[Note]: struct snd_kcontrol_new is referred to https://elixir.bootlin.com/linux/v4.0/source/include/sound/control.h#L44
SNDRV_CTL_ELEM_IFACE_MIXER is refered to https://elixir.bootlin.com/linux/latest/source/include/uapi/sound/asound.h#L851

## Slide 90: CONTROL INTERFACE
Volume Control:
struct snd_kcontrol_new snd_adsp_capture_volume_control[MAX_DAI_IDX – 1]. n-th element is assigned as below (n = 0, 1, 2, 3):
snd_adsp_capture_volume_control[n] =
{
.iface = SNDRV_CTL_ELEM_IFACE_MIXER,
.index = RDR_DAI_IDXn,
.name = “CaptureVolume”,
.info = &snd_adsp_control_volume_info,
.get = &snd_adsp_control_volume_get,
.put = &snd_adsp_control_volume_put
}
[Note]: struct snd_kcontrol_new is referred to https://elixir.bootlin.com/linux/v4.0/source/include/sound/control.h#L44
SNDRV_CTL_ELEM_IFACE_MIXER is refered to https://elixir.bootlin.com/linux/latest/source/include/uapi/sound/asound.h#L851

## Slide 91: CONTROL INTERFACE
Volume Control:
struct snd_kcontrol_new snd_adsp_tdm_playback_volume_control =
{
.iface = SNDRV_CTL_ELEM_IFACE_MIXER,
.name = “TDMPlaybackVolume”,
.info = &snd_adsp_control_volume_info,
.get = &snd_adsp_control_volume_get,
.put = &snd_adsp_control_volume_put
}
[Note]: struct snd_kcontrol_new is referred to https://elixir.bootlin.com/linux/v4.0/source/include/sound/control.h#L44
SNDRV_CTL_ELEM_IFACE_MIXER is refered to https://elixir.bootlin.com/linux/latest/source/include/uapi/sound/asound.h#L851

## Slide 92: CONTROL INTERFACE
Volume Control:
struct snd_kcontrol_new snd_adsp_tdm_capture_volume_control =
{
.iface = SNDRV_CTL_ELEM_IFACE_MIXER,
.name = “TDMCaptureVolume”,
.info = &snd_adsp_control_volume_info,
.get = &snd_adsp_control_volume_get,
.put = &snd_adsp_control_volume_put
}
[Note]: struct snd_kcontrol_new is referred to https://elixir.bootlin.com/linux/v4.0/source/include/sound/control.h#L44
SNDRV_CTL_ELEM_IFACE_MIXER is refered to https://elixir.bootlin.com/linux/latest/source/include/uapi/sound/asound.h#L851

## Slide 93: CONTROL INTERFACE
Volume Control:
snd_adsp_control_volume_info
snd_adsp_control_volume_get
snd_adsp_control_volume_put

## Slide 94: CONTROL INTERFACE
Volume Control:
snd_adsp_control_volume_info
Element Information | Description
uinfo->type | The type field specifies the type of the control. There are BOOLEAN, INTEGER, ENUMERATED, BYTES, IEC958 and INTEGER64. Volume control use INTEGER type
uinfo->count | count field specifies the number of elements in this control.
uinfo->value.integer.min | -1 means volume does not set
uinfo->value.integer.max | 799 means volume increase 799%
Implementation in source code:
int snd_adsp_control_volume_info(struct snd_kcontrol *kcontrol, struct snd_ctl_elem_info *uinfo)
{
  ….
  uinfo->type = SNDRV_CTL_ELEM_TYPE_INTEGER;
  uinfo->count = 1;
  uinfo->value.integer.min = -1;
  uinfo->value.integer.max = 799;
  ….
}
snd_adsp_control_volume_info |  | 
Synopsis | Get detailed information on volume control in playback, capture, TDM playback, TDM capture cases | 
Syntax | int snd_adsp_control_volume_info(struct snd_kcontrol *kcontrol, struct snd_ctl_elem_info *uinfo) | 
Parameter | struct snd_kcontrol *kcontrol | Pointer to control instance
 | struct snd_ctl_elem_info *uinfo | Pointer to info structure of volume control
Return value | 0 | Always return 0

## Slide 95: CONTROL INTERFACE
Volume Control:
snd_adsp_control_volume_get
snd_adsp_control_volume_get |  | 
Synopsis | Get the PCM volume rate setting value in playback, capture, TDM playback, TDM capture cases | 
Syntax | int snd_adsp_control_volume_get(struct snd_kcontrol *kcontrol, struct snd_ctl_elem_value *ucontrol) | 
Parameter | struct snd_kcontrol *kcontrol | Pointer to control instance
 | struct snd_ctl_elem_value *ucontrol | Pointer to volume value
Return value | 0 | Success
 | -EINVAL | Can’t get parameter information from ADSP.

## Slide 96
snd_adsp_control_volume_get
Indentify control type(playback/capture/TDM playback/TDM capture)
Start
Handle state = renderer state/ capture state/TDM renderer state/TDM capture state
Command idx = volume setting subcommand for renderer/capture/TDM renderer/TDM capture
DAI index is RDR_DAI_IDXn (n = 0, 1, 2, 3)/TDM_DAI_IDX (got from kcontrol->id.index)
direction = DIRECT_PLAYBACK/DIRECT_RECORD
Handle ID = Renderer ID /Capture ID/TDM Renderer ID/TDM Capture ID
Call xf_adsp_get_param(Handle ID, Command idx, &volume)
To get volume value from ADSP => volume
Process value volume
if(volume == 0xffffffff) {… ucontrol->value.integer.value[0] = -1 …}
else { …ucontrol->value.integer.value[0] = (volume * 100) >> 20…}
Is Renderer/Capture/TDM Renderer/TDM Capture Plugin running?
Get information from control structure stored in ADSP ALSA driver.
+ Renderer/Capture case, ucontrol->value.integer.value[0] = (ctr_if->vol_rate[direction][DAI index] * 100) >> 20.
+ TDM Renderer/TDM capture case, ucontrol->value.integer.value[0] = (ctr_if->tdm_vol_rate[direction] * 100) >> 20.
[Note] The control structure contains volume value set by an audio app. When Renderer/Capture/TDM Renderer/TDM Capture plugin run after, it set volume with above volume value.
No
Yes
End
error?
Return -EINVAL
Yes
No

## Slide 97: CONTROL INTERFACE
Volume Control:
snd_adsp_control_volume_put
snd_adsp_control_volume_put |  | 
Synopsis | Set the PCM volume rate value in playback, capture, TDM playback, TDM capture cases | 
Syntax | int snd_adsp_control_volume_put(struct snd_kcontrol *kcontrol, struct snd_ctl_elem_value *ucontrol) | 
Parameter | struct snd_kcontrol *kcontrol | Pointer to control instance
 | struct snd_ctl_elem_value *ucontrol | Pointer to volume setting value
Return value | 0 | Hardware parameter is still not changed.
 | 1 | Hardware parameter is changed.
 | -EINVAL | Can’t set parameter to ADSP. Set volume TDM Capture/TDM Renderer at runtime

## Slide 98
snd_adsp_control_volume_put
Indentify control type(playback/capture/TDM playback/TDM capture)
Start
Handle state = renderer state/ capture state/TDM renderer state/TDM capture state
Command idx = volume setting subcommand for renderer/capture/TDM renderer/TDM capture
DAI index is RDR_DAI_IDXn (n = 0, 1, 2, 3)/TDM_DAI_IDX (got from kcontrol->id.index)
direction = DIRECT_PLAYBACK/DIRECT_RECORD
Handle ID = Renderer ID /Capture ID/TDM Renderer ID/TDM capture
volume = (ucontrol->value.integer.value[0] * (1 << 20))/100
Call xf_adsp_set_param(Handle ID, Command idx, volume)
To set volume value for ADSP
Call xf_adsp_get_param(Handle ID, Command idx, &volume_get)
Compare volume and volume get.
volume != volume_get return 0(means not change)
volume == volume_get return 1(means change)
Is Renderer/Capture/TDM Renderer/TDM Capture Plugin running?
Store volume value into the control structure.
+ Renderer/Capture case:
ctr_if->vol_rate[direction][DAI index] = volume and return 1
+ TDM Renderer/TDM capture case:
ctr_if->tdm_vol_rate[direction] = volume and return 1
[Note] When Renderer/Capture/TDM Renderer/TDM Capture plugin run after, it will set volume with value stored in the control structure
No
Yes
End
Return -EINVAL
error?
error?
Yes
No
Yes
No
is it TDM Renderer/TDM Capture
Yes
No

## Slide 99: CONTROL INTERFACE
Sample Rate Converter Control:
struct snd_kcontrol_new snd_adsp_playback_sample_rate_out_control[MAX_DAI_IDX – 1]. n-th element is assigned as below (n = 0, 1, 2, 3):
snd_adsp_playback_sample_rate_out_control[n] =
{
.iface = SNDRV_CTL_ELEM_IFACE_MIXER,
.index = RDR_DAI_IDXn,
.name = “PlaybackOutRate”,
.info = &snd_adsp_control_sample_rate_info,
.get = &snd_adsp_control_sample_rate_get,
.put = &snd_adsp_control_sample_rate_put
}
[Note]: struct snd_kcontrol_new is referred to https://elixir.bootlin.com/linux/v4.0/source/include/sound/control.h#L44
SNDRV_CTL_ELEM_IFACE_MIXER is refered to https://elixir.bootlin.com/linux/latest/source/include/uapi/sound/asound.h#L851

## Slide 100: CONTROL INTERFACE
Sample Rate Converter Control:
struct snd_kcontrol_new snd_adsp_capture_sample_rate_in_control[MAX_DAI_IDX – 1]. n-th element is assigned as below (n = 0, 1, 2, 3):
snd_adsp_capture_sample_rate_in_control[n] =
{
.iface = SNDRV_CTL_ELEM_IFACE_MIXER,
.index = RDR_DAI_IDXn,
.name = “CaptureInRate”,
.info = &snd_adsp_control_sample_rate_info,
.get = &snd_adsp_control_sample_rate_get,
.put = &snd_adsp_control_sample_rate_put
}
[Note]: struct snd_kcontrol_new is referred to https://elixir.bootlin.com/linux/v4.0/source/include/sound/control.h#L44
SNDRV_CTL_ELEM_IFACE_MIXER is refered to https://elixir.bootlin.com/linux/latest/source/include/uapi/sound/asound.h#L851

## Slide 101: CONTROL INTERFACE
Sample Rate Converter Control:
struct snd_kcontrol_new snd_adsp_tdm_playback_sample_rate_out_control =
{
.iface = SNDRV_CTL_ELEM_IFACE_MIXER,
.name = “TDMPlaybackOutRate”,
.info = &snd_adsp_control_sample_rate_info,
.get = &snd_adsp_control_sample_rate_get,
.put = &snd_adsp_control_sample_rate_put
}
[Note]: struct snd_kcontrol_new is referred to https://elixir.bootlin.com/linux/v4.0/source/include/sound/control.h#L44
SNDRV_CTL_ELEM_IFACE_MIXER is refered to https://elixir.bootlin.com/linux/latest/source/include/uapi/sound/asound.h#L851

## Slide 102: CONTROL INTERFACE
Sample Rate Converter Control:
struct snd_kcontrol_new snd_adsp_tdm_capture_sample_rate_in_control =
{
.iface = SNDRV_CTL_ELEM_IFACE_MIXER,
.name = “TDMCaptureInRate”,
.info = &snd_adsp_control_sample_rate_info,
.get = &snd_adsp_control_sample_rate_get,
.put = &snd_adsp_control_sample_rate_put
}
[Note]: struct snd_kcontrol_new is referred to https://elixir.bootlin.com/linux/v4.0/source/include/sound/control.h#L44
SNDRV_CTL_ELEM_IFACE_MIXER is refered to https://elixir.bootlin.com/linux/latest/source/include/uapi/sound/asound.h#L851

## Slide 103: CONTROL INTERFACE
Sample Rate Converter Control:
snd_adsp_control_sample_rate_info
snd_adsp_control_sample_rate_get
snd_adsp_control_sample_rate_put

## Slide 104: CONTROL INTERFACE
Sample Rate Converter Control:
snd_adsp_control_sample_rate_info
Element Information | Description
uinfo->type | The type field specifies the type of the control. There are BOOLEAN, INTEGER, ENUMERATED, BYTES, IEC958 and INTEGER64. Volume control use INTEGER type
uinfo->count | count field specifies the number of elements in this control. A sample rate converter is used => count = 1
uinfo->value.integer.min | -1 means volume does not set
uinfo->value.integer.max | 48000. ADSP support 32000, 44100, 48000Hz
Implementation in source code:
int snd_adsp_control_sample_rate_info(struct snd_kcontrol *kcontrol, struct snd_ctl_elem_info *uinfo)
{
  ….
  uinfo->type = SNDRV_CTL_ELEM_TYPE_INTEGER;
  uinfo->count = 1;
  uinfo->value.integer.min = -1;
  uinfo->value.integer.max = 48000;
  ….
}
snd_adsp_control_sample_rate_info |  | 
Synopsis | Get detailed information on sample rate control in playback, capture, TDM playback, TDM capture cases | 
Syntax | int snd_adsp_control_sample_rate_info(struct snd_kcontrol *kcontrol, struct snd_ctl_elem_info *uinfo) | 
Parameter | struct snd_kcontrol *kcontrol | Pointer to control instance
 | struct snd_ctl_elem_info *uinfo | Pointer to info structure of sample rate control
Return value | 0 | Always return 0

## Slide 105: CONTROL INTERFACE
Sample Rate Converter Control:
snd_adsp_control_sample_rate_get
snd_adsp_control_sample_rate_get |  | 
Synopsis | Get sample rate value of hardware output in playback/TDM playback case and sample rate of hardware input in capture/TDM capture case. | 
Syntax | int snd_adsp_control_sample_rate_get(struct snd_kcontrol *kcontrol, struct snd_ctl_elem_value *ucontrol) | 
Parameter | struct snd_kcontrol *kcontrol | Pointer to control instance
 | struct snd_ctl_elem_value *ucontrol | Pointer to sample rate value
Return value | 0 | Success
 | -EINVAL | Can’t get parameter information from ADSP.

## Slide 106
snd_adsp_control_sample_rate_get
Indentify control type(playback/capture/TDM playback/TDM capture)
Start
Handle state = renderer state/ capture state/TDM renderer state/TDM capture state
Command idx = sample rate getting subcommand for renderer/capture/TDM renderer/TDM capture
DAI index = RDR_DAI_IDXn (n = 0, 1, 2, 3)/TDM_DAI_IDX (got from kcontrol->id.index)
direction = DIRECT_PLAYBACK/DIRECT_RECORD
Handle ID = Renderer ID /Capture ID/TDM Renderer ID/TDM capture
Call xf_adsp_get_param(Handle ID, Command idx, &samplerate)
To get volume value from ADSP => samplerate
Is Renderer/Capture/TDM Renderer/TDM Capture Plugin running?
Renderer/Capture case:
ucontrol->value.integer.value[0] = adsp_card->ctr_if.sample_rate[direction][DAI index]
+ TDM Renderer/TDM capture case:
ucontrol->value.integer.value[0] = adsp_card->ctr_if.tdm_sample_rate[direction]
No
Yes
End
Return -EINVAL
error?
Yes
No

## Slide 107: CONTROL INTERFACE
Sample Rate Converter Control:
snd_adsp_control_sample_rate_put
snd_adsp_control_sample_rate_put |  | 
Synopsis | Set sample rate for hardware output in playback and TDM playback case, input in the capture and TDM capture case | 
Syntax | int snd_adsp_control_sample_rate_put(struct snd_kcontrol *kcontrol, struct snd_ctl_elem_value *ucontrol) | 
Parameter | struct snd_kcontrol *kcontrol | Pointer to control instance
 | struct snd_ctl_elem_value *ucontrol | Pointer to sample rate value
Return value | 1 | Hardware parameter is changed.
 | -EINVAL | Can’t set parameter to ADSP.

## Slide 108
snd_adsp_control_sample_rate_put
Indentify control type(playback/capture/TDM playback/TDM capture)
Start
Handle state = renderer state/ capture state/TDM renderer state/TDM capture state
Command idx = sample rate getting subcommand for renderer/capture/TDM renderer/TDM capture
DAI index = RDR_DAI_IDXn (n = 0, 1, 2, 3)/TDM_DAI_IDX (got from kcontrol->id.index)
direction = DIRECT_PLAYBACK/DIRECT_RECORD
Return -EINVAL means that can’t set sample rate when Renderer/Capture/TDM Renderer/TDM Capture is running.
Renderer/Capture/TDM Renderer/TDM Capture Plugin running?
Store volume value into the control structure.
+ Renderer/Capture case:
ctr_if->sample_rate[direction][DAI index] = ucontrol->value.integer.value[0] and return 1
+ TDM Renderer/TDM capture case:
ctr_if->tdm_sample_rate[direction] = ucontrol->value.integer.value[0] and return 1
[Note] When Renderer/Capture/TDM Renderer/TDM Capture plugin run after, it will set sampling rate with value stored in the control structure
No
Yes
End
[Note]: Sample rate setting is not available for real time. So when setting sample rate after playback/capture/TDM playback/TDM capture data it should return -EINVAL.

## Slide 109: CONTROL INTERFACE
Equalizer Switch Control: enable or disable Equalizer function
struct snd_kcontrol_new snd_adsp_playback_equalizer_switch_control[MAX_DAI_IDX - 1]. n-th element is assigned as below (n = 0, 1, 2, 3):
snd_adsp_playback_equalizer_switch_control[n] =
{
.iface = SNDRV_CTL_ELEM_IFACE_MIXER,
.index = RDR_DAI_IDXn,
.name = “PlaybackEQZSwitch”,
.info = &snd_adsp_control_eqz_switch_info,
.get = &snd_adsp_control_eqz_switch_get,
.put = &snd_adsp_control_eqz_switch_put
}
[Note]: struct snd_kcontrol_new is referred to https://elixir.bootlin.com/linux/v4.0/source/include/sound/control.h#L44
SNDRV_CTL_ELEM_IFACE_MIXER is refered to https://elixir.bootlin.com/linux/latest/source/include/uapi/sound/asound.h#L851

## Slide 110: CONTROL INTERFACE
Equalizer Switch Control: enable or disable Equalizer function
struct snd_kcontrol_new snd_adsp_capture_equalizer_switch_control[MAX_DAI_IDX - 1]. n-th element is assigned as below (n = 0, 1, 2, 3):
snd_adsp_capture_equalizer_switch_control[n] =
{
.iface = SNDRV_CTL_ELEM_IFACE_MIXER,
.index = RDR_DAI_IDXn,
.name = “CaptureEQZSwitch”,
.info = &snd_adsp_control_eqz_switch_info,
.get = &snd_adsp_control_eqz_switch_get,
.put = &snd_adsp_control_eqz_switch_info_put
}
[Note]: struct snd_kcontrol_new is referred to https://elixir.bootlin.com/linux/v4.0/source/include/sound/control.h#L44
SNDRV_CTL_ELEM_IFACE_MIXER is refered to https://elixir.bootlin.com/linux/latest/source/include/uapi/sound/asound.h#L851

## Slide 111: CONTROL INTERFACE
Equalizer Switch Control: enable or disable Equalizer function
snd_adsp_control_eqz_switch_info
snd_adsp_control_eqz_switch_get
snd_adsp_control_eqz_switch_put

## Slide 112: CONTROL INTERFACE
Equalizer Switch Control:
snd_adsp_control_eqz_switch_info
Element Information | Description
uinfo->type | The type field specifies the type of the control. There are BOOLEAN, INTEGER, ENUMERATED, BYTES, IEC958 and INTEGER64. Volume control use INTEGER type
uinfo->count | count field specifies the number of elements in this control. One switch is used => count = 1
uinfo->value.integer.min | 0 means Equalizer function is not enabled
uinfo->value.integer.max | 1 means Equalizer function is enabled
Implementation in source code:
int snd_adsp_control_eqz_switch_info(struct snd_kcontrol *kcontrol, struct snd_ctl_elem_info *uinfo)
{
  ….
  uinfo->type = SNDRV_CTL_ELEM_TYPE_INTEGER;
  uinfo->count = 1;
  uinfo->value.integer.min = 0;
  uinfo->value.integer.max = 1;
  ….
}
snd_adsp_control_eqz_switch_info |  | 
Synopsis | Get detailed info on the equalizer switch control in playback, capture cases | 
Syntax | int snd_adsp_control_eqz_switch_info(struct snd_kcontrol *kcontrol, struct snd_ctl_elem_info *uinfo) | 
Parameter | struct snd_kcontrol *kcontrol | Pointer to control instance
 | struct snd_ctl_elem_info *uinfo | Pointer to info structure of the equalizer switch control
Return value | 0 | Always return 0

## Slide 113: CONTROL INTERFACE
Equalizer Switch Control :
snd_adsp_control_eqz_switch_get
snd_adsp_control_eqz_switch_get |  | 
Synopsis | Get status of Equalizer control in playback, capture cases | 
Syntax | int snd_adsp_control_eqz_switch_get(struct snd_kcontrol *kcontrol, struct snd_ctl_elem_value *ucontrol) | 
Parameter | struct snd_kcontrol *kcontrol | Pointer to control instance
 | struct snd_ctl_elem_value *ucontrol | Pointer to equalizer switch.
Return value | 0 | Success
Indentify control type(playback/capture) and DAI index
Start
direction = DIRECT_PLAYBACK/DIRECT_RECORD
ucontrol->value.integer.value[0] = adsp_card->ctr_if.eqz_switch[direction][DAI index]
End

## Slide 114: CONTROL INTERFACE
Equalizer Switch Control:
snd_adsp_control_eqz_switch_put
snd_adsp_control_eqz__switch_put |  | 
Synopsis | Enable or disable Equalizer control in playback, capture cases | 
Syntax | int snd_adsp_control_eqz_switch_put(struct snd_kcontrol *kcontrol, struct snd_ctl_elem_value *ucontrol) | 
Parameter | struct snd_kcontrol *kcontrol | Pointer to control instance
 | struct snd_ctl_elem_value *ucontrol | Pointer to equalizer switch
Return value | 1 | Success
 | -EINVAL | Can’t enable EQZ when Renderer/Capture plugin is running
Indentify control type(playback/capture) and DAI index
Start
direction = DIRECT_PLAYBACK/DIRECT_RECORD
Handle state of playback/capture
adsp_card-> ctr_if.eqz_switch[direction][DAI index]
= ucontrol->value.integer.value[0] and return 1
End
Is Renderer/CapturePlugin running?
Return –EINVAL means that can’t enable EQZ when Renderer/Capture plugin is running
Yes
No

## Slide 115: CONTROL INTERFACE
Equalizer Control: Setting and getting Equalizer parameters
struct snd_kcontrol_new snd_adsp_playback_equalizer_control[MAX_DAI_IDX - 1]. n-th element is assigned as below (n = 0, 1, 2, 3):
snd_adsp_playback_equalizer_control[n] =
{
.iface = SNDRV_CTL_ELEM_IFACE_MIXER,
.index = RDR_DAI_IDXn,
.name = “PlaybackEQZControl”,
.info = &snd_adsp_control_eqz_info,
.get = &snd_adsp_control_eqz_get,
.put = &snd_adsp_control_eqz_put
}
[Note]: struct snd_kcontrol_new is referred to https://elixir.bootlin.com/linux/v4.0/source/include/sound/control.h#L44
SNDRV_CTL_ELEM_IFACE_MIXER is refered to https://elixir.bootlin.com/linux/latest/source/include/uapi/sound/asound.h#L851

## Slide 116: CONTROL INTERFACE
Equalizer Control: Setting and getting Equalizer parameters
struct snd_kcontrol_new snd_adsp_capture_equalizer_control[MAX_DAI_IDX - 1]. n-th element is assigned as below (n = 0, 1, 2, 3):
snd_adsp_capture_equalizer_control[n] =
{
.iface = SNDRV_CTL_ELEM_IFACE_MIXER,
.index = RDR_DAI_IDXn,
.name = “CaptureEQZControl”,
.info = &snd_adsp_control_eqz_info,
.get = &snd_adsp_control_eqz_get,
.put = &snd_adsp_control_eqz_put
}
[Note]: struct snd_kcontrol_new is referred to https://elixir.bootlin.com/linux/v4.0/source/include/sound/control.h#L44
SNDRV_CTL_ELEM_IFACE_MIXER is refered to https://elixir.bootlin.com/linux/latest/source/include/uapi/sound/asound.h#L851

## Slide 117: CONTROL INTERFACE
Equalizer Control:
Parametric Equalizer:
Equalizer Control
ADSP
Filter 1
Filter 2
Filter 9
………….…….
Set/Get parameter
fc, type, bw, gain, gain base
filter id = 2
Set/Get parameter
fc, type, bw, gain, gain base
filter id = 1
filter id = 9

## Slide 118: CONTROL INTERFACE
Equalizer Control:
Graphic Equalizer:
Equalizer Control
ADSP
Filter 1
Filter 2
Filter 5
………….…….
Set/Get parameter
graphic gain
filter id = 2
Set/Get parameter
graphic gain
filter id = 1
filter id = 5

## Slide 119: CONTROL INTERFACE
Equalizer Control: This control set/get parameters(fc, type, bw, gain, base gain) for every filter.
Beside, parameters are different from format and value range.
So these paramters should use integer format and same value range -1 to 0x7ffffff.
Filter id is added to specify the filter needs to set/get param.
Below table describe detail information of Equalizer Control:
Element Information | Description
Type of control | INTEGER
Number of element in the control | 55
Minimum value | - 1
Maximum value | 0x7FFFFFFF
Implementation in source code:
int snd_adsp_control_equalizer_info(struct snd_kcontrol *kcontrol, struct snd_ctl_elem_info *uinfo)
{
  ….
  uinfo->type = SNDRV_CTL_ELEM_TYPE_INTEGER;
  uinfo->count = 55;
  uinfo->value.integer.min = -1;
  uinfo->value.integer.max = 0x7fffffff;
  ….
}

## Slide 120: CONTROL INTERFACE
Equalizer Control: Detail information of control
Below table explains that why number of element in control is 55
Parameter | Number | Number of element in control
EQZ type | 1 | 1 + 9 x 6 = 55
Filter index | 9 | 
Frequency center | 9 | 
Band width | 9 | 
Filter type | 9 | 
Gain base | 9 | 
Gain | 9 | 
Every parameter is as a element of the control

## Slide 121: CONTROL INTERFACE
Equalizer Control: Detail information of control
Below table explains that why value range of control is -1 – 0x7FFFFFFF
Equalizer type | Parameter | Format | Actual value range | Value range of Control
Parametric | fc | Integer |  | 
 | bw | Fixed point Q5.27 |  | 
 | type | Integer |  | 
 | gain base | Fixed point Q4.28 |  | 
 | gain | Fixed point Q4.28 | - | 
Graphic | graphic gain | Fixed point Q4.28 | - | 
Equalizer type | Parameter | Format | Actual value range | Value range of Control
Parametric | fc | Integer |  | 
 | bw | Fixed point Q5.27 |  | 
 | type | Integer |  | 
 | gain base | Fixed point Q4.28 |  | 
 | gain | Fixed point Q4.28 |  | 
Graphic | graphic gain | Fixed point Q4.28 |  | 
-1 means that the param is not set.
0x7FFFFFFF to cover for maximum value range of all parameter

## Slide 122: CONTROL INTERFACE
Equalizer Control: Elements order of control for Parametric Equalizer
Eqz_type, (Filter index, Frequency center, Band width, Filter type, Gain base, Gain),
(Filter index, Frequency center, Band width, Filter type, Gain base, Gain),
(Filter index, Frequency center, Band width, Filter type, Gain base, Gain),
(Filter index, Frequency center, Band width, Filter type, Gain base, Gain),
(Filter index, Frequency center, Band width, Filter type, Gain base, Gain),
(Filter index, Frequency center, Band width, Filter type, Gain base, Gain),
(Filter index, Frequency center, Band width, Filter type, Gain base, Gain),
(Filter index, Frequency center, Band width, Filter type, Gain base, Gain),
(Filter index, Frequency center, Band width, Filter type, Gain base, Gain)

## Slide 123: CONTROL INTERFACE
Equalizer Control: Elements order of control for Graphic Equalizer
Eqz_type, (Filter index, Graphic gain), (Filter index, Graphic gain), (Filter index, Graphic gain), (Filter index, Graphic gain), (Filter index, Graphic gain)

## Slide 124: CONTROL INTERFACE
Equalizer Control callbacks:
snd_adsp_control_eqz_info
Implementation in source code:
int snd_adsp_control_equalizer_info(struct snd_kcontrol *kcontrol, struct snd_ctl_elem_info *uinfo)
{
  ….
  uinfo->type = SNDRV_CTL_ELEM_TYPE_INTEGER;
  uinfo->count = 55;
  uinfo->value.integer.min = -1;
  uinfo->value.integer.max = 0xffffffff;
  ….
}
snd_adsp_control_eqz_info |  | 
Synopsis | Get detailed info on the equalizer control. | 
Syntax | int snd_adsp_control_eqz_info(struct snd_kcontrol *kcontrol, struct snd_ctl_elem_info *uinfo) | 
Parameter | struct snd_kcontrol *kcontrol | Pointer to control instance
 | struct snd_ctl_elem_info *uinfo | Pointer to info structure of the equalizer control
Return value | 0 | Always return 0

## Slide 125: CONTROL INTERFACE
snd_adsp_control_eqz_get
snd_adsp_control_eqz_get |  | 
Synopsis | Get parameters info of equalizer control in playback, capture cases | 
Syntax | static int snd_adsp_control_eqz_get(struct snd_kcontrol *kcontrol, struct snd_ctl_elem_value *ucontrol) | 
Parameter | struct snd_kcontrol *kcontrol | Pointer to control instance
 | struct snd_ctl_elem_value *ucontrol | Pointer to equalizer parameters.
Return value | 0 | Success
 | -EINVAL | Can’t get parameter information from ADSP.

## Slide 126: CONTROL INTERFACE
snd_adsp_control_eqz_get
Start
direction = DIRECT_PLAYBACK/DIRECT_RECORD
Handle state of Equalizer of playback/capture
equalizer : Equalizer data of playback/capture
Call xf_adsp_equalizer_get_param(equalizer);
eqz_params = &equalizer->params
Parametric EQZ?
Is Renderer/Capture Plugin running?
Indentify control type(playback/capture)
Yes
Error?
Return -EINVAL
No
Yes
Get Equalier type:
ucontrol->value.integer.value[0] = eqz_params->eqz_type;
filter_index = 1
A
B
End
Yes
No
No
eqz_param = &ctr_if->eqz_params[direction][index]

## Slide 127: CONTROL INTERFACE
snd_adsp_control_eqz_get
A
Get parameters (filter index, frequency centre, bandwidth, filter type, gain base, gain)’ values to appropriate parameters of ucontrol
End
Yes
i < 8
i = i + 1
filter_index++
No
i = 0
B
Get parameters (filter index, graphic gain)’ values to appropriate parameters of ucontrol. Assign -1 to the rest parameters of ucontrol
Yes
i < 5
i = i + 1
filter_index++
No
i = 0

## Slide 128: CONTROL INTERFACE
snd_adsp_control_eqz_put
snd_adsp_control_eqz_put |  | 
Synopsis | Set equalizer parameter in playback, capture cases | 
Syntax | static int snd_adsp_control_eqz_put(struct snd_kcontrol *kcontrol, struct snd_ctl_elem_value *ucontrol) | 
Parameter | struct snd_kcontrol *kcontrol | Pointer to control instance
 | struct snd_ctl_elem_value *ucontrol | Pointer to equalizer parameters
Return value | 1 | Hardware parameter is changed.
 | -EINVAL | Can’t set parameter to ADSP.

## Slide 129: CONTROL INTERFACE
snd_adsp_control_eqz_put
Start
direction = DIRECT_PLAYBACK/DIRECT_RECORD
Handle state of Equalizer of playback/capture
End
Indentify control type(playback/capture)
Yes
Yes
Is Renderer/Capture plugin running?
eqz_params->eqz_type = ucontrol->value.integer.value[0];
i = 1;
Return 1 means that Equalizer parameters are set
Return –EINVAL
eqz_type == EQZ_PARAMETRIC
while (i < (5 * 2 + 1))
{ filter_idx = ucontrol->value.integer.value[i++];
if((1 <= filter_idx) && (filter_idx <= 5)) {
eqz_params->g_coef.gain_g[filter_idx - 1] = ucontrol->value.integer.value[i++];
}
else if ((filter_idx == -1) || (filter_idx == 0)) {
i += 1;
}
else {
return -EINVAL;
}
}
while (i < 55) {
filter_idx = ucontrol->value.integer.value[i++];
if((1 <= filter_idx) && (filter_idx <= 9)) {
  eqz_params->p_coef.fc[filter_idx - 1] = ucontrol->value.integer.value[i++];
  eqz_params->p_coef.band_width[filter_idx -1] = ucontrol->value.integer.value[i++];
  eqz_params->p_coef.type[filter_idx -1] = ucontrol->value.integer.value[i++];
  eqz_params->p_coef.gain_base[filter_idx - 1] = ucontrol->value.integer.value[i++];
  eqz_params->p_coef.gain[filter_idx - 1] = ucontrol->value.integer.value[i++]; }
else if ((n == -1) || (n == 0)) {
snd_printk("n = %d\n", n);
i += 5;}
else{
return -EINVAL;}
}
No
No
eqz_type == EQZ_GRAPHIC
Yes
No

## Slide 130: CONTROL INTERFACE
Renderer Output Channel Control: setting and getting Renderer output channel’s value
struct snd_kcontrol_new snd_adsp_playback_out_channel_control[MAX_DAI_IDX - 1]. n-th element is assigned as below (n = 0, 1, 2, 3):
snd_adsp_playback_out_channel_control[n] =
{
.iface = SNDRV_CTL_ELEM_IFACE_MIXER,
.index = RDR_DAI_IDXn,
.name = "PlaybackOutChannel",
.info = &snd_adsp_control_rdr_out_channel_info,
.get = &snd_adsp_control_rdr_out_channel_get,
.put = &snd_adsp_control_rdr_out_channel_put
}
[Note]: struct snd_kcontrol_new is referred to https://elixir.bootlin.com/linux/v4.0/source/include/sound/control.h#L44
SNDRV_CTL_ELEM_IFACE_MIXER is refered to https://elixir.bootlin.com/linux/latest/source/include/uapi/sound/asound.h#L851

## Slide 131: CONTROL INTERFACE
Renderer Output Channel Control:
snd_adsp_control_rdr_out_channel_info
snd_adsp_control_rdr_out_channel_get
snd_adsp_control_rdr_out_channel_put

## Slide 132: CONTROL INTERFACE
Renderer Output Channel Control:
snd_adsp_control_rdr_out_channel_info
Element Information | Description
uinfo->type | The type field specifies the type of the control. There are BOOLEAN, INTEGER, ENUMERATED, BYTES, IEC958 and INTEGER64. Volume control use INTEGER type
uinfo->count | count field specifies the number of elements in this control. One output channel => count = 1
uinfo->value.integer.min | 1 means mono
uinfo->value.integer.max | 2 means stereo
Implementation in source code:
int snd_adsp_control_rdr_out_channel_info(struct snd_kcontrol *kcontrol, struct snd_ctl_elem_info *uinfo)
{
  ….
  uinfo->type = SNDRV_CTL_ELEM_TYPE_INTEGER;
  uinfo->count = 1;
  uinfo->value.integer.min = 1;
  uinfo->value.integer.max = 2;
  ….
}
snd_adsp_control_rdr_out_channel_info |  | 
Synopsis | Get detailed info of Renderer output channel control in playback case | 
Syntax | static int snd_adsp_control_rdr_out_channel_info(struct snd_kcontrol *kcontrol, struct snd_ctl_elem_info *uinfo) | 
Parameter | struct snd_kcontrol *kcontrol | Pointer to control instance
 | struct snd_ctl_elem_info *uinfo | Pointer to info structure of Renderer output channel
Return value | 0 | Always return 0

## Slide 133: CONTROL INTERFACE
Renderer Output Channel Control:
snd_adsp_control_rdr_out_channel_get
snd_adsp_control_rdr_out_channel_get |  | 
Synopsis | Get value of Renderer output channel in playback case | 
Syntax | static int snd_adsp_control_rdr_out_channel_get(struct snd_kcontrol *kcontrol, struct snd_ctl_elem_value *ucontrol) | 
Parameter | struct snd_kcontrol *kcontrol | Pointer to control instance
 | struct snd_ctl_elem_value *ucontrol | Pointer to Renderer output channel value
Return value | 0 | Success
 | -EINVAL | Can’t get value of output channel from Renderer plugin

## Slide 134
snd_adsp_control_rdr_out_channel_get
Start
Handle state = renderer state
Command idx = Renderer output channel setting subcommand for renderer
DAI index = RDR_DAI_IDXn (n = 0, 1, 2, 3) (got from kcontrol->id.index)
Handle ID = Renderer ID
Call xf_adsp_get_param(Handle ID, Command idx, &rdr_out_ch) to get Renderer output channel to rdr_out_ch
ucontrol->value.integer.value[0] = rdr_out_ch
Is Renderer Plugin running?
Get information from control structure stored in ADSP ALSA driver.
ucontrol->value.integer.value[0] = ctr_if->rdr_out_ch[DAI index]
[Note] The control interface structure holds the value of Renderer output channel set by an Audio app and that value will be set to Renderer plugin.
No
Yes
End
error?
Return -EINVAL
Yes
No

## Slide 135: CONTROL INTERFACE
Renderer Output Channel Control:
snd_adsp_control_rdr_out_channel_put
snd_adsp_control_rdr_out_channel_put |  | 
Synopsis | Set Renderer output channel in playback case | 
Syntax | static int snd_adsp_control_rdr_out_channel_put(struct snd_kcontrol *kcontrol, struct snd_ctl_elem_value *ucontrol) | 
Parameter | struct snd_kcontrol *kcontrol | Pointer to control instance
 | struct snd_ctl_elem_value *ucontrol | Pointer to Renderer output channel value
Return value | 1 | Parameter after setting is changed.
 | -EINVAL | Cannot set output channel for Renderer

## Slide 136
snd_adsp_control_rdr_out_channel_put
Start
Handle state = renderer state
DAI index = RDR_DAI_IDXn (n = 0, 1, 2, 3) (got from kcontrol->id.index)
Is Renderer Plugin running?
Store volume value into the control structure.
ctr_if->rdr_out_ch[DAI index] = ucontrol->value.integer.value[0] and return 1
[Note] When Renderer plugin runs after, it will set output channel with value stored in the control structure
No
Yes
End
Return -EINVAL

## Slide 137: ERROR CODE
Error code | Description | Reference
EINVAL | Invalid argument or some functions get failed | https://elixir.free-electrons.com/linux/v4.0/source/include/uapi/asm-generic/errno-base.h
ENOMEM | Cannot allocate memory for the soundcard | 
ENODEV | Invalid driver data in the platform device | 
Below table shows error types and corresponding value of callback functions in ALSA Interface

## Slide 138: REVISION HISTORY
Revision History | ADSP ALSA Driver
Rev. | Date | Description | 
 |  | Page | Summary
1.00 | 29/11/2017 | - | First Edition issued.
2.00 | 21/06/2018 | 22 to 58 | Support ASoC
3.00 | 13/08/2018 | - | Add TDM/CTU/MIX feature
4.00 | 27/08/2018 | - | Add CTU/MIX feature