## Slide 1
Detail design
For
ADSP Driver EXTENSION
november, 2017
Audio DSP project

## Slide 2
REVISION HISTORY
Rev. | Date | Description |  | Approved by | Created by
 |  | Page | Summary |  | 
1.00 | 29/11/2017 | - | First Edition issued. | Nguyen Nguyen | Tien Tran
2.00 | 21/06/2018 | - | Support ASoC | Vu Phan | Nguyen Dang
3.00 | 13/08/2018 | 41 to 50 | Add TDM feature | Vu Phan | Nguyen Dang

## Slide 3
APPENDIX
Overview
ADSP Base
  Introduction
  Base Control
  Internal Controls
    Handle Control
    Message Control
    Response Thread
    Other APIs
Proxy Driver Interface - Extension Interface

## Slide 4
APPENDIX
Overview
ADSP Base
  Introduction
  Base Control
  Internal Controls
    Handle Control
    Message Control
    Response Thread
    Other APIs
Proxy Driver Interface - Extension Interface

## Slide 5: I. Overview
This figure shows the basic configuration of ADSP driver and the connection with the ALSA framework when performs playback and record to ADSP device.

## Slide 6: I. Overview
Audio applications (aplay, arecord, amixer, etc):
The user applications that support to play or record sound by using ALSA library.
ALSA Lib:
The ALSA library APIs are the interface to the ALSA drivers.
ALSA Middle Layer:
It is a set of libraries which APIs gives applications access to the sound card drivers. And it can be broken down into the major interfaces such as control interface, PCM interface, raw MIDI interface, timer interface, sequencer interface and mixer interface.
ALSA SoC core:
It is part of ALSA Framework and does processing of PCM data
ADSP ALSA:
It is an ALSA device driver, implements to register a sound card for ADSP device. It provides callback functions for the native supports from ALSA framework to perform both playback and record. For playback/TDM playback, it receives PCM data from user app and transfers to ADSP Renderer plugin/ADSP TDM Renderer plugin. For record, it receives PCM data from ADSP Capture plugin/ADSP TDM Capture plugin and transfers to user app. The equalization function can be integrated into playback and record by routing between Equalizer and Renderer plugin, and between Equalizer and Capture plugins.
CPU DAI:
DAI stands for Digital Audio Interface. CPU DAI is the interface for the platform driver to communicate with other drivers.
Platform driver:
This is used to register ADSP sound card into ASoC framework. It holds ADSP ALSA driver, ADSP Driver Extension and ADSP sound card.

## Slide 7: I. Overview
Codec driver:
It represents interface for codecs.
Codec DAI:
The DAI for codecs to communicate with other drivers
Machine driver:
The ASoC machine (or board) driver is the code that glues together the platform driver and codec driver.
Proxy Extension Interface:
APIs of methods through which ADSP Driver Extension communicates with shared memory area in Hardware side.
Shared memory area:
Shared memory is a memory area which can be read and written by both CPU and ADSP.
ADSP:
It is an audio DSP hardware unit. It provides ADSP framework which has the capability to control and execute multiple plugins (Renderer/Capture/Equalizer/TDM Renderer/TDM Capture) for playback, record, TDM and equalization. The communication between ADSP side and CPU side is performed by the interrupt, and the shared memory area.

## Slide 8
APPENDIX
Overview
ADSP Base
  Introduction
  Base Control
  Internal Controls
    Handle Control
    Message Control
    Response Thread
    Other APIs
Proxy Driver Interface - Extension Interface

## Slide 9: INTRODUCTION
This slide shows the simple detail architecture of ADSP base
The red square includes the main blocks of ADSP base.
Base control is all the global APIs for ADSP ALSA driver usage. It controls ADSP ALSA components and other commands from ADSP ALSA driver.
Handle control responds to control the handle data which ASDP ALSA components have registered to.
Message control responds to control the sending and receiving message to and from ADSP.
Response thread is created in the ADSP base’s initialization. This thread sleeps, waits, and gets the response messages from ADSP independently.
Beside these blocks, ADSP base also has some other APIs to support the control operation.
[Note] Due to maximum of 256 components that can be registered, n = 256
Handle
Control
ADSP Base
Response thread
ADSP ALSA Driver
Proxy driver
Handle #1
Handle #2
Proxy Extension Interface
Component 2
Component n
Message Control
Client data
Response message queue
Command message queue
Proxy data
ADSP Driver
Base Control
Component 1
Handle #n
…
…

## Slide 10: INTRODUCTION
This slide shows the simple detail architecture of ADSP base
(1)
ADSP base initialization
When ADSP driver is going to initialization, it initializes proxy driver. Proxy data with the command message queue inside are also initialized.
In this initialization stage, proxy driver initializes ADSP base also(1). Then, ADSP base creates a response thread to receive the response messages independently. To support the reception of message from ADSP, ADSP base sends a command (2) to proxy driver to allocate a client data (3) and initializes a response message queue.
Proxy driver
Proxy Extension Interface
Client data
Response message queue
Command message queue
Proxy data
ADSP Driver
(3)
Handle
Control
ADSP Base
Response thread
ADSP ALSA Driver
Message Control
Base Control
(2)
Handle #1
Handle #2
Component 2
Component n
Component 1
Handle #n
…
…

## Slide 11: INTRODUCTION
This slide shows the simple detail architecture of ADSP base
Proxy driver
Proxy Extension Interface
(5)
(6)
Client data
Response message queue
Command message queue
Proxy data
(10)
ADSP Driver
(7)
(8)
(9)
ADSP ALSA component initialization
After ADSP base was created successfully, ADSP ALSA driver can create component (4) (5) (6) for playback or record or TDM playback or TDM record or equalizer purpose.
Each component (Capture/Equalizer/Renderer) registers (8) a corresponding ADSP plugin by sending a message (9) to proxy’s command queue (10). This message then will be sent to ADSP framework by proxy process.
Handle
Control
ADSP Base
Response thread
ADSP ALSA Driver
Message Control
Base Control
(4)
Handle #1
Handle #2
Component 2
Component n
Component 1
Handle #n
…
…

## Slide 12: INTRODUCTION
Base Control
Handle
Control
This slide shows the simple detail architecture of ADSP base
Proxy driver
Proxy Extension Interface
Client data
Response message queue
Command message queue
Proxy data
ADSP Driver
(13)
(5’)
(11)
(12)
(14)
(15)
ADSP ALSA component initialization
To get the register results, the response thread independently waits for the valid message in the response message queue (11).
If the message in the response message queue is valid, response thread gets it from (12) (13) (14) response message queue corresponding to the registered client, and returns to base control (15).
If the plugin register is success. The component will register a handle data (4’) (5’) (6’) (7’) to store its operation information.
Each handle has a ID corresponding to the order of creation command from ADSP ALSA driver.
Handle
Control
ADSP Base
Response thread
ADSP ALSA Driver
Message Control
(4’)
(6’)
(7’)
Handle #1
Handle #2
Component 2
Component n
Component 1
Handle #n
…
…

## Slide 13: INTRODUCTION
ADSP Base
This slide shows the simple detail architecture of ADSP base
ADSP ALSA Driver
Proxy driver
Proxy Extension Interface
Message Control
Client data
Response message queue
Command message queue
Proxy data
ADSP Driver
(19)
(17)
(20)
ADSP ALSA component execution
When a ADSP ALSA component sends (16) a command message to ADSP.
Firstly, base control gets the handle ID (17) of that component, and set the ID to command message’s ID. After that, this message is sent to command message queue (18) (19) (20) of proxy driver for the transfer process to ADSP.
(16)
(18)
Base Control
Handle
Control
Response thread
Handle #1
Handle #2
Component 2
Component n
Component 1
Handle #n
…
…

## Slide 14: INTRODUCTION
ADSP Base
This slide shows the simple detail architecture of ADSP base
ADSP ALSA Driver
Proxy driver
Proxy Extension Interface
Message Control
Client data
Response message queue
Command message queue
Proxy data
ADSP Driver
(23)
(21)
(22)
(24)
ADSP ALSA component execution
To get the response message, the response thread independently waits for the valid message in the response message queue (21).
If the message in the response message queue is valid, response thread gets it from (22) (23) (24) response message queue corresponding to the registered client.
To know which component the received message belong to, the response thread extracts the handle ID from response message’s ID, and gets the registered handle data (25) correspondingly.
If the handle data is valid, the callback function in this data will be called (26) for the specific operation from ADSP ALSA driver.
After completing the callback, response thread continues to wait (21) for the next response message from client’s message queue.
(26)
(25)
Base Control
Handle
Control
Response thread
Handle #1
Handle #2
Component 2
Component n
Component 1
Handle #n
…
…

## Slide 15: INTRODUCTION
ADSP Base
This slide shows the simple detail architecture of ADSP base
ADSP ALSA Driver
Proxy driver
Proxy Extension Interface
Message Control
Client data
Response message queue
Command message queue
Proxy data
ADSP Driver
Base Control
ADSP ALSA component de-initialization
When a ADSP ALSA driver want to terminate the playback or record function. The corresponding component will be destroyed.
It sends a destruction command (27) to ADSP base. ADSP base checks the handle data (28), and sends an unregister command to ADSP (29) (30) (31).
(30)
(28)
(31)
(27)
(29)
Handle
Control
Response thread
Handle #1
Handle #2
Component 2
Component n
Component 1
Handle #n
…
…

## Slide 16: INTRODUCTION
This slide shows the simple detail architecture of ADSP base
ADSP base de-initialization
ADSP base is destroyed when ADSP driver is removed from kernel.
In the proxy driver’s de-initialization, it calls a destruction command (32) to ADSP base. ADSP base starts to release the response thread, all the allocated resources, and unregisters client to proxy (33) (34).
(32)
Proxy driver
Proxy Extension Interface
Client data
Response message queue
Command message queue
Proxy data
ADSP Driver
(34)
Handle
Control
ADSP Base
Response thread
ADSP ALSA Driver
Message Control
Base Control
(33)
Handle #1
Handle #2
Component 2
Component n
Component 1
Handle #n
…
…

## Slide 17: INTRODUCTION
APIs for base control
xf_adsp_base_create
xf_adsp_base_destroy
xf_adsp_empty_this_buffer
xf_adsp_fill_this_buffer
xf_adsp_allocate_mem_pool
xf_adsp_free_mem_pool
xf_adsp_get_data_from_pool
xf_adsp_set_param
xf_adsp_get_param
xf_adsp_route
xf_adsp_renderer_create
xf_adsp_renderer_destroy
xf_adsp_renderer_set_params
xf_adsp_renderer_get_params
xf_adsp_capture_create
xf_adsp_capture_destroy
xf_adsp_capture_set_params
xf_adsp_capture_get_params
xf_adsp_equalizer_create
xf_adsp_equalizer_destroy
xf_adsp_equalizer_set_params
xf_adsp_equalizer_get_params
xf_adsp_tdm_renderer_create
xf_adsp_tdm_renderer_destroy
xf_adsp_tdm_renderer_set_params
xf_adsp_tdm_renderer_get_params
xf_adsp_tdm_capture_create
xf_adsp_tdm_capture_destroy
xf_adsp_tdm_capture_set_params
xf_adsp_tdm_capture_get_params
These above APIs are defined in the ADSP Driver Extension Function Design

## Slide 18: INTRODUCTION
APIs for handle control
xf_adsp_base_init_handle
xf_adsp_base_get_valid_handle
xf_adsp_base_register_handle
xf_adsp_base_get_handle
xf_adsp_base_free_handle
APIs for message control.
xf_send
xf_receive
xf_send_and_receive
Response thread
xf_response_thread
Other APIs
xf_adsp_register
xf_adsp_unregister
These above APIs are internal APIs.

## Slide 19
APPENDIX
Overview
ADSP Base
  Introduction
  Base Control
  Internal Controls
    Handle Control
    Message Control
    Response Thread
    Other APIs
Proxy Driver Interface - Extension Interface

## Slide 20: Base control
xf_adsp_base_create()
Begin job
Return
-ENOMEM
Allocate memory for base instance with size of struct xf_adsp_base in the kernel space using kmalloc()
Register client to proxy driver:
base->cmd.client_register(&base->client)
Allocate base successfully?
F
T
Base instance is NULL
Return
-EINVAL
F
T
Synopsis | This API creates and initializes ADSP base data that ADSP ALSA driver can use to control ADSP plugins (Renderer/Capture/Equalizer/TDM Capture/TDM Renderer). | 
Syntax | int xf_adsp_base_create(struct xf_adsp_base_cmd *cmd) | 
Parameter | struct xf_adsp_base_cmd *cmd | Pointer to struct of commands for extension interface
Return value | 0 | ADSP base is registered successfully
 | -EINVAL | ADSP base has been alive. Parameter cmd is invalid.
 | -ENOMEM | Cannot allocate memory for ADSP base usage.
 | -EBUSY | ADSP base cannot register to proxy driver due to number of client has been exceeded.
cmd is not NULL or any cmd’s member is not NULL
T
F
Return
-EINVAL
A
End job

## Slide 21: Base control
xf_adsp_base_create()
A
End job
No error returned?
T
F
Initialize waiting queue:
init_waitqueue_head(&base->base_wait)
Initialize handle data: xf_adsp_base_init_handle()
Register and start a thread for the response message from ADSP and with kthread_run()
Free base instance using kfree
base = NULL
Valid kthread data?
Register aux_pool data for the component usage by calling xf_adsp_allocate_mem_pool()
T
F
Valid aux_pool?
T
Cancel the response threat by setting wait_flag to 1 and calling kthread_stop()
Unregister proxy client:
base->cmd.client_unregister(&base->client)
F

## Slide 22: Base control
xf_adsp_base_destroy()
Begin job
Free aux_pool by calling xf_adsp_free_mem_pool()
Cancel the response threat by setting wait_flag to 1 and calling kthread_stop()
End job
Valid base instance?
Return
-EINVAL
Unregister proxy client:
base->cmd.client_unregister()
F
T
Free the allocated base instance using kfree
base = NULL
Synopsis | This API frees all resources that ADSP base has registered. | 
Syntax | int xf_adsp_base_destroy (void) | 
Parameter | - | -
Return value | 0 | ADSP base destroy successful.
 | -EINVAL | ADSP base has not registered yet.

## Slide 23: Base control
xf_adsp_empty_this_buffer()
Begin job
Get handle data based on the given hande_id by calling xf_adsp_base_get_handle()
End job
Valid base instance?
Return
-EINVAL
F
T
Create a msg with opcode XF_EMPTY_THIS_BUFFER and the given buffer size and buffer pointer
Valid handle?
Return
-EINVAL
F
T
Send the created msg to proxy driver by calling xf_send()
Synopsis | This API sends a XF_EMPTY_THIS_BUFFER command to ADSP framework. | 
Syntax | int xf_adsp_empty_this_buffer(int handle_id, char *buffer, int length) | 
Parameter | int handle_id | Handle id that registered in ADSP base
 | char *buffer | Pointer to PCM buffer
 | int length | Size of buffer in byte
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet, or the handle id has not registered to ADSP base yet.

## Slide 24: Base control
xf_adsp_fill_this_buffer()
Begin job
Get handle data based on the given hande_id by calling xf_adsp_base_get_handle()
End job
Valid base instance?
Return
-EINVAL
F
T
Create a msg with opcode XF_FILL_THIS_BUFFER and the given buffer size and buffer pointer
Valid handle?
Return
-EINVAL
F
T
Send the created msg to proxy driver by calling xf_send()
Synopsis | This API sends a XF_FILL_THIS_BUFFER command to ADSP framework. | 
Syntax | int xf_adsp_fill_this_buffer(int handle_id, char *buffer, int length) | 
Parameter | int handle_id | Handle id that registered in ADSP base
 | char *buffer | Pointer to PCM buffer
 | int length | Size of buffer in byte
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet, or the handle id has not registered to ADSP base yet.

## Slide 25: Base control
xf_adsp_allocate_mem_pool()
Begin job
Create a msg with opcode XF_ALLOC and the expected pool size
End job
Valid base instance?
Return
-EINVAL
F
T
Valid pool?
Return
-ENOMEM
F
T
Send the created msg to proxy driver and wait for the result by calling xf_send_and_receive()
No error returned?
Return -EINVAL
F
Allocate pool data to stored the registered buffer
Synopsis | This API sends a XF_ALLOC to ADSP to request a memory pool with desired pool size and buffer length. | 
Syntax | struct xf_pool *xf_adsp_allocate_mem_pool(int pool_size, int buf_length) | 
Parameter | int pool_size | Number of buffer need to allocate from ADSP
 | int buf_length | Size of buffer need to allocate from ADSP
Return value | Pointer | Pointer to registered memory pool
 | -EINVAL | ADSP base has not registered yet.
 | -ENOMEM | Cannot allocate memory for pool
A
Return pool allocated

## Slide 26: Base control
xf_adsp_allocate_mem_pool()
End
pool->length = buf_length
pool->number = pool_size
pool->p = msg.buffer
number = pool->size
i = 0
data = &pool->p[0]
A
pool->free = &pool->buffer[0]
pool->buffer[i].address = data
number > 0
number == 1
pool->buffer[i].link.next = NULL
T
pool->buffer[i].link.next = &pool->buffer[i + 1]
i++
data += buf_length
number--
F
T
F

## Slide 27: Base control
xf_adsp_free_mem_pool()
Begin job
Create a msg with opcode XF_FREE and buffer size, buffer pointer
End job
Valid base instance and pool data?
Return
-EINVAL
F
T
Send the created msg to proxy driver and wait for the result by calling xf_send_and_receive()
Free pool data
xf_adsp_free_mem_pool |  | 
Synopsis | This API frees memory pool and sends a XF_FREE to ADSP to return the previous registered buffers. | 
Syntax | int xf_adsp_free_mem_pool(struct xf_pool *pool) | 
Parameter | struct xf_pool *pool | Pointer to allocated memory pool
Return value | 0 | Pool has been free successfully.
 | -EINVAL | ADSP base has not registered yet, or memory pool is invalid.

## Slide 28: Base control
xf_adsp_get_data_from_pool()
Begin job
End job
Valid pool data?
Return
-EINVAL
F
T
Get data buffer pointer from pool based on the index
Return the data buffer
index is valid?
F
T
Synopsis | This API gets a data buffer from pool, which registered before. | 
Syntax | char *xf_adsp_get_data_from_pool(struct xf_pool *pool, int index) | 
Parameter | struct xf_pool *pool | Pointer to allocated memory pool
 | int index | The index of buffer in pool
Return value | Pointer | Buffer address of pool
 | -EINVAL | Memory pool is invalid or, the index is over than number of buffer in pool.

## Slide 29: Base control
xf_adsp_set_param()
Begin job
Get handle data based on the given hande_id by calling xf_adsp_base_get_handle()
End job
Valid base instance?
Return
-EINVAL
F
T
Get a buffer from aux_pool to store the parameter information:
b = xf_buffer_get(base->aux_pool)
msg_params = xf_buffer_data(b)
Valid handle?
Return
-EINVAL
F
T
Create a message msg with opcode XF_SET_PARAM and msg->buffer = msg_params
msg_params->item[0].id = index
msg_params->item[0].value = value
Send the created msg to proxy driver and wait for the result:
err = xf_send_and_receive()
Return the buffer to the aux_pool
Synopsis | This API sets a single parameter to a registered plugin. | 
Syntax | int xf_adsp_set_param(int handle_id, int index, int value) | 
Parameter | int handle_id | Handle id that registered in ADSP base
 | int index | The sub-command index of the setting value
 | int value | The setting value
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet, or the handle id has not registered to ADSP base yet, or the setting command makes a fatal error from ADSP plugin.
Return err

## Slide 30: Base control
xf_adsp_get_param()
Begin job
Get handle data based on the given hande_id by calling xf_adsp_base_get_handle()
End job
Valid base instance and value pointer?
Return
-EINVAL
F
T
Get a buffer from aux_pool to store the parameter information
Valid handle?
Return
-EINVAL
F
T
Create a message with opcode XF_GET_PARAM and the buffer pointer
Set the sub-command index to given buffer
Send the created msg to proxy driver and wait for the result:
err = xf_send_and_receive()
Return the given buffer to aux_pool
No error returned?
Save the respond value
F
T
Synopsis | This API gets a single parameter to a registered plugin. | 
Syntax | int xf_adsp_get_param(int handle_id, int index, int *value) | 
Parameter | int handle_id | Handle id that registered in ADSP base
 | int index | The sub-command index of the getting value
 | int *value | Pointer of the stored getting value
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet, or the handle id has not registered to ADSP base yet, or the pointer of value is invalid, or the getting command makes a fatal error from ADSP plugin.
Return err

## Slide 31: Base control
xf_adsp_route()
Begin job
Get destination and source handle data (dst_handle/src_handle) based on the given dst_hande_id and src_handle_id by calling xf_adsp_base_get_handle()
End job
Valid base instance?
Return
-EINVAL
F
T
Get a buffer from aux_pool to store the routing information
Valid dst_handle and src_handle?
Return
-EINVAL
F
T
Create a message with opcode XF_ROUTE and the given buffer information
Set the routing information (buffer size, buffer count, destination id) to buffer
Send the created msg to proxy driver and wait for the result:
err = xf_send_and_receive()
Return the given buffer to aux_pool
Synopsis | This API sends a XF_ROUTE command to ADSP framework to register a tunnel for transfer data between two ADSP plugins. | 
Syntax | int xf_adsp_route(int src_handle_id, int dst_handle_id, int buf_cnt, int buf_size) | 
Parameter | int src_handle_id | Handle id of source component
 | int dst_handle_id | Handle id of destination component
 | int buf_cnt | Number of buffer that used for tunnel
 | int buf_size | Size of a buffer that used for tunnel
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet, or the src/dst handle id have not registered to ADSP base yet, or the tunnel request cannot complete from ADSP.
Return err

## Slide 32: Base control
xf_adsp_renderer_create()
Synopsis | This API initializes a Renderer instance, registers ADSP Renderer plugin. After Renderer has registered successful, the API registers a handler to ADSP base, and get a handle ID which represents for a new handler which has been registered completely. Finally, it initializes all parameters as default values with default values of ADSP Renderer plugin. | 
Syntax | int xf_adsp_renderer_create( struct xf_adsp_renderer **renderer, struct xf_callback_func *cb, void *private_data) | 
Parameter | struct xf_adsp_renderer **renderer | The pointer to store the created Renderer instance
 | struct xf_callback_func *cb | Pointer to the callback functions
 | void *private_data | Pointer to a private data that used as a parameter in callback functions
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet, or cannot register new handler to ADSP base, or cannot register Renderer plugin to ADSP, or cannot get default value from ADSP Renderer plugin.
 | -ENOMEM | Cannot allocate Renderer instance
Begin job
Allocate data for Renderer component:
rdr = kmalloc(sizeof(struct xf_adsp_renderer), GFP_KERNEL)
End job
Valid base instance?
Return
-EINVAL
F
T
Register ADSP Renderer plugin:
xf_adsp_register(“renderer”, &comp_id)
rdr != NULL
Return
-ENOMEM
F
T
A
Return err

## Slide 33: Base control
xf_adsp_renderer_create()
A
End job
Register handler for this component into ADSP base:
rdr->handle_id = xf_adsp_base_register_handle(private_data, cb, comp_id)
Get the default parameters of plugin:
err = xf_adsp_renderer_get_params()
The returned handle id > 0?
Free Renderer component’s data:
kfree(rdr)
No error returned?
T
T
F
F
Unregister ADSP Renderer plugin by calling xf_adsp_unregister()
err = -EINVAL
err != 0
F
T
*renderer = rdr

## Slide 34: Base control
xf_adsp_renderer_destroy()
Begin job
Get handle data based on the component’s hande_id by calling xf_adsp_base_get_handle()
Valid base instance and Renderer’s data?
Return
-EINVAL
F
T
Unregister ADSP Renderer plugin by calling xf_adsp_unregister()
Valid handle?
F
T
Synopsis | This API unregisters ADSP Renderer plugin, frees registered handler and instance. | 
Syntax | int xf_adsp_renderer_destroy(struct xf_adsp_renderer *renderer) | 
Parameter | struct xf_adsp_renderer *renderer | Pointer to Renderer instance
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet, or Renderer instance is invalid.
End job
Free Renderer component’s data
Free handle data by xf_adsp_base_free_handle()

## Slide 35: Base control
xf_adsp_renderer_set_params()
Begin job
Get handle data based on the given hande_id by calling xf_adsp_base_get_handle()
End job
Valid base instance or valid Renderer instance?
Return
-EINVAL
F
T
Get a buffer from aux_pool to store the parameter information
Valid handle?
Return
-EINVAL
F
T
Create a message with opcode XF_SET_PARAM and the given buffer information
Set all the sub-command index and the corresponding value in its params structure to the buffer
Send the created msg to proxy driver and wait for the result:
err = xf_send_and_receive()
Return the given buffer to aux_pool
Synopsis | This API sets all parameters for ADSP Renderer plugin based on the values in params structure of Renderer instance. | 
Syntax | int xf_adsp_renderer_set_params(struct xf_adsp_capture *renderer) | 
Parameter | struct xf_adsp_renderer *renderer | Pointer to Renderer instance
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet, or Renderer instance is invalid, or Renderer instance has not register to ADSP base yet, or the setting command make a fatal error from ADSP Renderer plugin.
err != 0
err = -EINVAL
Return err
F
T

## Slide 36: Base control
xf_adsp_renderer_get_params()
Begin job
Get handle data based on the given hande_id by calling xf_adsp_base_get_handle()
End job
Valid base instance or valid Renderer instance?
Return
-EINVAL
F
T
Get a buffer from aux_pool to store the parameter information
Valid handle?
Return
-EINVAL
F
T
Create a message with opcode XF_GET_PARAM and the buffer pointer
Set the sub-command indexes to given buffer
Send the created msg to proxy driver and wait for the result:
err = xf_send_and_receive()
Return the given buffer to aux_pool
err = 0?
Save the respond values to its params structure
F
T
Synopsis | This API gets all ADSP Renderer’s parameters and stores the returned values in params structure of Renderer instance. | 
Syntax | int xf_adsp_renderer_get_params(struct xf_adsp_renderer *renderer) | 
Parameter | struct xf_adsp_renderer *renderer | Pointer to Renderer instance
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet, or Renderer instance is invalid, or Renderer instance has not register to ADSP base yet, or the getting command make a fatal error from ADSP Renderer plugin.
err = -EINVAL
Return err

## Slide 37: Base control
xf_adsp_capture_create()
Synopsis | This API initializes a Capture instance, registers ADSP Capture plugin. After Capture has registered successful, the API registers a handler to ADSP base, and get a handle ID which represents for a new handler which has been registered completely. Finally, it initializes all parameters as default values with default values of ADSP Capture plugin. | 
Syntax | int xf_adsp_capture_create( struct xf_adsp_capture **capture, struct xf_callback_func *cb, void *private_data) | 
Parameter | struct xf_adsp_capture **capture | The pointer to store the created Capture instance
 | struct xf_callback_func *cb | Pointer to the callback functions
 | void *private_data | Pointer to a private data that used as a parameter in callback functions
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet or cannot register new handler to ADSP base, or cannot register Capture plugin to ADSP, or cannot get default values from ADSP Capture plugin.
 | -ENOMEM | Cannot allocate Capture instance
Begin job
Allocate data for Capture component:
cap = kmalloc(sizeof(struct xf_adsp_capture), GFP_KERNEL)
End job
Valid base instance?
Return
-EINVAL
F
T
Register ADSP Capture plugin:
xf_adsp_register(“capture”, &comp_id)
cap != NULL
Return
-ENOMEM
F
T
A
Return err

## Slide 38: Base control
xf_adsp_capture_create()
A
End job
Register handler for this component into ADSP base:
cap->handle_id = xf_adsp_base_register_handle(private_data, cb, comp_id)
Get the default parameters of plugin:
err = xf_adsp_capture_get_params()
The returned handle id > 0?
Free Capture component’s data:
kfree(cap)
No error returned?
T
T
F
F
Unregister ADSP Capture plugin by calling xf_adsp_unregister()
err = -EINVAL
err != 0
F
T
*capture = cap

## Slide 39: Base control
xf_adsp_capture_destroy()
Begin job
Get handle data based on the component’s hande_id by calling xf_adsp_base_get_handle()
Valid base instance and Capture’s data?
Return
-EINVAL
F
T
Unregister ADSP Capture plugin by calling xf_adsp_unregister()
Valid handle?
F
T
Synopsis | This API unregisters ADSP Capture plugin, frees registered handler and instance. | 
Syntax | int xf_adsp_capture_destroy(struct xf_adsp_capture *capture) | 
Parameter | struct xf_adsp_capture *capture | Pointer to Capture instance
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet, or Capture instance is invalid.
End job
Free Capture component’s data
Free handle data by xf_adsp_base_free_handle()

## Slide 40: Base control
xf_adsp_capture_set_params()
Begin job
Get handle data based on the given hande_id by calling xf_adsp_base_get_handle()
End job
Valid base instance or valid Capture instance?
Return
-EINVAL
F
T
Get a buffer from aux_pool to store the parameter information
Valid handle?
Return
-EINVAL
F
T
Create a message with opcode XF_SET_PARAM and the given buffer information
Set all the sub-command index and the corresponding value in its params structure to the buffer
Send the created msg to proxy driver and wait for the result:
err = xf_send_and_receive()
Return the given buffer to aux_pool
Synopsis | This API sets all parameters for ADSP Capture plugin based on the values in params structure of Capture instance. | 
Syntax | int xf_adsp_capture_set_params(struct xf_adsp_capture *capture) | 
Parameter | struct xf_adsp_capture *capture | Pointer to Capture instance
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet, or Capture instance is invalid, or Capture instance has not register to ADSP base yet, or the setting command make a fatal error from ADSP Capture plugin.
err != 0
err = -EINVAL
Return err
F
T

## Slide 41: Base control
xf_adsp_capture_get_params()
Begin job
Get handle data based on the given hande_id by calling xf_adsp_base_get_handle()
End job
Valid base instance or valid Capture instance?
Return
-EINVAL
F
T
Get a buffer from aux_pool to store the parameter information
Valid handle?
Return
-EINVAL
F
T
Create a message with opcode XF_GET_PARAM and the buffer pointer
Set the sub-command indexes to given buffer
Send the created msg to proxy driver and wait for the result:
err = xf_send_and_receive()
Return the given buffer to aux_pool
err = 0?
Save the respond values to its params structure
F
T
Synopsis | This API gets all ADSP Capture’s parameters and stores the returned values in params structure of Capture instance. | 
Syntax | int xf_adsp_capture_get_params(struct xf_adsp_capture *capture) | 
Parameter | struct xf_adsp_capture *capture | Pointer to Capture instance
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet, or Capture instance is invalid, or Capture instance has not register to ADSP base yet, or the getting command make a fatal error from ADSP Capture plugin.
err = -EINVAL
Return err

## Slide 42: Base control
xf_adsp_tdm_renderer_create()
Synopsis | This API initializes a TDM Renderer instance, registers ADSP TDM Renderer plugin. After TDM Renderer has been registered successfully, the API registers a handler to ADSP base, and gets a handle ID which represents for a new handler which has been registered completely. Finally, it initializes all parameters as default values with default values of TDM Renderer plugin. | 
Syntax | int xf_adsp_tdm_renderer_create( struct xf_adsp_tdm_renderer **tdm_renderer, struct xf_callback_func *cb, void *private_data) | 
Parameter | struct xf_adsp_tdm_renderer **tdm_renderer | The pointer to store the created TDM Renderer instance
 | struct xf_callback_func *cb | Pointer to the callback functions
 | void *private_data | Pointer to a private data that used as a parameter in callback functions
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet, or cannot register new handler to ADSP base, or cannot register TDM Renderer plugin to ADSP, or cannot get default values from ADSP TDM Renderer plugin.
 | -ENOMEM | Cannot allocate TDM Renderer instance
Begin job
Allocate data for TDM Renderer component:
tdm_rdr = kmalloc(sizeof(struct xf_adsp_tdm_renderer), GFP_KERNEL)
End job
Valid base instance?
Return
-EINVAL
F
T
Register ADSP TDM Renderer plugin:
xf_adsp_register(“tdm-renderer”, &comp_id)
tdm_rdr != NULL
Return
-ENOMEM
F
T
A
Return err

## Slide 43: Base control
xf_adsp_tdm_renderer_create()
A
End job
Register handler for this component into ADSP base:
tdm_rdr->handle_id = xf_adsp_base_register_handle(private_data, cb, comp_id)
Get the default parameters of plugin:
err = xf_adsp_tdm_renderer_get_params()
The returned handle id > 0?
Free TDM Renderer component’s data:
kfree(tdm_rdr)
No error returned?
T
T
F
F
Unregister ADSP TDM Renderer plugin by calling xf_adsp_unregister()
err = -EINVAL
err != 0
F
T
*tdm_renderer = tdm_rdr

## Slide 44: Base control
xf_adsp_tdm_renderer_destroy()
Begin job
Get handle data based on the component’s hande_id by calling xf_adsp_base_get_handle()
Valid base instance and TDM Renderer’s data?
Return
-EINVAL
F
T
Unregister ADSP TDM Renderer plugin: xf_adsp_unregister()
Valid handle?
F
T
Synopsis | This API unregisters ADSP TDM Renderer plugin, frees registered handler and instance. | 
Syntax | int xf_adsp_tdm_renderer_destroy(struct xf_adsp_tdm_renderer *tdm_renderer) | 
Parameter | struct xf_adsp_tdm_renderer *tdm_renderer | Pointer to TDM Renderer instance
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet, or TDM Renderer instance is invalid.
End job
Free TDM Renderer component’s data
Free handle data by xf_adsp_base_free_handle()

## Slide 45: Base control
xf_adsp_tdm_renderer_set_params()
Begin job
Get handle data based on the given hande_id by calling xf_adsp_base_get_handle()
End job
Valid base instance or valid TDM Renderer instance?
Return
-EINVAL
F
T
Get a buffer from aux_pool to store the parameter information
Valid handle?
Return
-EINVAL
F
T
Create a message with opcode XF_SET_PARAM and the given buffer information
Set all the sub-command index and the corresponding value in its params structure to the buffer
Send the created msg to proxy driver and wait for the result:
err = xf_send_and_receive()
Return the given buffer to aux_pool
Synopsis | This API sets all parameters for ADSP TDM Renderer plugin based on the values in params structure of TDM Renderer instance. | 
Syntax | int xf_adsp_tdm_renderer_set_params(struct xf_adsp_tdm_renderer *tdm_renderer) | 
Parameter | struct xf_adsp_tdm_renderer *tdm_renderer | Pointer to TDM Renderer instance
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet, or TDM Renderer instance is invalid, or TDM Renderer instance has not register to ADSP base yet, or the setting command make a fatal error from ADSP TDM Renderer plugin.
err != 0
err = -EINVAL
Return err
F
T

## Slide 46: Base control
xf_adsp_tdm_renderer_get_params()
Begin job
Get handle data based on the given hande_id by calling xf_adsp_base_get_handle()
End job
Valid base instance or valid TDM Renderer instance?
Return
-EINVAL
F
T
Get a buffer from aux_pool to store the parameter information
Valid handle?
Return
-EINVAL
F
T
Create a message with opcode XF_GET_PARAM and the buffer pointer
Set the sub-command indexes to given buffer
Send the created msg to proxy driver and wait for the result:
err = xf_send_and_receive()
Return the given buffer to aux_pool
err = 0?
Save the respond values to its params structure
F
T
Synopsis | This API gets all ADSP TDM Renderer’s parameters and stores the returned values in params structure of TDM Renderer instance. | 
Syntax | int xf_adsp_tdm_renderer_get_params(struct xf_adsp_tdm_renderer *tdm_renderer) | 
Parameter | struct xf_adsp_tdm_renderer *tdm_renderer | Pointer to TDM Renderer instance
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet, or TDM Renderer instance is invalid, or TDM Renderer instance has not register to ADSP base yet, or the getting command make a fatal error from ADSP TDM Renderer plugin.
err = -EINVAL
Return err

## Slide 47: Base control
xf_adsp_tdm_capture_create()
Synopsis | This API initializes a TDM Capture instance, registers ADSP TDM Capture plugin. After TDM Capture has been registered successfully, the API registers a handler to ADSP base, and get a handle ID which represents for a new handler has been registered completely. Finally, it initializes all parameters as default values with default values of the plugin. | 
Syntax | int xf_adsp_tdm_capture_create( struct xf_adsp_tdm_capture **tdm_capture, struct xf_callback_func *cb, void *private_data) | 
Parameter | struct xf_adsp_tdm_capture **tdm_capture | The pointer to store the created TDM Capture instance
 | struct xf_callback_func *cb | Pointer to the callback functions
 | void *private_data | Pointer to a private data that used as a parameter in callback functions
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet or cannot register new handler to ADSP base, or cannot register TDM Capture plugin to ADSP, or cannot get default values from ADSP TDM Capture plugin.
 | -ENOMEM | Cannot allocate TDM Capture instance
Begin job
Allocate data for TDM Capture component:
tdm_cap = kmalloc(sizeof(struct xf_adsp_tdm_capture), GFP_KERNEL)
End job
Valid base instance?
Return
-EINVAL
F
T
Register ADSP TDM Capture plugin:
xf_adsp_register(“tdm-capture”, &comp_id)
tdm_cap != NULL
Return
-ENOMEM
F
T
A
Return err

## Slide 48: Base control
xf_adsp_tdm_capture_create()
A
End job
Register handler for this component into ADSP base:
tdm_cap->handle_id = xf_adsp_base_register_handle(private_data, cb, comp_id)
Get the default parameters of plugin:
err = xf_adsp_tdm_capture_get_params()
The returned handle id > 0?
Free TDM Capture component’s data:
kfree(tdm_cap)
No error returned?
T
T
F
F
Unregister ADSP TDM Capture plugin: xf_adsp_unregister()
err = -EINVAL
err != 0
F
T
*tdm_capture = tdm_cap

## Slide 49: Base control
xf_adsp_tdm_capture_destroy()
Begin job
Get handle data based on the component’s hande_id by calling xf_adsp_base_get_handle()
End job
Valid base instance and TDM Capture’s data?
Return
-EINVAL
F
T
Unregister ADSP TDM Capture plugin by calling xf_adsp_unregister()
Valid handle?
F
T
Free TDM Capture component’s data
Synopsis | This API unregisters ADSP TDM Capture plugin, frees registered handler and instance. | 
Syntax | int xf_adsp_tdm_capture_destroy(struct xf_adsp_tdm_capture *tdm_capture) | 
Parameter | struct xf_adsp_tdm_capture *tdm_capture | Pointer to TDM Capture instance
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet, or TDM Capture instance is invalid.
Free handle data by xf_adsp_base_free_handle()

## Slide 50: Base control
xf_adsp_tdm_capture_set_params()
Begin job
Get handle data based on the given hande_id by calling xf_adsp_base_get_handle()
End job
Valid base instance or valid TDM Capture instance?
Return
-EINVAL
F
T
Get a buffer from aux_pool to store the parameter information
Valid handle?
Return
-EINVAL
F
T
Create a message with opcode XF_SET_PARAM and the given buffer information
Set all the sub-command index and the corresponding value in its params structure to the buffer
Send the created msg to proxy driver and wait for the result:
err = xf_send_and_receive()
Return the given buffer to aux_pool
Synopsis | This API sets all parameters for ADSP TDM Capture plugin based on the values in params structure of TDM Capture instance. | 
Syntax | int xf_adsp_tdm_capture_set_params(struct xf_adsp_tdm_capture *tdm_capture) | 
Parameter | struct xf_adsp_tdm_capture *tdm_capture | Pointer to TDM Capture instance
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet, or TDM Capture instance is invalid, or TDM Capture instance has not register to ADSP base yet, or the setting command make a fatal error from ADSP TDM Capture plugin.
err != 0
err = -EINVAL
Return err
F
T

## Slide 51: Base control
xf_adsp_tdm_capture_get_params()
Begin job
Get handle data based on the given hande_id by calling xf_adsp_base_get_handle()
End job
Valid base instance or valid TDM Capture instance?
Return
-EINVAL
F
T
Get a buffer from aux_pool to store the parameter information
Valid handle?
Return
-EINVAL
F
T
Create a message with opcode XF_GET_PARAM and the buffer pointer
Set the sub-command indexes to given buffer
Send the created msg to proxy driver and wait for the result:
err = xf_send_and_receive()
Return the given buffer to aux_pool
err = 0?
Save the respond values to its params structure
F
T
Synopsis | This API gets all ADSP TDM Capture’s parameters and stores the returned values in params structure of TDM Capture instance. | 
Syntax | int xf_adsp_tdm_capture_get_params(struct xf_adsp_tdm_capture *tdm_capture) | 
Parameter | struct xf_adsp_tdm_capture *tdm_capture | Pointer to TDM Capture instance
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet, or TDM Capture instance is invalid, or TDM Capture instance has not register to ADSP base yet, or the getting command make a fatal error from ADSP TDM Capture plugin.
err = -EINVAL
Return err

## Slide 52: Base control
xf_adsp_equalizer_create()
Synopsis | This API initializes a Equalizer instance, registers ADSP Equalizer plugin and initializes parameters as the default values from plugin. After Equalizer has created successful, it registers a handler to ADSP base, and get a handle id which presents for a new handler has been registered completely. | 
Syntax | int xf_adsp_equalizer_create( struct xf_adsp_equalizer **equalizer, struct xf_callback_func *cb, void *private_data) | 
Parameter | struct xf_adsp_equalizer **equalizer | The pointer to store the created Equalizer instance
 | struct xf_callback_func *cb | Pointer to the callback functions
 | void *private_data | Pointer to a private data that used as a parameter in callback functions
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet or cannot register new handler to ADSP base, or cannot register Equalizer plugin to ADSP, or cannot get default values from ADSP Equalizer plugin.
 | -ENOMEM | Cannot allocate Equalizer instance
Begin job
Allocate data for Equalizer component
End job
Valid base instance?
Return
-EINVAL
F
T
Register ADSP Equalizer plugin: xf_adsp_register()
The data is valid?
Return
-ENOMEM
F
T
Register handler for this component into ADSP base by calling xf_adsp_base_register_handle()
Get the default parameters of plugin by calling xf_adsp_equalizer_get_params()
The returned handle id > 0?
Free Equalizer component’s data
No error returned?
T
T
F
F
Unregister ADSP Equalizer plugin by calling xf_adsp_unregister()
No error returned?
err = -EINVAL
T
F

## Slide 53: Base control
xf_adsp_equalizer_destroy()
Begin job
Get handle data based on the component’s hande_id by calling xf_adsp_base_get_handle()
Valid base instance and Equalizer’s data?
Return
-EINVAL
F
T
Unregister ADSP Equalizer plugin by calling xf_adsp_unregister()
Valid handle?
F
T
Synopsis | This API unregisters ADSP Equalizer plugin, frees registered handler and instance. | 
Syntax | int xf_adsp_equalizer_destroy(struct xf_adsp_equalizer *equalizer) | 
Parameter | struct xf_adsp_equalizer *equalizer | Pointer to Equalizer instance
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet, or Equalizer instance is invalid.
End job
Free Equalizer component’s data
Free handle data by xf_adsp_base_free_handle()

## Slide 54: Base control
xf_adsp_equalizer_set_params()
Begin job
Get handle data based on the given hande_id by calling xf_adsp_base_get_handle()
End job
Valid base instance?
Return
-EINVAL
F
T
Get a buffer from aux_pool to store the parameter information
Valid handle?
Return
-EINVAL
F
T
Create a message with opcode XF_SET_PARAM and the given buffer information
Set all the sub-command index and the corresponding value in its params structure to the buffer
Send the created msg to proxy driver and wait for the result by calling xf_send_and_receive()
Return the given buffer to aux_pool
Synopsis | This API sets all parameters for ADSP Equalizer plugin based on the values in params structure of Equalizer instance. | 
Syntax | int xf_adsp_equalizer_set_params(struct xf_adsp_equalizer *equalizer) | 
Parameter | struct xf_adsp_equalizer *equalizer | Pointer to Equalizer instance
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet, or Equalizer instance is invalid, or Equalizer instance has not register to ADSP base yet, or the setting command makes a fatal error from ADSP Equalizer plugin.

## Slide 55: Base control
xf_adsp_equalizer_get_params()
Begin job
Get handle data based on the given hande_id by calling xf_adsp_base_get_handle()
End job
Valid base instance?
Return
-EINVAL
F
T
Get a buffer from aux_pool to store the parameter information
Valid handle?
Return
-EINVAL
F
T
Create a message with opcode XF_GET_PARAM and the buffer pointer
Set the sub-command indexes to given buffer
Send the created msg to proxy driver and wait for the result by calling xf_send_and_receive()
Return the given buffer to aux_pool
No error returned?
Save the respond values to its params structure
F
T
Synopsis | This API gets all ADSP Equalizer’s parameters and stores the returned values in params structure of Equalizer instance. | 
Syntax | int xf_adsp_equalizer_get_params(struct xf_adsp_equalizer *equalizer) | 
Parameter | struct xf_adsp_equalizer *equalizer | Pointer to Equalizer instance
Return value | 0 | Success
 | -EINVAL | ADSP base has not registered yet, or Equalizer instance is invalid, or Equalizer instance has not register to ADSP base yet, or the getting command make a fatal error from ADSP plugin.

## Slide 56
APPENDIX
Overview
ADSP Base
  Introduction
  Base Control
  Internal Controls
    Handle Control
    Message Control
    Response Thread
    Other APIs
Proxy Driver Interface - Extension Interface

## Slide 57: HANDLE Control
Begin job
End job
Set all the handle[i] to NULL
(i = 0 to 255)
xf_adsp_base_init_handle()
Synopsis | This API sets all the handles to NULL as the default value. | 
Syntax | static inline void xf_adsp_base_init_handle(void) | 
Parameter | - | -
Return value | - | -

## Slide 58: HANDLE Control
Begin job
End job
handle[i] == NULL?
(i = 0 to 255)
Return i value
xf_adsp_base_get_valid_handle()
Synopsis | This API returns a first available handle index for component’s register | 
Syntax | static inline int xf_adsp_base_get_valid_handle(void) | 
Parameter | - | -
Return value | -1 | Number of handle in ADSP base has exceeded.
 | Number from 0 to 255 | Valid handle index
Get the next handle data handle[i]
( i = 0 to 255)
F
T
i == 255?
F
Return -1
T

## Slide 59: HANDLE Control
Begin job
End job
Allocate memory for handle instance
The returned index (index) >= 0?
F
T
Return
-EINVAL
Handle instance is valid?
Return
-ENOMEM
F
T
Save the information of private_data, cb, and comp_id into handle instance
Get the next available handle by calling xf_adsp_base_get_valid_handle()
Return the handle ID for the registered handle in ADSP base
(return (index+1))
xf_adsp_base_register_handle()
Synopsis | This API responds to register a handle data for component’s register (Capture/Renderer/Equalizer). | 
Syntax | static int xf_adsp_base_register_handle (void *private_data, struct xf_callback_func *cb, int comp_id) | 
Parameter | void *private_data | Private data which component has registered in ADSP base
 | struct xf_callback_func *cb | Callback function which component has registered in ADSP base
 | int comp_id | Component ID, which returned after registered a ADSP plugin
Return value | -EINVAL | Number of handle in ADSP base has exceeded.
 | -ENOMEM | Cannot allocate memory for handle usage
 | Handle ID (1 to 256) | Register handle successfully

## Slide 60: HANDLE Control
Begin job
End job
Return handle[handle_id - 1]
xf_adsp_base_get_handle()
Synopsis | This API returns the handle instance from the handle id. | 
Syntax | static inline struct xf_handle *xf_adsp_base_get_handle(int handle_id) | 
Parameter | int handle_id | The ID which component has registered into ADSP base
Return value | Pointer | The handle instance corresponding to handle ID

## Slide 61: HANDLE Control
Begin job
End job
Free handle[handle_id - 1]
Set handle[handle_id - 1] to NULL
Valid handle_id?
F
Return
-EINVAL
T
xf_adsp_base_free_handle()
Synopsis | This API releases the registered handle instance | 
Syntax | static int xf_adsp_base_free_handle(int handle_id) | 
Parameter | int handle_id | The ID which component has registered into ADSP base
Return value | -EINVAL | Invalid handle ID
 | 0 | Release handle instance successful

## Slide 62
APPENDIX
Overview
ADSP Base
  Introduction
  Base Control
  Internal Controls
    Handle Control
    Message Control
    Response Thread
    Other APIs
Proxy Driver Interface - Extension Interface

## Slide 63: Message Control
Begin job
End job
Return the function xf_adsp_base_send()
xf_send()
Synopsis | This API sends a command message to proxy driver, which will be transferred to ADSP through proxy process. | 
Syntax | static inline int xf_send(struct xf_message *msg) | 
Parameter | struct xf_message *msg | Message buffer which want to be sent
Return value | 0 | Success
 | -EINVAL | Client data is invalid, or it has not registered to proxy driver yet.

## Slide 64: Message Control
Begin job
End job
Return the function xf_adsp_base_recv()
xf_receive()
Synopsis | This API gets the response message from client message queue, which has been gotten by proxy process. | 
Syntax | static inline int xf_receive(struct xf_message *msg) | 
Parameter | struct xf_message *msg | Message buffer which stored the response message data
Return value | 0 | Success
 | -EINVAL | Client data is invalid, or it has not registered to proxy driver yet, or the response message is invalid

## Slide 65: Message Control
Begin job
End job
Send the message to proxy by calling xf_adsp_base_send()
No error returned?
Return -EINVAL
F
T
Sleep and wait for the wake up from response thread by calling wait_event_interruptible()
Set base_flag to zero for the waiting from response thread
Copy base_msg to the input message buffer
No error returned?
Return
-EINVAL
F
T
The response message’s opcode is difference from command message’s opcode
Return
-EINVAL
F
T
xf_send_and_receive()
Synopsis | This API sends a command message to proxy driver (which will be transferred to ADSP through proxy process), and waits for the response message by the wake up signal from response thread. | 
Syntax | static int xf_send_and_receive(struct xf_message *msg) | 
Parameter | struct xf_message *msg | Message buffer which stored the response message data
Return value | 0 | Success
 | -EINVAL | Client data is invalid, or it has not registered to proxy driver yet, or the response message is invalid, or the message caused an fatal error from ADSP

## Slide 66
APPENDIX
Overview
ADSP Base
  Introduction
  Base Control
  Internal Controls
    Handle Control
    Message Control
    Response Thread
    Other APIs
Proxy Driver Interface - Extension Interface

## Slide 67: Response Thread
Begin job
End job
Waiting for the valid message in client queue or the condition (wait_flag) is set by calling xf_adsp_base_poll()
kthread_should_stop() == 0?
F
T
Have a valid message?
Receive the message from client queue by calling xf_receive()
Get the client ID (id) from received message ID by macro XF_AP_CLIENT()
id ≠ 0?
Get the handle instance from the given ID
Valid handle?
Message opcode == XF_EMPTY_THIS_BUFFER
Message opcode == XF_FILL_THIS_BUFFER
Message opcode == XF_SET_PARAM | XF_GET_PARAM |
XF_ROUTE | XF_UNROUTE
Copy the received message to base_msg
Set base_flag to one
Wake up the base_wait by calling wake_up()
F
F
T
T
Exit the thread by calling do_exit(0)
T
T
T
Call the callback empty_buf_done()
Call the callback fill_buf_done()
F
F
The opcode is invalid indicate that an error has happened in ADSP
Call the callback event_hander()
Release the handle instance here by calling xf_adsp_base_free_handle()
Set base_flag to zero
Wake up base_wait
F
T
Copy the received message to base_msg
Set base_flag to one
Wake up the base_wait by calling wake_up()
F
xf_response_thread()
Synopsis | This thread is registered when ADSP base is created. And it is destroyed when ADSP base is destroyed. This thread waits the response message from client message queue and calls the callback functions or wake up the ADSP base’s waiting corresponding to the ID from response message’s ID. | 
Syntax | static int xf_response_thread(void *data) | 
Parameter | void *data | Input data for thread usage (not use in this case)
Return value | 0 | Success

## Slide 68
APPENDIX
Overview
ADSP Base
  Introduction
  Base Control
  Internal Controls
    Handle Control
    Message Control
    Response Thread
    Other APIs
Proxy Driver Interface - Extension Interface

## Slide 69: Other APIs
Begin job
End job
Save the component id (comp_id) from the response message ID with macro XF_MSG_SRC()
No error returned?
F
T
Get a buffer in aux_pool from base instance
Set the message information
Opcode is XF_REGISTER
Length is name ID length
Buffer is name ID value
Send the message and wait for the response by calling xf_send_and_receive()
Return the buffer back to aux_pool
xf_adsp_register()
Synopsis | This API registers an ADSP plugin corresponding to the given name ID. | 
Syntax | static int xf_adsp_register(char *name, int *comp_id) | 
Parameter | char *name | The name id of this component, which defined in ADSP framework
 | int *comp_id | The ID presents for the registered component in ADSP framework
Return value | -EINVAL | Register cannot complete
 | 0 | Register successful

## Slide 70: Other APIs
Begin job
End job
Set the message information with opcode XF_UNREGISTER and the given component id (comp_id)
Return the function xf_send_and_receive()
xf_adsp_unregister()
Synopsis | This API unregisters an ADSP plugin corresponding to the registered component ID | 
Syntax | static int xf_adsp_unregister(int comp_id) | 
Parameter | int *comp_id | The ID presents for the registered component in ADSP framework
Return value | -EINVAL | Unregister cannot complete
 | 0 | Register successful

## Slide 71
APPENDIX
Overview
ADSP Base
  Introduction
  Base Control
  Internal Controls
    Handle Control
    Message Control
    Response Thread
    Other APIs
Proxy Driver Interface - Extension Interface

## Slide 72: Proxy Driver Interface - Extension Interface
This slide shows the simple detail architecture of ADSP base
The red square is the extension interface part of proxy driver for ADSP base usage.
Proxy driver
Proxy Extension Interface
Client data
Response message queue
Command message queue
Proxy data
ADSP Driver
APIs for extension interface
xf_adsp_base_client_register
xf_adsp_base_client_unregister
xf_adsp_base_send
xf_adsp_base_recv
xf_adsp_base_poll
Handle
Control
ADSP Base
Response thread
ADSP ALSA Driver
Message Control
Base Control
Handle #1
Handle #2
Component 2
Component n
Component 1
Handle #n
…
…

## Slide 73: Proxy Driver Interface - Extension Interface
xf_adsp_base_client_register()
Begin job
Allocate a new client memory by calling err = xf_client_alloc()
End job
Initialize client waiting queue by calling init_waitqueue_head()
No error returned?
Return err
F
T
Initialize client pending message queue by calling xf_msg_queue_init()
Register this client to proxy driver by calling xf_client_register()
Synopsis | This API registers a new client from proxy driver for ADSP base control. | 
Syntax | int xf_adsp_base_client_register(void **private_data) | 
Parameter | void **private_data | The pointer to store the registered proxy client.
Return value | 0 | Success
 | -ENOMEM | Cannot allocate memory for client
 | -EBUSY | Number of client in proxy has exceeded.

## Slide 74: Proxy Driver Interface - Extension Interface
xf_adsp_base_client_unregister()
Begin job
Client pointer is valid?
End job
Release all pending message in client by calling xf_msg_free_all()
Proxy data of client is valid?
F
T
Release client memory by calling xf_client_free()
Return
-EINVAL
F
T
Synopsis | This API frees the registered client to proxy driver. | 
Syntax | int xf_adsp_base_client_unregister(void *private_data) | 
Parameter | void *private_data | Pointer to registered client of ADSP base
Return value | 0 | Success
 | -EINVAL | Client data is invalid.

## Slide 75: Proxy Driver Interface - Extension Interface
xf_adsp_base_send()
Begin job
Client pointer is valid?
End job
Add the client ID into message ID for identifying the destination client when the message is responded from ADSP (using macro XF_MSG_AP_FROM_USER)
Proxy data of client is valid?
F
T
Send the message to proxy queue by calling xf_cmd_send()
Return
-EINVAL
F
T
Return
-EINVAL
No error returned?
F
T
Synopsis | This API sends a command message from ADSP base for ADSP transfer process from proxy driver. | 
Syntax | int xf_adsp_base_send(void *private_data, void *buf) | 
Parameter | void *private_data | Pointer to registered client of ADSP base
 | void *buf | Pointer to command message data
Return value | 0 | Success
 | -EINVAL | Client data is invalid, or it has not registered to proxy driver yet, or cannot send message to proxy
Return
-EINVAL

## Slide 76: Proxy Driver Interface - Extension Interface
xf_adsp_base_recv()
Begin job
Client pointer is valid?
End job
Return the msg back to proxy message pool by calling xf_msg_free()
Proxy data of client is valid?
F
T
Get the message msg from client’s message queue by calling xf_cmd_recv().
(This message buffer is gotten from proxy message pool in function xf_cmd_recv())
Return
-EINVAL
F
T
Return
-EINVAL
No error returned?
Return -EINVAL
F
T
Copy msg to input message buffer and
remove the added client ID from message ID (using macro XF_MSG_AP_FROM_USER)
Synopsis | This API gets the message from client message queue | 
Syntax | int xf_adsp_base_recv (void *private_data, void *buf) | 
Parameter | void *private_data | Pointer to registered client of ADSP base
 | void *buf | Pointer to the stored message data
Return value | 0 | Success
 | -EINVAL | Client data is invalid, or it has not registered to proxy driver yet, or the response message is invalid.

## Slide 77: Proxy Driver Interface - Extension Interface
xf_adsp_base_poll()
Begin job
Client or condition pointer are valid?
End job
Wait for the valid response message from client queue or the condition value is set to one, or
Receive thread destroy signal
Condition value is valid?
F
T
Return
-EINVAL
F
T
Return
-EINVAL
No error returned?
Return -EINVAL
F
T
Return the condition value
Synopsis | This API sleeps and waits until there are a response message is available from client message queue or the condition flag becomes true. | 
Syntax | int xf_adsp_base_poll (void *private_data, int *condition) | 
Parameter | void *private_data | Pointer to registered client of ADSP base
 | int *condition | Pointer to a waiting condition flag Valid value: 0: wait for the valid response message from client queue 1: cancel the waiting
Return value | 0 | Responded message is available.
 | 1 | Responded message is not available.
 | -EINVAL | Client or condition data is invalid, or the value of condition is not supported, or the waiting of event is interrupted.

## Slide 78
Renesas.com