## Slide 1
ADSP know-how
10/25/2019
Renesas Design Vietnam

## Slide 2: AGENDA
Introduction
Overview
ADSP driver
ADSP framework
ADSP plugins
Related HW modules
Additional sharing

## Slide 3: introduction
This material is created to transfer knowledge for new members join AudioDSP project or someone who want to investigate about AudioDSP system.
It includes 4 main parts:
ADSP driver: Introduce component and operation of ADSP driver.
ADSP framework: Introduce ADSP framework, it’s sequence flow.
ADSP plugins: Introduce ADSP plugins.
Related HW modules: Introduce HW modules related to ADSP. Guide to set and control them.

## Slide 4: overview
The figure describes audio architecture in Linux platform which uses ADSP product (inside red dash line shape).
ALSA SoC core
Shared memory area
ADSP
Audio applications
User side
Kernel side
Hardware side
ALSA Lib
Renderer/Capture/ Equalizer/TDM Renderer/TDM Capture plugin
PCM interface
Control interface
Kernel side
ALSA Middleware Layer
Platform driver (rcar_adsp_sound)
ADSP ALSA
ADSP Driver Extension
CPU DAI
Machine driver
Codec driver
Codec DAI
Codec DAI
Codec DAI
Proxy Extension Interface
ADSP Driver
Codec
Codec
Codec
CPU DAI
CPU DAI
Machine driver
Machine driver
PCM data
Communication
Legend:

## Slide 5: overview
Android Framework
Audio HAL
The figure describes audio architecture in android platform which uses ADSP product (inside red dash line shape).
From kernel to hardware side, ADSP system has no difference between android and linux platform
Note: Android platform use TinyALSA as a small library to interface with ALSA in the Linux kernel.
ALSA SoC core
Shared memory area
ADSP
Kernel side
Hardware side
TinyALSA Lib
Renderer/Capture/ Equalizer/TDM Renderer/TDM Capture plugin
PCM interface
Control interface
Kernel side
ALSA Middleware Layer
Platform driver (rcar_adsp_sound)
ADSP ALSA
ADSP Driver Extension
CPU DAI
Machine driver
Codec driver
Codec DAI
Codec DAI
Codec DAI
Proxy Extension Interface
ADSP Driver
Codec
Codec
Codec
CPU DAI
CPU DAI
Machine driver
Machine driver
Android side
Application
PCM data
Communication
Legend:

## Slide 6: ADSP driver
Platform driver (rcar_adsp_sound)
ADSP ALSA
ADSP Driver Extension
CPU DAI
Proxy Extension Interface
ADSP Driver
CPU DAI
CPU DAI
It includes below main parts:
ADSP ALSA
It is an ALSA device driver, implements to register a sound card for ADSP device. It provides callback functions for the native supports from ALSA framework to perform both playback and record. For playback/TDM playback, it receives PCM data from user app and transfers to ADSP Renderer plugin/ADSP TDM Renderer plugin. For record, it receives PCM data from ADSP Capture plugin/ADSP TDM Capture plugin and transfers to user app. The equalization function can be integrated into playback and record by routing between Equalizer and Renderer plugin, and between Equalizer and Capture plugins.
ADSP Driver Extension
It provides APIs for ADSP ALSA to connect to ADSP Driver (Proxy Extension Interface)
ADSP Driver (Proxy Extension Interface)
APIs of methods through which ADSP Driver Extension communicates with shared memory area in Hardware side.
CPU DAI
DAI stands for Digital Audio Interface. CPU DAI is the interface for the platform driver to communicate with other drivers.

## Slide 7: ADSP driver
ADSP ALSA
Location:
Source code: https://socrm.dgn.renesas.com/grepos/s492/s492c.git (branch ‘extension’ for development, branch ‘tp_st’ and ‘tp_ut’ for testing.
User Manual: https://socrm.dgn.renesas.com/repos/s492/trunk/documents/40_FD/70_ALSA
Detailed Design: https://socrm.dgn.renesas.com/repos/s492/trunk/documents/50_DD/70_ALSA.
Related materials:
Presentation: ADSP_ALSA_Driver.pptx
Guide line to develop a ALSA driver: https://www.kernel.org/doc/html/v4.17/sound/kernel-api/writing-an-alsa-driver.html#

## Slide 8: ADSP driver
ADSP Driver Extension
Location:
Source code: https://socrm.dgn.renesas.com/grepos/s492/s492c.git (branch ‘extension’ for development, branch ‘tp_st’ and ‘tp_ut’ for testing.
User Manual: https://socrm.dgn.renesas.com/repos/s492/trunk/documents/40_FD/20_DRV
Detailed Design: https://socrm.dgn.renesas.com/repos/s492/trunk/documents/50_DD/70_ALSA.
Related materials:
Presentation: ADSP_Driver_Extension.pptx

## Slide 9: ADSP driver
ADSP Driver (Proxy Extension Interface)
Location:
Source code: https://socrm.dgn.renesas.com/grepos/s492/s492c.git (branch ‘extension’ for development, branch ‘tp_st’ and ‘tp_ut’ for testing)

## Slide 10: ADSP driver
CPU DAI
It is implemented in ADSP ALSA driver and device tree.
Location:
Source code: https://socrm.dgn.renesas.com/grepos/s492/s492c.git (branch ‘extension’ for development)
Configuration: It is configured in device tree files in kernel source (arch/arm64/boot/dts/renesas/). For guide line please refer to section 1.1 Device Tree in User Manual of ADSP ALSA driver: https://socrm.dgn.renesas.com/repos/s492/trunk/documents/40_FD/70_ALSA

## Slide 11: ADSP framework
ADSP framework
Location:
Source code: https://socrm.dgn.renesas.com/grepos/s492/s492d.git (branch ‘master’ for development, branch ‘tp_ut’ for testing)
User Manual: https://socrm.dgn.renesas.com/repos/s492/trunk/documents/40_FD/30_FWK
Detailed Design: https://socrm.dgn.renesas.com/repos/s492/trunk/documents/50_DD/30_FWK
Related materials:
Communication flow: Audio_Framework_Specification.pdf

## Slide 12: ADSP plugins
ADSP Renderer/Capture plugins
Location:
Source code: https://socrm.dgn.renesas.com/grepos/s492/s492e.git (branch ‘master’ for development, branch ‘tp_ut’ for testing)
User Manual: https://socrm.dgn.renesas.com/repos/s492/trunk/documents/40_FD/40_RDR
Detailed Design: https://socrm.dgn.renesas.com/repos/s492/trunk/documents/50_DD/40_RDR
Related materials:
Solution investigation for CTU/MIX: CTU&MIXER.pptx

## Slide 13: ADSP plugins
ADSP Equalizer plugin
Location:
Source code: https://socrm.dgn.renesas.com/grepos/s492/s492f.git (branch ‘master’ for development)
User Manual: https://socrm.dgn.renesas.com/repos/s492/trunk/documents/40_FD/50_EQZ
Detailed Design: https://socrm.dgn.renesas.com/repos/s492/trunk/documents/50_DD/50_EQZ
Related materials:
Investigation about Equalizer function: Equalizer_Investigation.pptx

## Slide 14: ADSP plugins
ADSP TDM Renderer/Capture plugins
Location:
Source code: https://socrm.dgn.renesas.com/grepos/s492/s492g.git (branch ‘master’ for development)
User Manual: https://socrm.dgn.renesas.com/repos/s492/trunk/documents/40_FD/60_TDM
Detailed Design: https://socrm.dgn.renesas.com/repos/s492/trunk/documents/50_DD/60_TDM

## Slide 15: Related HW modules
SSI driver
Location:
Source code: xa_ssi_drv.c, xa_ssi_drv.h in Renderer/Capture, xa_tdm_ssi_drv.c, xa_tdm_ssi_drv.h TDM Renderer/TDM Capture plugin’s source code
Detailed Design: https://socrm.dgn.renesas.com/repos/s492/trunk/documents/50_DD/40_RDR/en/
        https://socrm.dgn.renesas.com/repos/s492/trunk/documents/50_DD/60_TDM/en/
Related material:
Operation, setting: SSIU-SSI Register Setting for ADSP Project.pptx

## Slide 16: Related HW modules
SSIU driver
Location:
Source code: xa_ssiu_drv.c, xa_ssiu_drv.h in Renderer/Capture, xa_tdm_ssiu_drv.c, xa_tdm_ssiu_drv.h TDM Renderer/TDM Capture plugin’s source code
Detailed Design: https://socrm.dgn.renesas.com/repos/s492/trunk/documents/50_DD/40_RDR/en/
        https://socrm.dgn.renesas.com/repos/s492/trunk/documents/50_DD/60_TDM/en/
Related material:
Operation, setting: SSIU-SSI Register Setting for ADSP Project.pptx

## Slide 17: Related HW modules
SCU driver
Location:
Source code: xa_scu_drv.c, xa_scu_drv.h in Renderer/Capture, xa_tdm_scu_drv.c, xa_tdm_scu_drv.h TDM Renderer/TDM Capture plugin’s source code
Detailed Design: https://socrm.dgn.renesas.com/repos/s492/trunk/documents/50_DD/40_RDR/en/
        https://socrm.dgn.renesas.com/repos/s492/trunk/documents/50_DD/60_TDM/en/
Related material:
Operation, setting: CTU&MIXER.pptx

## Slide 18: Related HW modules
ADMAC driver
Location:
Source code: xa_dmac_regs.c, xa_dmac_regs.h in Renderer/Capture plugin’s source code, xa_tdm_dmac_regs.c, xa_tdm_dmac_regs.h TDM Renderer/TDM Capture plugin’s source code
Detailed Design: https://socrm.dgn.renesas.com/repos/s492/trunk/documents/50_DD/40_RDR/en/
        https://socrm.dgn.renesas.com/repos/s492/trunk/documents/50_DD/60_TDM/en/

## Slide 19: Related HW modules
PDMA driver
Location:
Source code: xa_pdma_regs.c, xa_pdma_regs.h in Renderer/Capture, xa_tdm_pdma_regs.c, xa_tdm_pdma_regs.h TDM Renderer/TDM Capture plugin’s source code
Detailed Design: https://socrm.dgn.renesas.com/repos/s492/trunk/documents/50_DD/40_RDR/en/
        https://socrm.dgn.renesas.com/repos/s492/trunk/documents/50_DD/60_TDM/en/

## Slide 20: Related HW modules
FIFO driver
Location:
Source code: xa_fifo_drv.c, xa_fifo_drv.h in Renderer/Capture, xa_tdm_fifo_drv.c, xa_tdm_fifo_drv.h TDM Renderer/TDM Capture plugin’s source code
Detailed Design: https://socrm.dgn.renesas.com/repos/s492/trunk/documents/50_DD/40_RDR/en/
        https://socrm.dgn.renesas.com/repos/s492/trunk/documents/50_DD/60_TDM/en/

## Slide 21: ADDITIONAL SHARING
180215_RNSL_R-Car Gen3_Audio WorkShop_shown.pptx: Material presented in Renault-Nissan’s workshop.
Gen3APN_Audio_flow_20161028.pptx : audio data control flow guide line provided by REL
Git_Branching_Investigation.pptx : guide line about Git

## Slide 22
Renesas.com