## Slide 1
CTU / mixer
  AUDIO – DSP Project
Date
Name
Position, Department,
Unit
Renesas Electronics Corporation

## Slide 2: Agenda
CTU/MIXER INTRODUCTION Page 03
USE CASE 1 – UPDATE RENDERER Page 09
USE CASE 2 – DEVELOP NEW PLUGIN Page 21

## Slide 3: CTU – channel transfer unit introduction
Downmixing and splitter functions
Conversion of eight input channels into two output channels
Conversion of six input channels into two output channels
Conversion of two input channels into four sets of two output channels
Conversion of one input channel into eight sets of one output channel
No conversion
CTU
input
output

## Slide 4: CTU – channel transfer unit Setting procedure
CTU Activation
CTUn_SWRSR.SWRST = 0; // Reset CTU, set software reset
CTUn_SWRSR.SWRST = 1; // Put to operation state, clear software reset
CTU Initial value setting
CTUn_CTUIR.INIT = 1; // Initialize the operation of the CTU internal circuits
CTUn_ADINR.CHNUM = 2; // set channel (1/2/4/6/8 are also supported)
CTUn_CPMDR = 0; // set the data pass
CTUn_SCMDR = 0; // no operation about the scale matrix
//CTUn_SV00R = 0x400000 // set the scale value for channel 0 of matrix row 0
//CTUn_SV11R = 0x400000 // set the scale value for channel 1 of matrix row 1
//CTUn_SV30R = 0x400000 // set the scale value for channel 3 of matrix row 3
CTUn_CTUIR.INIT = 0; // cancel initial and go to processing state
CTU Halting:
CTUn_CTUIR.INIT = 1; // Initialize the operation
CTUn_SWRSR.SWRST = 0; // Set software reset

## Slide 5: CTU – channel transfer unit downmixing solution for conversion of 5.1/7.1 to stereo
Left = 0 dB (or full)
Right = 0 dB
Center = -3 dB (the reason for this is covered in the article on Pan-Law)
LFE = -3 dB (the default is always “off”)
Ls/Rs = -6 dB
Lm/Rm = -6 dB

## Slide 6: MIX - mixer introduction
MIX
input 1
input 2
input 3
input 4
output
Mixing (adds) two to four sources into one

## Slide 7: MIX - mixer setting procedure
MIX Activation:
MIXp_SWRSR.SWRST = 0; // Set software reset for MIX
MIXp_SWRSR.SWRST = 1; // Clear reset bit, change to operating state
MIX Initial Value Setting:
MIXp_MIXIR.INIT = 1; // Initialization state
MIXp_ADINR.CHNUM = 2; // set the output channel of mixer
MIXp_MIXMR = 0; // Set mode volume step or volume ramp
MIXp_MVPDR = 0; // Set decibel that changed by one sample
MIXp_MDBER.MIXDBEN = 0; // Disable the setting of dB for system A/B/C/D
MIXp_MDBAR = 0; // Set decibel of system A
MIXp_MDBBR = 0; // Set decibel of system B
MIXp_MDBCR = 0; // Set decibel of system C
MIXp_MDBDR = 0; // Set decibel of system D
MIXp_MDBER.MIXDBEN = 1; // Enable the setting of dB for system A/B/C/D
MIXp_MIXIR.INIT = 0; // Processing state
MIX Halting:
MIXp_MIXIR.INIT = 1; // Initialization state
MIXp_SWRSR.SWRST = 0; // Set software reset for MIX

## Slide 8: Agenda
CTU/MIXER INTRODUCTION Page 03
USE CASE 1 – UPDATE RENDERER Page 09
USE CASE 2 – DEVELOP NEW PLUGIN Page 21

## Slide 9: USE CASE 1 Update RENDERER/Capture TO CONNECT CTU/MIXER internally
SRC 0
SRC 2
SRC 3
SRC 4
CTU 0
MIX
DVC
CTU 1
CTU 2
CTU 3
CMD
Module connection diagram for Capture
SSI 1
Capture
SSI 2
SSI 3
SSI 4
Plugin function | PCM input function | PCM output function
Capture and mix from one or multiple SSI to one stereo file | Channel number: 1/2/4/6/8 ch | Channel number: 1/2 ch
Support channel transfer from multiple channel (3.1/5.1/7.1) input to stereo output | Frequency: 32/44.1/48 kHz | Frequency: 32/44.1/48 kHz
 | Bit-width: 16/24 bit | Bit-width: 16/24 bit

## Slide 10: USE CASE 1 Update RENDERER/Capture TO CONNECT CTU/MIXER internally
Renderer 1
Renderer 2
Renderer 3
Renderer 4
SRC 0
SRC 2
SRC 3
SRC 4
CTU 0
MIX
DVC
SSI
CTU 1
CTU 2
CTU 3
CMD
Module connection diagram for Renderer
Plugin function | PCM input function | PCM output function
Mix and render from one or multiple Renderer to one SSI | Channel number: 1/2/4/6/8 ch | Channel number: 1/2 ch
Support channel transfer from multiple channel (3.1/5.1/7.1) input to stereo output | Frequency: 32/44.1/48 kHz | Frequency: 32/44.1/48 kHz
 | Bit-width: 16/24 bit | Bit-width: 16/24 bit

## Slide 11: USE CASE 1 Update RENDERER/Capture TO CONNECT CTU/MIXER internally
CMD0
Renderer 1
SRC 0
CTU 0
MIX
DVC
SSI
- 1st Renderer goes to Init-processing firstly.
- The route path will be set fully from SRC to SSI.
- All module currently are activing and transferring data.
The information of this connection including (CMD–DMA2SSI) will be stored in the COM1 register for other plugin’s reference.
(refer to page 13 for more information)
The route connection and SRC modules are presented in CMDn_ROUTE_SELECT register.
CTU 1
CTU 2
CTU 3
SRC 2
SRC 3
SRC 4
What’s happen when SRC2 is used by another plugin without mixing with Renderer1?
=> It is no problem for the output of Renderer1. Because data from SRC2 cannot be transferred to MIX when CTU1 is still disabled.
DMA1
DMA2
bit | 31 ~ 22 | 21 ~ 18 | 17 ~ 12 | 11 | 10 ~ 7 | 6 ~ 1 | 0
COM1 | … | SSI index | ADMA index | CMD1 bit | SSI index | ADMA index | CMD0 bit
Use case analysis

## Slide 12: USE CASE 1 Update RENDERER/Capture TO CONNECT CTU/MIXER internally
CMD0
Renderer 1
Renderer 2
MIX
DVC
SSI
2nd Renderer now is going to Init-processing.
If SSI is being enabled. It will be implied that the mixing function is required for 2nd Renderer.
In this case, it is mandatory that 1st and 2nd stream have to same the output data format (number of output channel, volume rate, output sampling rate, PCM width). If NOT, plugin will return error of hardware busy.
This area does NOT need to setup in 2nd Renderer. It has been set in 1st Renderer’s Init-processing.
2nd Renderer will connect to SRC2 because SRC0 was activated in the first data path.
How to check this condition?
SRC 0
SRC 2
CTU 0
CTU 1
CTU 2
CTU 3
SRC 3
SRC 4
Use case analysis

## Slide 13: USE CASE 1 Update RENDERER/Capture TO CONNECT CTU/MIXER internally
CMD0
Renderer 1
Renderer 2
MIX
DVC
SSI
How to check this condition?
Get register SRCm_ADINR for PCM width checking.
Get DVCp_VOLnR for volume rate checking.
Get SSICRn for output channel checking.
Get CMDOUT_TIMSEL for output frequency checking.
SRC 0
SRC 2
CTU 0
CTU 1
CTU 2
CTU 3
SRC 3
SRC 4
Use case analysis

## Slide 14: USE CASE 1 Update RENDERER/Capture TO CONNECT CTU/MIXER internally
CMD0
Renderer 1
Renderer 2
Renderer 3
Renderer 4
MIX
DVC
SSI
3rd and 4th Renderer is the same as 2nd Renderer.
SRC 0
SRC 2
SRC 3
SRC 4
CTU 0
CTU 1
CTU 2
CTU 3
Use case analysis

## Slide 15: USE CASE 1 Update RENDERER/Capture TO CONNECT CTU/MIXER internally
bit | 31 ~ 22 | 21 ~ 18 | 17 ~ 12 | 11 | 10 ~ 7 | 6 ~ 1 | 0
COM1 | … | SSI index | ADMA index | CMD1 bit | SSI index | ADMA index | CMD0 bit
CMDn bit | CMDn working status 0 : Inactivating 1 : Activating
ADMA index | ADMA module connects between CMD and SSI 0-28 : Audio-DMACpp[0-28] 29-60 : Audio-DMAC[0-31]
SSI index | SSI module connects to CMD correspondingly 0-9 : SSI[0-9]
Plugin start with SSIx
Get info of CMDm, ADMAm, SSIm module from COM1 register and compare with SSIx
SSIx is enabled?
SSIm=SSIx?
Get CMDm_ROUTE_SELECT register and connect to the corresponding SRC module
Operate as normal cases
Return error of hardware busy
Plugin stop
Executing
F
F
T
T
Init-processing state
COM register solution:
When using 4 Renderer for mixing data, the 2nd , 3rd and 4th Renderer have to know what CMD/DMAC/SSI module are used in the 1st Renderer. So that they can connect to the right destination. By using COM register (the registers belong to ADSP module and used for software purpose), plugin can get these information quickly and easily.
CMD1 connection info
CMD0 connection info
Use case analysis

## Slide 16: USE CASE 1 Update RENDERER/Capture TO CONNECT CTU/MIXER internally
CMD0
Renderer 1
Renderer 2
Renderer 3
Renderer 4
MIX
DVC
SSI
SRC 0
SRC 2
SRC 3
SRC 4
CTU 0
CTU 1
CTU 2
CTU 3
Ending procedure:
When Renderer1 is ending. It will check all the SRC modules. If they still enable, Renderer1 will disable SRC0 and goes to ending processing. CMD and SSI are still activating after Renderer1 stops.
When Renderer2 and Renderer3 are ending. It is the same as Renderer1, only SRC2 and SRC3 are disabled.
When the last plugin-Renderer4 is ending. After checking SRC0/2/3 modules and if they are disabled, It will disable all the remain hardware modules (CMD, SSI) and goes to ending processing.
Check these modules status in the ending procedure
Use case analysis

## Slide 17: USE CASE 1 Update RENDERER/Capture TO CONNECT CTU/MIXER internally
Can user set different volume rate in each stream?
=> Mixer has function to select gain level for each inputs. But the gain value is always less than zero (0dB - -∞). For this use case, it is better when all stream have a same volume rate setting.
Use case analysis
CMD0
Renderer 1
Renderer 2
Renderer 3
Renderer 4
SRC 1
SRC 2
SRC 3
SRC 4
MIX
DVC
SSI
CTU 0
CTU 1
CTU 2
CTU 3

## Slide 18: USE CASE 1 Update RENDERER/Capture TO CONNECT CTU/MIXER internally
What should we update in Renderer to add CTU/MIX function?
Remove option about SRC module index in set parameters phase. It doesn’t need to set SRC module, plugin can control and select the most suitable one to execute task.
Now the input stream can be 4 or 6 or 8 channels instead of only 1 or 2 channels (for using CTU function). So the whole source code will be updated to deal this condition.
Add more parameters for Renderer plugin such as input channel, output channel.
Update source code to checking the consistency of output data format between Renderers (get registers information of hardware (refer page 11)).
Update source code for ending procedure.
CMD0
Renderer 1
Renderer 2
Renderer 3
Renderer 4
SRC 1
SRC 2
SRC 3
SRC 4
MIX
DVC
SSI
CTU 0
CTU 1
CTU 2
CTU 3
Use case analysis

## Slide 19: USE CASE 1 Update RENDERER/Capture TO CONNECT CTU/MIXER internally
What should we update in Capture to add CTU/MIX function?
Remove option about SRC module index in set parameters phase. It doesn’t need to set SRC module, plugin can control and select the most suitable one to execute task.
Now the input stream can be 4 or 6 or 8 channels instead of only 1 or 2 channels (for using CTU function). So the whole source code will be updated to deal this condition.
Add more parameters for Renderer plugin such as input channel, output channel.
Update driver configuration support multiple SSI mode (use multiple SSI) and TDM mode (use channel transfer function)
CMD0
Renderer 1
Renderer 2
Renderer 3
Renderer 4
SRC 1
SRC 2
SRC 3
SRC 4
MIX
DVC
SSI
CTU 0
CTU 1
CTU 2
CTU 3
Use case analysis

## Slide 20: Agenda
CTU/MIXER INTRODUCTION Page 03
USE CASE 1 – UPDATE RENDERER Page 09
USE CASE 2 – DEVELOP NEW PLUGIN Page 21

## Slide 21: USE CASE 2 develop new plugin
SRC 0
SRC 2
SRC 3
SRC 4
CTU 0
MIX
DVC
SSI
CTU 1
CTU 2
CTU 3
CMD0
Mixer
plugin
Memory 1
Memory 2
Memory 3
Memory 4
The mixer plugin is responsible for transfer data from input ports to correspond output hardware module (SRC).
The mixer plugin has 1~4 input ports.
The data will be mixed into one stream and then output to SSI.
The input channel can be 1/2/4/6/8. The output channel can be 1 or 2.
It can set difference volume rate for input PCMs.
The input PCMs can have difference channel format.

## Slide 22
Renesas.com