## Slide 1
SSIU / SSI SETTING
User's Manual
ADSP Project
21st /MAR/2017

## Slide 2: Agenda
SSIU/SSI Overview 3
SSIU/SSI Register 6
SSIU/SSI Process 9

## Slide 3: SSIU/SSI - Overview
SSI - Serial Sound Interface
A transceiver module designed to send or receive audio data interfacing with a variety of devices offering I2S format.
Support multi-channel mode in addition to other common formats (left-aligned, right-aligned format).
Features
The SSI module can serve as both a transmitter and a receiver.
Only the MSB first data alignment is supported.
A value as the dividing ratio for the clock used by the serial bus interface is selectable.
Controlling of data transmission or reception with DMAC or interrupt requests is possible.
Monaural mode (8 bits, 16 bits) is supported.
Available module: SSI0 to SSI9
* For more information please refer to 42.1.1 in R-CarGen3_HW_Users_Manual

## Slide 4: SSIU/SSI - overview
SSIU - Serial Sound Interface Unit
An Audio Unit used to transfer data between SSIs and other audio modules (SRC, CMD, ...) or external memories via their Bus Interfaces (a bus is used for interfacing function) connected to audio DMA/local bus. Each SSI module connects with a specific Bus Interface.
Features
Incorporates 10 SSI modules.
Supports 6 channels/1 sound source with 3 SSI modules (SSI0, SSI1, and SSI2).
Supports 8 channels/1 sound source with 4 SSI modules (SSI0, SSI1, SSI2, and SSI9).
Operation of multiple modules on the same serial clock.
* For more information please refer to 41.1 in R-CarGen3_HW_Users_Manual

## Slide 5: SSIU/SSI - overview
SSIU - Serial Sound Interface Unit
A
Data transfer is performed between SSIU and SSI
via SSIn-0_BUSIF connected to the audio DMA/local bus.
This is basic configuration.
SSIn-0_BUSIF
SSIn-1_BUSIF
. . .
SSIn-7_BUSIF
MUX
SSIn
Audio DMA/Local bus
C
B
A
SSIU
Pin function control
Block diagram
B
Data transfer is performed between SSIU and SSI
via multiple BUSIF connected to the audio DMA/local bus.
C
Data transfer is performed independent of SSIU from
SSI to audio DMA/local bus.
Note: This document is applied for route
SSIn-0_BUSIF: Bus Interface 0 for SSIn (n = 0 to 9)
MUX: a multiplexer (mux) or a demultiplexer (demux)
A

## Slide 6: SSIU/SSI – register
SSI main registers
Control Register (SSICRn) control the IRQ, selects the polarity status, and sets operating mode.
Transmit Data Register (SSITDRn) holds data to be transmitted.
Receive Data Register (SSIRDRn) stores receive messages.
WS Mode Register (SSIWSRn) sets the TDM format, monaural format, and WS continue function.
Note: n = 0 to 9

## Slide 7: SSIU/SSI – register
SSIU main registers
SSIn BUSIF Mode Register (SSIn_BUSIF_MODE) determines the initial settings of bus interface.
SSIm BUSIF Audio Information Register (SSIm_BUSIF_ADINR) selects channel number and bit length of output audio data.
SSIr BUSIF Audio Information Register (SSIr_BUSIF_ADINR) selects channel number and bit length of output audio data.
SSIq Control Register (SSIq_CONTROL) control the start and stop of data transfer.
SSIr Control Register (SSIr_CONTROL) control the start and stop of data transfer.
Note: n = 0-0 to 0-7, 1-0 to 1-7, 2-0 to 2-7, 3-0 to 3-7, 4-0 to 4-7, 5 to 8, or 9-0 to 9-7
m = 0-0 to 0-7, 1-0 to 1-7, 2-0 to 2-7, 3-0 to 3-7, 4-0 to 4-7, or 9-0 to 9-7;
q = 0-0, 1-0, 2-0, 3-0, 4-0, or 9-0; r = 5 to 8

## Slide 8: SSIU/SSI – register
SSIU main registers
SSI Mode Register 0 (SSI_MODE0) specifies the independent SSI transfer.
SSI Mode Register 1 (SSI_MODE1) specifies the SSI pin mode.
SSI Mode Register 2 (SSI_MODE2) specifies the SSI pin mode.
SSI Mode Register 3 (SSI_MODE3) specifies the SSI pin mode.
SSI Control Register (SSI_CONTROL) controls the start up of the SSI modules when multiple SSI modules are used at the same time.

## Slide 9: SSIU/SSI – process
Example: Using SSI0 as the output device for Renderer plugin.
Parameters: channel = 2, PCM width = 16bits, sampling frequency = 32000Hz
Raw PCM stream
SSI setup
SSIU start
SSIU stop
Finish
Start
Data0 | Channel-1
Data0 | Channel-2
Data1 | Channel-1
Data1 | Channel-2
Data2 | Channel-1
... | ...
PCM width = 16 bits
MSB
LSB
- Input PCM format:
SSI stop
SSI start
SSIU setup
ADSP
Renderer Plugin
Memory
Memory
DMA
SSIU
SSI0
SSI0-0_BUSIF

## Slide 10: SSIU/SSI – process
Example: Using SSI0 as the output device for Renderer plugin.
Parameters: channel = 2, PCM width = 16bits, sampling frequency = 32000Hz
- Expected stereo output format for SSI module:
Data0 | Channel-1 | 
Data0 | Channel-2 | 
Data1 | Channel-1 | 
Data1 | Channel-2 | 
Data2 | Channel-1 | 
... | ... | 
A system word
A data word
32 bits system word length
16 bits data word length
MSB
LSB
SSI setup
SSIU start
SSIU stop
Finish
Start
SSI stop
SSI start
SSIU setup

## Slide 11: SSIU/SSI – process
Example: Using SSI0 as the output device for Renderer plugin.
Parameters: channel = 2, PCM width = 16bits, sampling frequency = 32000Hz
- Serial clock selection:
Note:
AUDIO_CLKA (22.5792 MHz) using for 44.1kHz, 88.2kHz
AUDIO_CLKB (24.576MHz) using for 48kHz, 96kHz
Serial bit clock frequency of SSI0 is 32000Hz .
ADG setting:
- select AUDIO_CLKB
- division ratio = 0
ssi0_clkfs = ACLK_B/2 (= 12.288MHz)
* This clock will be divided again by clock divider in SSI0 to generate 32000Hz for data transmission.
clock divider
SSI0
CLK_FS
ADG
ssi0_clkfs
AUDIO_CLKA
AUDIO_CLKB
AUDIO_CLKC
div
1/2
SSI setup
SSIU start
SSIU stop
Finish
Start
SSI stop
SSI start
SSIU setup

## Slide 12: SSIU/SSI – process
Example: Using SSI0 as the output device for Renderer plugin.
Parameters: channel = 2, PCM width = 16bits, sampling frequency = 32000Hz
- Serial clock selection:
clock divider
SSI0
CLK_FS
ssi0_clkfs
SCK
CLK_FS = ssi0_clkfs = 12.288MHz
serial bit clock (SCK) = 32000Hz
system word = 32 bit
number of channel = 2 ch
=> oversampling clock frequency = 12.288MHz / (32bit * 2ch) = 192000Hz
=> division ratio of SSI0 = 192000Hz / 32000Hz = 6
SSI setup
SSIU start
SSIU stop
Finish
Start
SSI stop
SSI start
SSIU setup
Note:
SSI0 will use its CLK_FS input clock to supply to serial clock (SCK) and word select (WS) signal.
=> SSI0 operates in the master mode.
WS

## Slide 13: SSIU/SSI – process
Example: Using SSI0 as the output device for Renderer plugin.
Parameters: channel = 2, PCM width = 16bits, sampling frequency = 32000Hz
1. Select mode format of SSI0 as stereo format.
SSIWSRn.WS_MODE = 0
2. SSI0 operates in master mode so the WS Continue Function must be enabled.
SSIWSRn.CONT = 1
WS Continue Function
0: WS continue function is disabled.
1: WS continue function is enabled.
WS Mode
0: Stereo format, multi-channel format.
1: TDM format, monaural format.
 |  | Bit |  | 31 | ... | 8 | ... | 0
SSIWSRn |  |  |  | -- | -- | CONT | -- | WS_MODE
SSI setup
SSIU start
SSIU stop
Finish
Start
SSI stop
SSI start
SSIU setup

## Slide 14: SSIU/SSI – process
Example: Using SSI0 as the output device for Renderer plugin.
Parameters: channel = 2, PCM width = 16bits, sampling frequency = 32000Hz
3. Set the FORCE bit. This bit is always be set to 1.
SSICRn.FORCE = 1
4. Enable DMA request
SSICRn.DMEN = 1
5. Set the number of channels in each system word.
SSICRn.CHNL = 0x00
DMA Enable
0: DMA request is disabled
1: DMA request is enabled
 |  | Bit |  | 31 | ... | 28 | ... | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16
SSICRn |  |  |  | FORCE | --- | DMEN | --- | CHNL[1:0] |  | DWL[2:0] |  |  | SWL[2:0] |  | 
Channels
With stereo or multi-channel format:
00: A system word has 1 channel.
01: A system word has 2 channels.
10: A system word has 3 channels.
11: A system word has 4 channels.
SSI setup
SSIU start
SSIU stop
Finish
Start
SSI stop
SSI start
SSIU setup

## Slide 15: SSIU/SSI – process
Example: Using SSI0 as the output device for Renderer plugin.
Parameters: channel = 2, PCM width = 16bits, sampling frequency = 32000Hz
6. Set number of bits in a data word
SSICRn.DWL = 0x001
7. Set number of bits in a system word
SSICRn.SWL = 0x011
Data word length
With stereo or multi-channel format:
000: 8 bits
001: 16 bits
010: 18 bits
011: 20 bits
100: 22 bits
101: 24 bits
110: 32 bits
111: Prohibited
 |  | Bit |  | 31 | ... | 28 | ... | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16
SSICRn |  |  |  | FORCE | --- | DMEN | --- | CHNL[1:0] |  | DWL[2:0] |  |  | SWL[2:0] |  | 
System word length
With stereo or multi-channel format:
000: 8 bits
001: 16 bits
010: 24 bits
011: 32 bits
100: 48 bits
101: 64 bits
110: 128 bits
111: 256 bits
SSI setup
SSIU start
SSIU stop
Finish
Start
SSI stop
SSI start
SSIU setup

## Slide 16: SSIU/SSI – process
Example: Using SSI0 as the output device for Renderer plugin.
Parameters: channel = 2, PCM width = 16bits, sampling frequency = 32000Hz
8. Set the serial bit clock and WS direction of SSI0
is output, master mode.
SSICRn.SCKD = 1
SSICRn.SWSD = 1
9. Set no delay between SSI_WS and SSI_SDATA
SSICRn.DEL = 1
Serial bit clock direction
0: Serial bit clock is input, slave mode
1: Serial bit clock is output, master mode
 |  | Bit |  | 15 | 14 | ... | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
SSICRn |  |  |  | SCKD | SWSD | -- | DEL | -- | SKDV[2:0] |  |  | MUEN | -- | TRMD | EN
Serial WS direction
0: Serial word select is input, slave mode
1: Serial word select is output, master mode
Serial Data Delay
0: One clock cycle delay between
SSI_WS and SSI_SDATA
1: No delay
SSI setup
SSIU start
SSIU stop
Finish
Start
SSI stop
SSI start
SSIU setup

## Slide 17: SSIU/SSI – process
Example: Using SSI0 as the output device for Renderer plugin.
Parameters: channel = 2, PCM width = 16bits, sampling frequency = 32000Hz
10. Set the ratio between oversampling clock
and the serial bit clock.
(refer to slide 12 for more detail)
SSICRn.SKDV = 0x101
 |  | Bit |  | 15 | 14 | ... | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
SSICRn |  |  |  | SCKD | SWSD | -- | DEL | -- | SKDV[2:0] |  |  | MUEN | -- | TRMD | EN
Serial Oversampling Clock Division Ratio
These bits are ignored if SCKD = 0 (slave mode)
The serial bit clock is used in the shift register and is provided on the SSI_SCK module pin.
000: Serial bit clock frequency = oversampling clock frequency / 1
001: Serial bit clock frequency = oversampling clock frequency / 2
010: Serial bit clock frequency = oversampling clock frequency / 4
011: Serial bit clock frequency = oversampling clock frequency / 8
100: Serial bit clock frequency = oversampling clock frequency / 16
101: Serial bit clock frequency = oversampling clock frequency / 6
110: Serial bit clock frequency = oversampling clock frequency / 12
111: Setting prohibited
SSI setup
SSIU start
SSIU stop
Finish
Start
SSI stop
SSI start
SSIU setup

## Slide 18: SSIU/SSI – process
Example: Using SSI0 as the output device for Renderer plugin.
Parameters: channel = 2, PCM width = 16bits, sampling frequency = 32000Hz
11. Enable serial data output.
SSICRn.MUEN = 0
12. SSI0 used to transmit serial data to another device.
So the module will be in the transmit mode.
SSICRn.TRMD = 1
 |  | Bit |  | 15 | 14 | ... | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
SSICRn |  |  |  | SCKD | SWSD | -- | DEL | -- | SKDV[2:0] |  |  | MUEN | -- | TRMD | EN
Serial Data Output Disable
0: Module is not muted.
1: Module is muted
Transmit / Receive Mode Select
0: Module is in receive mode
1: Module is in transmit mode.
SSI setup
SSIU start
SSIU stop
Finish
Start
SSI stop
SSI start
SSIU setup

## Slide 19: SSIU/SSI – process
Example: Using SSI0 as the output device for Renderer plugin.
Parameters: channel = 2, PCM width = 16bits, sampling frequency = 32000Hz
1. Select the access type for SSIn_BUSIF as DMA access. (n = 0-0)
SSIn_BUSIF_MODE.dma = 1
2. Setting SSIm_BUSIF Audio Information Register. (m = 0-0)
SSIm_BUSIF_ADINR.OTBL = 0x01000
SSIm_BUSIF_ADINR.CHNUM = 0x00010
DMA Access Type
0: PIO access (prohibited)
1: DMA access
 |  |  |  | Bit |  | 31 | ... | 20 | 19 | 18 | 17 | ... | 4 | 3 | 2 | 1
SSIm_BUSIF_ADINR |  |  |  |  |  | -- | -- | OTBL[4:0] |  |  |  | -- | CHNUM[4:0] |  |  | 
 |  |  |  | Bit |  | 31 | 30 | ... | 1 | 0
SSIn_BUSIF_MODE |  |  |  |  |  | -- | -- | -- | -- | dma
Bit Length of Output Audio Data
00000: 24 bits
00001: 22 bits
00100: 20 bits
00110: 18 bits
01000: 16 bits
10000: 8 bits
Others: Reserved
Channel Number
With Basic configuration:
00000: 0 (none)
00001: 1 channel
00010: 2 channels
00100: 4 channels
00110: 6 channels
01000: 8 channels
Others: Reserved
SSI setup
SSIU start
SSIU stop
Finish
Start
SSI stop
SSI start
SSIU setup

## Slide 20: SSIU/SSI – process
1. Select the access type for SSIn_BUSIF as DMA access. (n = 0-0)
SSIn_BUSIF_MODE.dma = 1
2. Setting SSIm_BUSIF Audio Information Register. (m = 0-0)
SSIm_BUSIF_ADINR.OTBL = 0x01000
SSIm_BUSIF_ADINR.CHNUM = 0x00010
3. Set SSI0 to no perform independent transfer.
(refer to route A in the page 5 for more detail)
SSI_MODE0.ind0 = 0
Independent SSI0 transfer setting
0: Independent SSI0 transfer is not performed
1: Independent SSI0 transfer is performed
 |  | Bit |  | 31 | ... | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
SSI_MODE0 |  |  |  | -- | -- | ind9 | ind8 | ind7 | ind6 | ind5 | ind4 | ind3 | ind2 | ind1 | ind0
Example: Using SSI0 as the output device for Renderer plugin.
Parameters: channel = 2, PCM width = 16bits, sampling frequency = 32000Hz
SSI setup
SSIU start
SSIU stop
Finish
Start
SSI stop
SSI start
SSIU setup

## Slide 21: SSIU/SSI – process
Example: Using SSI0 as the output device for Renderer plugin.
Parameters: channel = 2, PCM width = 16bits, sampling frequency = 32000Hz
- Set bit EN in Control Register to enable module.
SSICRn.EN = 1
 |  | Bit |  | 15 | 14 | ... | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
SSICRn |  |  |  | SCKD | SWSD | -- | DEL | -- | SKDV[2:0] |  |  | MUEN | -- | TRMD | EN
SSI Module Enable
0: Module is disabled.
1: Module is enabled.
SSI setup
SSIU start
SSIU stop
Finish
Start
SSI stop
SSI start
SSIU setup

## Slide 22: SSIU/SSI – process
Start SSI0-0 transfer by setting bit start_0 in SSIq Control Register (q = 0-0)
SSIq_CONTROL.start_0 = 1
 |  |  | Bit |  | 31 | ... | 28 | ... | 24 | ... | 20 | ... | 16 | ... | 12 | ... | 8 | ... | 4 | ... | 0
SSIq_CONTROL |  |  |  |  | -- | -- | start_7 | -- | start_6 | -- | start_5 | -- | start_4 | -- | start_3 | -- | start_2 | -- | start_1 | -- | start_0
Example: Using SSI0 as the output device for Renderer plugin.
Parameters: channel = 2, PCM width = 16bits, sampling frequency = 32000Hz
SSIi-0_start_flag
0: Stop data transfer through SSIi-0
1: Start data transfer through SSIi-0
(i = 0 to 4, 9)
SSI setup
SSIU start
SSIU stop
Finish
Start
SSI stop
SSI start
SSIU setup

## Slide 23: SSIU/SSI – process
Example: Using SSI0 as the output device for Renderer plugin.
Parameters: channel = 2, PCM width = 16bits, sampling frequency = 32000Hz
- Reset bit EN in Control Register to disable module.
SSICRn.EN = 0
 |  | Bit |  | 15 | 14 | ... | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
SSICRn |  |  |  | SCKD | SWSD | -- | DEL | -- | SKDV[2:0] |  |  | MUEN | -- | TRMD | EN
SSI Module Enable
0: Module is disabled.
1: Module is enabled.
SSI setup
SSIU start
SSIU stop
Finish
Start
SSI stop
SSI start
SSIU setup

## Slide 24: SSIU/SSI – process
Stop SSI00 transfer by resetting bit start_0 in SSIq Control Register (q = 0-0)
SSIq_CONTROL.start_0 = 0
 |  |  | Bit |  | 31 | ... | 28 | ... | 24 | ... | 20 | ... | 16 | ... | 12 | ... | 8 | ... | 4 | ... | 0
SSIq_CONTROL |  |  |  |  | -- | -- | start_7 | -- | start_6 | -- | start_5 | -- | start_4 | -- | start_3 | -- | start_2 | -- | start_1 | -- | start_0
SSIi-0_start_flag
0: Stop data transfer through SSIi-0
1: Start data transfer through SSIi-0
(i = 0 to 4, 9)
Example: Using SSI0 as the output device for Renderer plugin.
Parameters: channel = 2, PCM width = 16bits, sampling frequency = 32000Hz
SSI setup
SSIU start
SSIU stop
Finish
Start
SSI stop
SSI start
SSIU setup